## Slide 1: JCTVC-J0147: Subjective test results on ALF
J. Takiue
T.K. Tan
A. Fujibayashi
Y. Suzuki
NTT DOCOMO, Inc.
10th Meeting: Stockholm, SE, 11–20 July 2012

## Slide 2: Summary
What was done
  Subjective evaluation of ALF by non-expert viewers based on subjective test method used in JCTVC-I0585 (Report on subjective viewing of ALF)
  Comparison of two coding methods for 40 cases defined in JCTVC-I0585
    HM 7.0 Main
    HM 7.0 Main with ALF
Results of 22 non-expert viewers
  ALF improves the visual quality at five test points out of forty test points.
  ALF also causes the subjective loss at six test points.
Conclusion
  Results indicate that there is no clear benefit from ALF in the subjective sense of non-experts.

## Slide 3: Test conditions
Compare visual quality of two coding methods
  HM7.0 main ALF on  A
  HM7.0 main (ALF off)  B
5-grade scale (same as JCTVC-I0585)
  -2: A is worse, -1: A is slightly worse, 0: Equal,1: A is slightly better, 2: A is better
  Viewing order of 1) and 2) is randomized
40 test cases (same as JCTVC-I0585)
  Sequences and coding structures
    Class A (4), Class B (5) and RiverBed for Random Access
    Class B (5), Class E (3), RiverBed and SpinCalendar for Low Delay B
  Qp; 32, 37
Display
  EIZO FlexScan SX3031 (30 inch LCD, resolution: 2560x1600) and
  NEC LCD5220 (52 inch, 1920x1080)
  Viewing condition: Viewing distance was set to 2H

## Slide 4: 22 Non-expert Viewers
LB,Qp37:1:KristenAndSara,2:Johnny,3:FourPeople,4:SpinCalendar,5:RiverBed,
6:Kimono,7:ParkScene,8:Cactus,9:BasketballDrive,10:BQTerrace
RA,Qp37:11:Traffic,12:PeopleOnStreet,13:NebutaFestival,14:SteamLocomotive,15:RiverBed,
16:Kimono,17:ParkScene,18:Cactus,19:BasketballDrive,20:BQTerrace
LB,Qp32:Repeat of LB,Qp37(21-30), RA:Qp32:Repeat of RA,Qp32(31-40)
Positive value means ALF improve visual quality. Mean MOS across 40 cases is 0.03
Five test points showed better subjective picture quality of ALF than the HM7.0 anchor.
Six test point showed worse subjective picture quality of ALF than the HM7.0 anchor

## Slide 5: Comments
Visual quality of sequences encoded at QP=37 is not good for entertainment service. Except for Riverbed, the difference between 2 coding method could not be found at QP=32.
At QP=32, 4 cases were found the difference out of 20 test points
  One test points showed better subjective picture quality of ALF than the HM7.0 anchor.
    Riverbed
  Three test point showed worse subjective picture quality of ALF than the HM7.0 anchor
    SpinCalendar, BQTerrace
Blocking artefacts may be suppressed by modifying the deblocking filter. e.g. JCTVC-J0096

## Slide 6: FYI: JCTVC-I0585: 18 Expert viewers
LB, Qp=37
RA, Qp=37
LB, Qp=32
RA, Qp=32
LB,Qp37:1:KristenAndSara,2:Johnny,3:FourPeople,4:SpinCalendar,5:RiverBed,
6:Kimono,7:ParkScene,8:Cactus,9:BasketballDrive,10:BQTerrace
RA,Qp37:11:Traffic,12:PeopleOnStreet,13:NebutaFestival,14:SteamLocomotive,15:RiverBed,
16:Kimono,17:ParkScene,18:Cactus,19:BasketballDrive,20:BQTerrace
LB,Qp32:Repeat of LB,Qp37(21-30), RA:Qp32:Repeat of RA,Qp32(31-40)
Positive value means ALF improve visual quality
Six test points showed better subjective picture quality of Option2_RA_ALF than the HM6.0 anchor.
One test point showed worse subjective picture quality of Option2_RA_ALF than the HM6.0 anchor