## Slide 1: AhG5/AhG6: Bypass coding for SAO syntax elements
<number>
JCTVC-J0148
Toru Matsunobu
Kengo Terada
Hisao Sasai
Takahiro Nishi
Panasonic Corporation
Notes: <number>

## Slide 2
<number>
Summary
In this proposal, we modify syntax structure for SAO in order to simplify the implementation and improve the throughput.
Solution 1
  sao_lcu_enable_flag is added for decoupling SAO on/off from sao_type_idx, and sao_lcu_enable_flag is moved to the top of SAO syntax elements.
  Unary coding for sao_type_idx is replaced with truncated unary coding.
  SAO syntax elements after sao_merge_up_flag are signaled using bypass models.
  The number of context models for sao_merge_left_flag is reduce from 3 to 1.
Solution 2
  Context coding for sao_merge_left_flag and sao_merge_up_flag in solution 1 changes into bypass coding.
Our proposal can reduce the number of context models and bins for SAO with no significant loss (0.03%).

## Slide 3
<number>
Introduction
Motivation
For improvement of the throughput and simplification of the implementation,
Reduction of the number of context models and bins.
Grouping bypass bins together.
Problem
sao_merge_left_flag is signaled using 3 context models for every color components.
Many context bins are generated in the worst case of sao_type_idx and sao_offset_abs.
SAO syntax element | Coding model | The number of context models | Context bins per sample in the worst case
sao_merge_left_flag | Context | 3 | 0.01
sao_merge_up_flag | Context | 1 | 0.01
sao_type_idx | Context | 2 | 0.07
sao_offset_sign | Bypass | 0 | 0
sao_offset_abs | Context | 2 | 0.15
sao_band_position | Bypass | 0 | 0

## Slide 4
Solutions
Solution 1.
Modification of syntax structure in order to reduce the number of context models and bins for SAO syntax elements and group bypass bins together.
Modification | Same proposal
sao_lcu_enable_flag is added for decoupling sao on/off state from sao_type_idx, and sao_lcu_enable_flag is moved to the top of SAO syntax elements. | J0103 (J0437) by Qualcomm / MediaTek
Unary coding for sao_type_idx is replaced with truncated unary coding. | J0054 by Samsung, J0104 (J0437) by Qualcomm / MediaTek, J0178 by Sony,
sao_type_idx is signaled using bypass models instead of context models. | J0437 by Qualcomm / MediaTek
sao_offset_abs is signaled using bypass models instead of context models. | J0041 by Samsung
The number of context models for sao_merge_left_flag is reduced from 3 to 1 by sharing one context for every color component. | J0178 by Canon, J0355 by Motorola
sao_band_position and sao_offset_sign are signaled continuously. | J0046 by Samsung, J0054 by Qualcomm, J0268 by Sony
<number>

## Slide 5
Solutions
Solution 1.
Modifications of sao_type_idx
Syntax element |  | Bin string |  |  |  |  | 
sao_type _idx | BinIdxCtx | 0 | 1 | 1 | 1 | 1 | 1
 | off | 0 |  |  |  |  | 
 | EO(0) | 1 | 0 |  |  |  | 
 | EO(1) | 1 | 1 | 0 |  |  | 
 | EO(2) | 1 | 1 | 1 | 0 |  | 
 | EO(3) | 1 | 1 | 1 | 1 | 0 | 
 | BO | 1 | 1 | 1 | 1 | 1 | 0
Syntax element |  | Bin string |  |  | 
sao_lcu_ enable_flag | binIdxCtx | 0 |  |  | 
 | off | 0 |  |  | 
 | on | 1 |  |  | 
sao_type _idx | binIdxCtx | na | na | na | na
 | EO(0) | 0 |  |  | 
 | EO(1) | 1 | 0 |  | 
 | EO(2) | 1 | 1 | 0 | 
 | EO(3) | 1 | 1 | 1 | 0
 | BO | 1 | 1 | 1 | 1
Current sao_type_idx
Proposal
<number>

## Slide 6
Solutions
Solution 2.
Solution 1 changes into the following.
<number>
Contents | Same proposal
sao_merge_left_flag and sao_merge_up_flag are signaled using bypass models instead of context models. | -

## Slide 7
<number>
Solutions
<number>
Modifications of syntax structure for SAO in our proposal
CD | Solution 1 | Solution 2
- | Context | Context
Context |  | Bypass
 | Bypass | 
Bypass |  | 
Context |  | 
Bypass |  | 

## Slide 8
<number>
Results
Summary of results
Anchor: HM7.0
Not significant loss (0.03%)
Similar in run time
test | The number of context models | Context bins per sample in the worst case | BD-rate for Y | BD-rate for U | BD-rate for V
Solution 1 | 8 → 3 | 1.50 → 0.01 | 0.03% | 0.10% | 0.15%
Solution 2 | 8 → 1 | 1.50 → 0.01 | 0.03% | 0.23% | 0.27%

## Slide 9
<number>
Conclusion
Our proposal can reduce the number of context models and bins for SAO and group bypass bins together with no significant loss.
Many thanks to NEC for cross-check (JCTVC-J0350)
Solution 1 is recommended for adoption to DIS text.

## Slide 10
<number>
<number>

## Slide 11
<number>
<number>
reference data

## Slide 12
<number>
Preliminary tests for sao_type_idx and sao_offset_abs
test | AI-Main | RA-Main | LDB-Main | LDP-Main | AI-HE10 | RA-HE10 | LDB-HE10 | LDP-HE10
Test 1 | 0.00% | -0.02% | 0.02% | 0.01% | 0.00% | 0.01% | 0.01% | 0.01%
Test 2 | 0.01% | 0.99% | 1.02% | 0.83% | 0.00% | 0.62% | 0.86% | 0.77%
Test 3 | 0.03% | 0.03% | 0.03% | 0.14% | 0.01% | 0.04% | 0.05% | 0.05%
Test 1.
  Bypass coding for the bins except binIdx0 for sao_type_idx.
Test 2.
  Bypass coding for all bins for sao_type_idx.
Test 3.
  Bypass coding for all bins for sao_offset_abs.
BD-rate of preliminary tests
→ Not significant loss if bins except binIdx0 for sao_type_idx and all bins for sao_offset_abs are signaled using bypass coding.

## Slide 13
<number>
Solutions
<number>
SAO syntax element | Current SAO | Solution 1 | Solution 2
NEW! sao_lcu_enable_flag | - | Context | Context
sao_merge_left_flag | Context | Context | Bypass
sao_merge_up_flag | Context | Context | Bypass
sao_type_idx | Context | Bypass | Bypass
sao_offset_sign | Bypass | Bypass | Bypass
sao_offset_abs | Context | Bypass | Bypass
sao_band_position | Bypass | Bypass | Bypass
Modifications of coding for SAO syntax elements

## Slide 14
<number>
<number>
test | Context bins for SAO |  |  |  |  | 
 | sao lcu enable flag | sao merge left flag | sao merge up flag | sao type idx | sao offset abs | Total
HM7.0 | - | 100% | 100% | 100% | 100% | 100%
Solution 1 | DIV/0 | 20.67% | 15.75% | 0.00% | 0.00% | 38.07%
Solution 2 | DIV/0 | 0.00% | 0.00% | 0.00% | 0.00% | 29.93%
test | Context bins for SAO |  |  |  |  | 
 | sao lcu enable flag | sao merge left flag | sao merge up flag | sao type idx | sao offset abs | Total
HM7.0 | - | 0.84% | 0.25% | 0.19% | 0.31% | 2.72%
Solution 1 | 0.87% | 0.08% | 0.05% | 0.00% | 0.00% | 1.00%
Solution 2 | 0.86% | 0.00% | 0.00% | 0.00% | 0.00% | 0.86%
The ratio of context bins relative to HM7.0
The ratio of context bins for SAO in total context bins
Results

## Slide 15
<number>
<number>
The ratio of isolated bypass bins relative to HM7.0
Results
 | AI-Main | RA-Main | LB-Main | LP-Main | AI-HE10 | RA-HE10 | LB-HE10 | LP-HE10
HM7.0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Solution 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Solution 2 | 21 | 69 | 525624 | 2004 | 35 | 99 | 90 | 138
cb | cb | cb | bb | cb | cb | bb | cb | cb | bb | bb | cb
Isolated bypass bin
Isolated bypass bin
cb: context bin
bb: bypass bin
Example of bins order