## Slide 1: JCTVC-J0156 Generalized definition of the TLA for scalable extension
LG Electronics

## Slide 2: Introduction
The purpose of the TLA picture is to indicate where switching to higher temporal layer can be done after one or more temporal layers have been extracted / removed.
Such concept seems to be applicable for other scalability direction as well.

## Slide 3: Proposed modifications
1. Change the name of Temporal Layer Access
  more general term, for example SLA (Switching Layer Access).
2. Modify current semantic of TLA
  ‘temporal_id’  ‘layer level’
  ’TLA’  ‘SLA’
  When the value of nal_unit_type is equal to 3 for all VCL NAL units of a particular picture, that particular picture is referred to as a SLA picture. A SLA picture and all coded pictures with layer level greater than or equal to the layer level of the SLA picture that follow the SLA picture in decoding order shall not use inter prediction from any picture with layer level greater than or equal to the layer level of the SLA picture that precedes the SLA picture in decoding order

## Slide 4: Temporal layer switching
Group A pictures precede the SLA picture in decoding order and their layer levels are greater than or equal to the layer level of the LA picture.
Group B pictures follow the SLA picture in decoding order and their layer levels are greater than or equal to that of the SLA picture.
Group C pictures have the layer level smaller than SLA picture’s layer level.

## Slide 5: Spatial layer switching

## Slide 6: Conclusion
We propose a generalized (extended) definition of the TLA picture to support spatial and quality scalabilities in addition to the temporal scalability.
With this proposition, one does not need to add new NAL types when other kinds of scalability are included in scalable extension.
Single-layer HEVC has only temporal layers so this modification does not require any changes in the current TLA features