## Slide 1: Removal of the inference of CBFY at the transform depth level zero in inter CU
J. Kim
JCTVC-J0161

## Slide 2: Introduction
Coded Block Flag
  Indication of existence of non zero coefficients in a TU
  Basically coded every TU
  Conditionally derived at the first transform depth level

## Slide 3: Introduction
Conditions of derivation for luma blocks : luma CBF is inferred as 1 when
  Current CU is not intra CU
  Current transform depth level is 0
  CBFU and CBFV are zero
no_residual_data_flag =false
CBFU/CBFV
Transform_split_flag = false
CBFY coding
Tr_depth=0 &&
CBFU=0 &&
CBFV=0
CBFY, CBFU, CBFV
residual coefficient coding
transform_split_flag coding
N
Y
Y
Y
CBFY inference
N

## Slide 4: Proposed Method
We suggest not to infer CBFY in any case for simple and clear implementation
no_residual_data_flag =false
CBFU/CBFV
Transform_split_flag = false
CBFY coding
Tr_depth=0 &&
CBFU=0 &&
CBFV=0
CBFY, CBFU, CBFV
residual coefficient coding
transform_split_flag coding
N
Y
Y
Y
CBFY inference
N
no_residual_data_flag =false
CBFU/CBFV
Transform_split_flag = false
CBFY coding
CBFY, CBFU, CBFV
residual coefficient coding
transform_split_flag coding
N
Y
Y

## Slide 5: Proposed Method
transform_tree( x0L, y0L, x0C, y0C, xBase, yBase, log2CbSize, log2TrafoWidth, log2TrafoHeight, trafoDepth, blkIdx ) { | Descriptor
… | 
if( split_transform_flag[ x0L ][ y0L ][ trafoDepth ] ) { | 
… | 
transform_tree( x0L, y0L, x0C, y0C, x0L, y0L, log2CbSize, log2TrafoWidth − 1, log2TrafoHeight − 1, trafoDepth + 1, 0 ) | 
transform_tree( x1L, y1L, x1C, y1C, x0L, y0L, log2CbSize, log2TrafoWidth − 1, log2TrafoHeight − 1, trafoDepth + 1, 1 ) | 
transform_tree( x2L, y2L, x2C, y2C, x0L, y0L, log2CbSize, log2TrafoWidth − 1, log2TrafoHeight − 1, trafoDepth + 1, 2 ) | 
transform_tree( x3L, y3L, x3C, y3C, x0L, y0L, log2CbSize, log2TrafoWidth − 1, log2TrafoHeight − 1, trafoDepth + 1, 3 ) | 
} else { | 
if( PredMode = = MODE_INTRA ¦ ¦ trafoDepth != 0 ¦ ¦ cbf_cb[ x0 ][ y0 ][ trafoDepth ] ¦ ¦ cbf_cr[ x0 ][ y0 ][ trafoDepth ] ) | 
cbf_luma[ x0L ][ y0L ][ trafoDepth ] | ae(v)
transform_unit (x0L, y0L, x0C, y0C, log2TrafoWidth, log2TrafoHeight, trafoDepth, blkIdx) | 
} | 
} | 
cbf_luma[ x0L ][ y0L ][ trafoDepth ] equal to 1 specifies that the luma transform block contains one or more transform coefficient levels not equal to 0. The array indices x0L, y0L specify the location ( x0L, y0L ) of the top-left luma sample of the considered transform block relative to the top-left luma sample of the picture. The array index trafoDepth specifies the current subdivision level of a coding unit into blocks for the purpose of transform coding. trafoDepth is equal to 0 for blocks that correspond to coding units.
When cbf_luma[ x0 ][ y0 ][ trafoDepth ] is not present, it is inferred to be equal to 1.

## Slide 6: Experimental Results
< BD rate when the proposed method applied to luma blocks>
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.1% | 0.0% | 0.1% | 0.0% | 0.1%
Class B | 0.1% | 0.2% | 0.2% | 0.0% | 0.1% | 0.1%
Class C | 0.0% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
Class D | 0.0% | 0.1% | 0.0% | 0.1% | 0.1% | 0.1%
Class E |  |  |  |  |  | 
Overall | 0.0% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
 | 0.0% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
Class F | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% | 0.1%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.1% | 0.4% | 0.4% | 0.1% | 0.4% | 0.3%
Class C | 0.1% | 0.3% | 0.3% | 0.1% | 0.1% | 0.3%
Class D | 0.0% | 0.3% | 0.6% | 0.1% | 0.8% | 0.4%
Class E | 0.2% | 0.4% | -0.2% | 0.1% | 0.2% | 0.6%
Overall | 0.1% | 0.3% | 0.3% | 0.1% | 0.4% | 0.4%
 | 0.1% | 0.4% | 0.3% | 0.1% | 0.4% | 0.4%
Class F | 0.0% | 0.5% | 0.6% | 0.1% | 0.4% | 0.7%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 7: Conclusion
We proposed to code CBFs for luma every cases without inference for simple and clear implementation