## Slide 1: LCU-based framework with zero pixel line buffers for non-local means filter
JCTVC-I0165
M. Matsumura, S. Takamura and A. Shimizu
NTT Media Intelligence Laboratories
NTT Corporation, Japan

## Slide 2: Proposal
Proposed in-loop filter
In-loop filter for HEVC version 2.
Deblocking Filter
NLM filter
ALF
SAO
Additional
HE10 only
Zero-delay non-local means filtering for decoder.
  Restricts pixel reference to un-reconstructed LCUs
  Restricts pixel reference across slice/tile boundaries.
Target
LCU
Target
LCU
Target
LCU
LCU boundary
Slice boundary
Tile boundary
Referable
Non-referable

## Slide 3: Objective evaluations
Picture-based RD-optimization (with high-delay encoding)
  Permits filter on/off adaptation of slice-based control for NLM.
 | GOP | Y | U | V | Enc Time[%] | Dec Time[%]
Main | All Intra | -0.4% | -0.5% | -0.8% | 110.3% | 111.3%
 | Random Access | -0.4% | 0.0% | -0.3% | 102.3% | 109.0%
 | Low delay B | -0.7% | -0.6% | -0.8% | 101.6% | 109.7%
 | Low delay P | -1.8% | -1.4% | -1.5% | 102.4% | 112.8%
HE10 | All Intra | -0.4% | -0.2% | -0.5% | 108.9% | 117.8%
 | Random Access | -0.7% | -0.9% | -1.0% | 102.7% | 111.1%
 | Low delay B | -0.8% | -1.5% | -1.6% | 101.7% | 111.6%
 | Low delay P | -1.4% | -2.1% | -2.2% | 102.6% | 114.3%
 | GOP | Y | U | V | Enc Time[%] | Dec Time[%]
Main | All Intra | -0.3% | -0.9% | -1.3% | 109.8% | 112.2%
 | Random Access | -0.2% | -0.6% | -1.0% | 102.2% | 110.6%
 | Low delay B | -0.3% | -0.9% | -1.6% | 101.5% | 111.5%
 | Low delay P | -1.5% | -1.7% | -2.1% | 102.3% | 114.6%
HE10 | All Intra | -0.3% | -0.5% | -0.8% | 108.6% | 118.8%
 | Random Access | -0.5% | -1.3% | -1.5% | 102.5% | 112.9%
 | Low delay B | -0.4% | -2.2% | -2.3% | 101.9% | 113.7%
 | Low delay P | -1.0% | -2.9% | -3.2% | 102.6% | 116.4%
LCU-based RD-optimization (with zero-delay encoding)
  Slice-based control for NLM filter is set always equal to on.

## Slide 4: Subjective evaluations
BasketballDrive (class B), LD-P (Main Profile), QP=37, POC #335, Anchor: 17880 [bits], PSNR-Y 32.92 [dB], PSNR-U 40.25 [dB], PSNR-V 39.68 [dB], Proposed: 17328 [bits], PSNR-Y 33.58 [dB], PSNR-U 40.30 [dB], PSNR-V 39.82 [dB].

## Slide 5: Subjective evaluations
BasketballDrill (class C), LD-P (Main Profile), QP=37, POC #270, Anchor: 5952 [bits], PSNR-Y 31.28 [dB], PSNR-U 36.13 [dB], PSNR-V 36.06 [dB], Proposed: 6624 [bits], PSNR-Y 31.53 [dB], PSNR-U 36.27 [dB], PSNR-V 36.28 [dB].

## Slide 6: Subjective evaluations
KristenAndSara (class E), LD-P (Main Profile), QP=37, POC #141, Anchor: 17880 [bits], PSNR-Y 32.92 [dB], PSNR-U 40.25 [dB], PSNR-V 39.68 [dB], Proposed: 17328 [bits], PSNR-Y 33.58 [dB], PSNR-U 40.30 [dB], PSNR-V 39.82 [dB].

## Slide 7: Subjective evaluations
SlideEditing (class F), LD-B (Main Profile), QP=37, POC #001, Anchor: 368 [bits], PSNR-Y 32.43 [dB], PSNR-U 37.81 [dB], PSNR-V 37.22 [dB], Proposed: 320 [bits], PSNR-Y 33.04 [dB], PSNR-U 37.88 [dB], PSNR-V 37.30 [dB].

## Slide 8: Conclusion
Zero-delay NLM filter for encoder/decoder are proposed.
  The improvements of coding efficiency are:
    Picture-based: luma 0.4-1.8%, chroma 0.0-2.2%
    LCU-based: luma 0.2-1.5%, chroma 0.6-3.2%.
NLM filtering provides visible benefits in still picture.
  Need to evaluate subjective quality in moving picture.
NLM filtering is a promising candidate to be explored.