## Slide 1: JCTVC-J0199: Comments on DPB size
Thomas Davies
Arild Fuldseth (Cisco Systems)

## Slide 2: Summary
In the HEVC draft DPB size is specified in units of pictures, unlike AVC, allowing:
  6 pictures for all levels, including current picture
  1 more reference than AVC at the highest resolution
  Fewer references than AVC at lower resolutions
This limit prevents the effective use of long-term references for error resilience
  Widely used in video conferencing today
  Up to 16 reference frames in shipping products
We propose modifying the draft to allow up to 16 pictures in the DPB

## Slide 3: Flexible DPB size in AVC
In AVC systems with a capability exchange, it is possible to indicate (IETF RFC 3984):
  Support for decoding e.g. level 4 resolutions
  Support for a larger DPB size than level 4 supports
Then an encoder may use a higher level value to capture the DPB size but otherwise stick to level 4
The purpose is to use many more references for error recovery – for example 16
The recovery frames are used very frequently – frame losses are common

## Slide 4: LTRs and error recovery in AVC
In flight – sent but no ACK/NACK yet
ACKed/NACKed
Current
good recovery
frame
Earlier
Later
Red frames are recovery
reference frames

## Slide 5: LTRs and error recovery in AVC
ACKed/NACKed
Current
good recovery
frame
Earlier
Later
Next candidate
recovery frame
Red frames are recovery
reference frames
In flight – sent but no ACK/NACK yet

## Slide 6: Distribution of recovery frames
AGE = (1 + 1/(N-1)) * Effective RTT
6 pictures = current + 3*STR + 2*LTR

## Slide 7: Distribution of recovery frames
Recovery frames must be distributed over the effective RTT i.e. incorporating all delays:
  Feedback can also be lost
  Feedback can be required from multiple participants
  ERTT is a variable and the worst-case can be very significant
  Want to cover small and worst-case RTTs at the same time
A small number of recovery frames increases the age of the one used by a large amount

## Slide 8: Conclusions
Analysis of DPB size so far has not included LTRs
We believe that HEVC should offer at least the same reference capabilities as AVC in practice
Use of multiple LTRs in AVC has proved extremely valuable in video conferencing
We have shipping products making use of 16 reference pictures
We are agnostic about the method by which an increased DPB size is achieved (AVC method or other)

## Slide 9: Some options
MaxDpbSize = 16 for all levels
AVC method: DPB memory equivalent to N largest pictures including current, N=5, 6
“Layered” solution: DPB memory may be split into N full-size, 2*N half-size, 4*N quarter size, N=5, 6
  Extends J0111, J0210, J0283, J0367, J0496 to 4*N
As 3, but add 3*N/2, 4*N/3 (J0496)
As 2, 3, or 4, but with N=5 for level > 4 (as per J0163)