## Slide 1: JCTVC-J0212: Modified scan method for intra transform skipping
<number>

## Slide 2
In this proposal, we introduce a modified scan method for intra transform skipping
Proposed scan method for intra transform skipping
  if transform_skip_flag is equal to 1 and the scanIdx is equal to 2 (vertical scan), the scanIdx is modified to 1 (horizontal scan)
  Otherwise, if the transform_skip_flag is equal to 1 and the scanIdx is equal to 1 (horizontal scan), the scanIdx is modified to 2 (vertical scan)
For class F sequence,
  0.9% gain for AI, 0.7% gain for RA, 0.3% gain for LDB
Same proposal
  JCTVC-J0202 Method2
  JCTVC-J0313 Method1
<number>
Summary

## Slide 3
<number>
Introduction
Intra transform skipping was adopted in the last meeting
On the other hand, a scan method for coefficient coding is adaptively determined based on the intra prediction mode even for the block using intra transform skipping ex) If the intra prediction is equal to horizontal mode,  Vertical scan is applied because zero coefficients tend to be successive in a vertical direction after transforming
However, if the transform were skipped, the vertical scan would not be effective since zero coefficients tend to be successive in horizontal direction

## Slide 4
<number>
7.3.10 Residual coding syntax
Proposal
scanIdx | 
0 | Diagonal scan
1 | Horizontal scan
2 | Vertical scan
This proposal would introduce the conversion of the scan method
  if transform_skip_flag is equal to 1 and scanIdx is equal to 2 (vertical scan),  scanIdx is modified to 1 (horizontal scan)
    otherwise, if the transform_skip_flag is equal to 1 and scanIdx is equal to 1 (horizontal scan),  scanIdx is modified to 2 (vertical scan)
Modified draft text
  － Change only the assignment of scanIdx for intra transform skipping

## Slide 5
<number>
Experimental result
Proposed method was implemented on HM7.0 software
It shows 0.9% gain for AI, 0.7% gain for RA, 0.4% gain for LDB in class F sequence
The transform skipping would be especially effective to class F sequences  Proposed method could strengthen its effectiveness
anchor:HM7.0+transform skipping

## Slide 6
<number>
We propose to modify the scan method for intra transform skipping
Proposed method saves 0.9% bits for AI in class F sequences without obvious difference in encoding and decoding time
We suggest the proposed method be adopted in the DIS of HEVC
Conclusion