## Slide 1: JCTVC-J0213: AHG6: A threshold for SAO edge offset
<number>

## Slide 2
In this proposal, we introduce a threshold for SAO edge offset
It would be helpful for encoder to control the categorization for a strong edge and a weak edge inside LCU
It would improve the flexibility of SAO in terms of a subjective quality and an objective quality
  By applying edge offset only for a strong edge inside LCU  Prevent a blurring degradation due to the loss of an original weak edge, such as a camera noise or a film grain
0.1% gain for RA, 0.2% gain for LDB in Main setting while improving the flexibility of SAO
<number>
Summary

## Slide 3
<number>
Introduction
EO (Edge Offset) has four categories with different features
In this categorization, a strong edge and a weak edge could be included in the same category since there is no threshold to distinguish them  It would be difficult for encoder to tune SAO ex) Difficult to apply EO for only strong edge inside LCU to keep an original weak edge (camera noise, film grain)
To improve it, an adjustable parameter for EO would be needed
pixel index
pixel index
x-1
x
x+1
pixel level
category 4
category 3
x-1
x
x+1
pixel level
x-1
x
x+1
pixel level
category 2
x-1
x
x+1
pixel level
x-1
x
x+1
pixel level
x-1
x
x+1
pixel level
category 1
pixel index
pixel index
pixel index
pixel index
LCU
strong edge
weak edge
ringing
noise
category4
original pixel
reconstructed pixel
LCU
lose original
weak edge
remain
ringing
noise
category4
original pixel
reconstructed pixel applied EO
Original weak edge, such as a camera noise or a film grain, would be lost
 it might cause a blurring degradation

## Slide 4
<number>
category = 2 + Sign(Px-Px-1) + Sign(Px+1-Px)
Sign(x)=
1 (x>0)
-1 (x<0)
0 (otherwise)
Sign(x)=
1 (x>0 & x<threshold)
-1 (x<0 & x>-threshold)
0 (otherwise)
x-1
x
x+1
pixel level
pixel index
x-1
x
x+1
pixel level
category 4
pixel index
x-1
x
x+1
pixel level
threshold
category 3
pixel index
x-1
x
x+1
pixel level
threshold
category 4
pixel index
HM7.0
proposal
Px-1
Px
Px+1
Proposal
We introduce a threshold for EO to distinguish a strong edge and a weak edge
By changing the threshold, the assignment of a strong edge and a weak edge could be controlled
Same categorization as HM7.0 is possible by setting a maximum pixel value to the threshold
It would be helpful for encoder in tuning SAO ex) Possible to apply EO for only strong edge inside LCU to keep an original weak edge (for content including camera noise, film grain)
A threshold is added to the condition
 possible to distinguish them
LCU
strong edge
weak edge
ringing
noise
category4
original pixel
reconstructed pixel
LCU
keep original
weak edge
eliminate
ringing
noise
category3
original pixel
reconstructed pixel applied EO in proposal
category4
Set offset value 0 to category4 in encoder
 Eliminate a ringing noise with keeping an original weak edge
weak edge
strong edge
HM7.0
proposal

## Slide 5
<number>
Syntax and semantics changes
Three syntax parameters are added in the slice header to calculate thresholds for Y, Cb and Cr
7.3.3 Slice header syntax
7.4.3 Slice header semantics

## Slide 6
<number>
Experimental result
Proposed method was implemented on HM7.0 software
In this test, threshold was set according to the slice type and depth value of coding structure
anchor:HM7.0

## Slide 7
<number>
Subjective test result
Compared method
  SAO off
  HM7.0
  Proposal with setting offset value 0 to a weak edge (category 1 and 4)
Test image: including a camera noise or a film grain
  PeopleOnStreet
  Panslow
  Spincalendar

## Slide 8
<number>
PeopleOnStreet ( 2560x1600, 30p, frame no. 1 )

## Slide 9
<number>
original
SAO off
PeopleOnStreet ( 2560x1600, 30p, frame no. 1, B-slice, QP22)

## Slide 10
<number>
original
HM7.0
PeopleOnStreet ( 2560x1600, 30p, frame no. 1, B-slice, QP22 )
blurring

## Slide 11
<number>
original
proposal with setting
offset value 0 to weak edge
PeopleOnStreet ( 2560x1600, 30p, frame no. 1, B-slice, QP22 )

## Slide 12
<number>
Panslow ( 1280x720, 60p, frame no. 513 )
Reference: “Description of new High Definition Video Test Sequences”, ISO/IEC JTC1/SC29/WG11, MPEG02/N5125, Shanghai, Oct, 2002.

## Slide 13
<number>
original
SAO off
Panslow ( 1280x720, 60p, frame no. 513, B-slice, QP22 )

## Slide 14
<number>
original
HM7.0
Panslow ( 1280x720, 60p, frame no. 513, B-slice, QP22 )
blurring

## Slide 15
<number>
original
Panslow ( 1280x720, 60p, frame no. 513, B-slice, QP22 )
proposal with setting
offset value 0 to weak edge

## Slide 16
<number>
Spincalendar ( 1280x720, 60p, frame no. 8 )
Reference: “Description of new High Definition Video Test Sequences”, ISO/IEC JTC1/SC29/WG11, MPEG02/N5125, Shanghai, Oct, 2002.

## Slide 17
<number>
original
SAO off
Spincalendar ( 1280x720, 60p, frame no. 8, B-slice, QP22 )

## Slide 18
<number>
original
HM7.0
Spincalendar ( 1280x720, 60p, frame no. 8, B-slice, QP22 )
blurring

## Slide 19
<number>
original
Spincalendar ( 1280x720, 60p, frame no. 8, B-slice, QP22 )
proposal with setting
offset value 0 to weak edge

## Slide 20
<number>
We propose to introduce a threshold for SAO EO
It could improve the flexibility of EO in terms of a subjective quality and an objective quality
  Ex) By applying EO only for a strong edge inside LCU in encoder tuning  Prevent a blurring degradation due to the loss of an original weak edge, such as a camera noise or a film grain
We suggest the proposed method be adopted in the DIS of HEVC
Conclusion