## Slide 1: JCTVC-J0216 AHG 9: Signalling slice index to detect lost slice earlier
Hendry
The 10th JCT-VC Meeting
LG Electronics

## Slide 2: Summary
When a picture is coded into multiple slices
  Only first slice is easily recognized  first_slice_in_pic_flag
  The 2nd ~ the last slice are not easily recognized
Problem:
  When lost occurs, it can be detected only after all received slices are already decoded
Adv of detecting lost slice earlier:
  Decoder can decide whether or not to decode other received slices. If the chosen error concealment is frame copy, other slices are not necessarily to be decoded to save resource
  Decoder can try to conceal the lost slice earlier.
Proposal: Modification to enable detecting lost slice earlier
  Instead of first_slice_in_pic_flag (u(1)), signal slice_idx_in_pic (ue(v))
  Signal indication of last slice in pic  last_slice_in_pic_flag (u(1))

## Slide 3: Detecting lost slices earlier

## Slide 4: Detecting lost slices earlier
Signalling slice index only may not be enough
  When the lost slice is the last one, having index does not help to detect this lost
Need to signal indication of last slice as well

## Slide 5: Proposed modification

## Slide 6: Effect to coding performance
Tested with Slice mode 2 (1500 bytes per slice)
Effect to coding performance is small. Only 0.1% when there are many slices in a picture (e.g., Class A and B test sequences)

## Slide 7: Conclusion
Currently we can detect lost slice only after all received slices of a picture have been decoded
This contribution proposes modification to enable lost slice detection earlier, that is when parsing slice header.
Adv of detecting lost slice earlier:
  Decoder can decide whether or not to decode other received slices to save coding resource
  Decoder can try to conceal the lost slice earlier.
The proposed modification has very small impact to coding performance
  0.1% lost when there are many slices exists
Considering the enabled feature, request the proposed modification to be adopted.