## Slide 1: JCTVC-I0224
Oguz Bici, Miska M. Hannuksela, Kemal Ugur
Nokia
AHG10: Hook for scalable extensions: Signalling TMVP reference index in slice header

## Slide 2: Summary
In HM7, Reference index of TMVP candidate in the motion merge mode is always set as 0

## Slide 3: Summary
In HEVC extensions, reference picture list contains a combination of base and inter-layer/view reference pictures.
This means, picture at reference index=0 may be an inter-layer or inter-view reference picture:
  For scalable coding, an inter-layer reference picture.
  For multiview coding, an inter-view reference picture.
  For depth-enhanced multiview coding, a view synthesis reference picture.
For enhancement layers/views, TMVP cannot be utilized since POC based scaling is impossible
  Illustrated in next slide

## Slide 4: Summary

## Slide 5: Proposal
Signal reference index of the TMVP candidate in the slice header
Allows utilizing TMVP merge candidate for the extensions of HEVC, the same way it is used in the base layer.
Reference index can be always set as 0 in the base HEVC.
  0.0% coding efficiency change for RA and LB main cases.

## Slide 6: Changes in the syntax
Picture parameter set RBSP semantics
  merge_tmvp_ref_idx_present_flag equal to 0 indicates that merge_tmvp_ref_idxl0 and merge_tmvp_ref_idxl1 are not present. merge_tmvp_ref_idx_present_flag equal to 1 indicates that merge_tmvp_ref_idxl0 and merge_tmvp_ref_idxl1 are present.
Slice header semantics
  merge_tmvp_ref_idx_l0 specifies the reference index in list 0 for the temporal merging candidate in merge mode. merge_tmvp_ref_idx_l0 shall always refer to a valid list entry, and the resulting picture shall be the same for all slices of a coded picture. When merge_tmvp_ref_idx_l0 is not present, it is inferred to be equal to 0.
  merge_tmvp_ref_idx_l1.
        Derivation process for luma motion vectors for merge mode
          … The reference index for temporal merging candidate refIdxLX is set equal to 0 merge_tmvp_ref_idx_lX …