## Slide 1
Improvement of HEVC Lossless Coding using Transform Coefficient Coding
DMC R&D Center
JCTVC-J0230
Min-Su Cheon, Yumi Sohn, Sunil Lee, Il-Koo Kim, and Jeonghoon Park

## Slide 2
Contents
Inspire the World, Create the Future
Ⅰ
Ⅱ
Ⅲ
Ⅳ
Introduction
Algorithm Description
Simulation Results
Conclusion
DMC R&D Center

## Slide 3
Introduction
DMC R&D Center
Lossless coding has many applications, e.g. medical image compression.
However, the performance of the current HEVC lossless coding (HM7.1) is not satisfactory and need to be improved.
The goal of this contribution is to propose an improved HEVC lossless coding method based on HEVC lossy coding framework.
Motivation
In the current design of HEVC, lossless coding is implemented by bypassing transform, quantization, and all the in-loop filtering (de-blocking, SAO, and ALF).
The spatial residual, which is the difference between original and predicted CU, is directly signaled to the decoder.
Current Design

## Slide 4
Algorithm Description
DMC R&D Center
On top of HEVC lossy coding, the remaining residual is additionally signaled to the decoder to achieve lossless coding.
Only in-loop filtering is bypassed.
: Original CU
: Intra/Inter-Predicted CU
: Spatial residual
: Transform coefficients
: Quantized transform coefficients
: Reconstructed residual
: Remaining residual
)

## Slide 5
Simulation Results (1/2)
DMC R&D Center
The proposed method is implemented on top of HM7.1.
The simulation is performed using only All Intra Main and HE10 configurations.
The performance of the proposed method combined with the sample-based angular prediction (SAP) proposed by JCTVC-I0117 is also provided.
Simulation Set-up
The proposed method outperforms HM7.1 lossless coding by 8.8% and 8.3% in All Intra Main and HE10 configurations (w/o Class F), respectively.
The SAP provides 1.9 ~ 2.8% additional gain on average when combined with the proposed method.
The complexity at the encoder side can be reduced by limiting the number of intra prediction modes to 3 (DC, Vertical, and Horizontal), and the performance degradation due to this limit is 1.3 ~ 2.4% on average.
Summary of the Results

## Slide 6
Simulation Results (2/2)
DMC R&D Center
 | Proposed |  | Proposed + SAP |  | Proposed + SAP + 3 Intra pred. modes | 
 | AI Main | AI HE10 | AI Main | AI HE10 | AI Main | AI HE10
Class A | -12.4% | -11.6% | -14.5% | -13.8% | -13.3% | -12.1%
Class B | -7.4% | -6.8% | -8.1% | -8.3% | -6.7% | -7.7%
Class C | -8.0% | -7.7% | -9.5% | -10.0% | -5.7% | -7.8%
Class D | -9.1% | -9.8% | -11.5% | -13.0% | -8.8% | -11.3%
Class E | -6.7% | -5.3% | -10.8% | -12.0% | -9.5% | -11.7%
Overall (w/o F) | -8.8% | -8.3% | -10.8% | -11.2% | -8.7% | -9.9%
Overall (w/ F) | -8.3% | -7.9% | -10.9% | -11.7% | -8.5% | -10.1%
Class F | -5.8% | -5.5% | -11.4% | -13.2% | -7.5% | -11.0%
Enc Time | 193% | 158% | 195% | 156% | 117% | 90%
Dec Time | 107% | 101% | 104% | 94% | 105% | 92%

## Slide 7
Conclusion
DMC R&D Center
In this contribution, an improved HEVC lossless coding based on HEVC lossy coding framework is proposed.
The proposed method provides 8.8% and 8.3% coding gain in All Intra Main and HE10 configurations, respectively.
We recommend adopting the proposed method in the HM.

## Slide 8
THANK YOU
Inspire the World, Create the Future