## Slide 1
HEVC Lossless Coding for Medical Image Compression
DMC R&D Center
JCTVC-J0232
Sunil Lee, Min-Su Cheon, Yumi Sohn, Il-Koo Kim, Ken McCann and Jeonghoon Park

## Slide 2
Contents
Inspire the World, Create the Future
DMC R&D Center
Ⅰ
Ⅱ
Ⅲ
Ⅳ
Introduction
Simulation Set-up
Simulation Results
Conclusion

## Slide 3
Introduction – Motivation
DMC R&D Center
The amount of medical image data is increasing geometrically.
  The number of scans itself has significantly increased recently.
  Large amount of data is obtained from one single scan. (e.g. CT scan with 400 slices of 1024x1024 resolution  800MB)
Medical images need to be efficiently compressed.
Chart: 
| 2006년 | 2010년
CT | 2410 | 5250
 | 2410 | 5250
Chart: 
| 2006년 | 2010년
 | 440 | 730
MRI | 440 | 730
Number of scans (x1000)
241M
525M
44M
73M
Number of CT scans per year in Korea (120%↑)
Number of MRI scans per year in Korea (66%↑)
Number of scans (x1000)
2006
2010
2006
2010

## Slide 4
Introduction – Current Status
DMC R&D Center
Medical images have to be losslessly compressed during the treatment period, since any distortion introduced by lossy compression can affect the clinical decision and lead to the legal problems.
Currently, many ISO standards (e.g. JPEG, JPEG-LS, JPEG-2000 for still image coding, MPEG-2 and H.264/AVC for video coding) are employed by DICOM1) standard for medical image compression.
Medical image compression is one of the promising applications of HEVC.
Lossless Compression
JPEG Lossless
J2K Lossless
Lossy Compression


JPEG
JPEG-2000
JPEG-XR
JPEG-LS
Long-term Archive
Short-term Storage
Acquisition stage
Follow-up stage
Treatment stage
Medical imaging devices
CT
MRI
Medical image workflow
1) DICOM: Digital Imaging and Communications in Medicine

## Slide 5
Simulation Set-up
DMC R&D Center
The performance of HEVC lossless coding and its improvement proposed by JCTVC-J0230 is compared with that of JPEG lossless, JPEG-2000 lossless, and JPEG-LS for medical image compression.
Total 9 MR scans collected from the public database TCIA1) are used as test sequences.
Only All Intra configuration is tested, since random access to each individual slice is mandatory for medical image compression.
1) TCIA: The Cancer Imaging Archive (http://cancerimagingarchive.net/)
Sequence name | Resolution | Number of Slices | Max Bit-depth
Medical_Brain_1 | 512x512 | 22 | 10
Medical_Brain_2 | 512x512 | 60 | 9
Medical_Brain_3 | 512x512 | 60 | 10
Medical_Brain_4 | 512x512 | 60 | 9
Medical_Breast_1 | 864x864 | 84 | 9
Medical_Breast_2 | 560x560 | 84 | 9
Medical_Breast_3 | 640x640 | 90 | 9
Medical_Breast_4 | 528x528 | 41 | 10
Medical_Breast_5 | 672x672 | 60 | 10

## Slide 6
Simulation Results
DMC R&D Center
Sequence name | JPEG lossless | JPEG-2000 lossless | JPEG-LS | Proposed (J0230) | Proposed + SAP (J0230) | Proposed + SAP + 3 modes (J0230)
Medical_Brain_1 | 24.8 | -15.6 | -10.9 | -17.4 | -20.7 | -19.2
Medical_Brain_2 | 25.7 | -14.7 | -10.8 | -13.2 | -15.8 | -14.0
Medical_Brain_3 | 26.6 | -14.5 | -10.3 | -11.9 | -15.2 | -13.5
Medical_Brain_4 | 26.4 | -14.2 | -10.0 | -12.0 | -14.8 | -12.5
Medical_Breast_1 | 42.4 | -19.8 | -15.2 | -22.9 | -26.7 | -26.1
Medical_Breast_2 | 35.3 | -17.2 | -13.0 | -17.7 | -20.4 | -18.9
Medical_Breast_3 | 41.9 | -12.5 | -9.0 | -13.6 | -15.8 | -14.6
Medical_Breast_4 | 23.3 | -13.0 | -10.3 | -13.3 | -14.3 | -13.7
Medical_Breast_5 | 30.3 | -10.5 | -7.7 | -10.3 | -11.4 | -10.8
Average | 30.8 | -14.7 | -10.8 | -14.7 | -17.2 | -16.0
Anchor: HEVC lossless (HM7.1)
The performance of HEVC lossless coding is better than JPEG lossless, however, outperformed by JPEG-2000 lossless (14.7%) and JPEG-LS (10.8%).
The performance of HEVC lossless coding can be significantly improved by applying the method proposed in J0230, and J0230’s method outperforms the existing lossless image codec.

## Slide 7
Conclusion
DMC R&D Center
The medical image compression is one of the promising application areas of HEVC, since HEVC is the state-of-the-art codec which can provide the best coding efficiency.
However, the performance of the current HEVC lossless coding is not satisfactory and even outperformed by the existing lossless image codec including JPEG-LS and JPEG-2000 lossless.
To meet the requirements of the industry, the coding efficiency of HEVC lossless coding has to be significantly improved.
The method proposed in JCTVC-J0230 can be one of the candidate methods for the performance improvement.
Besides the coding efficiency, high bit-depth input (maximum bit-depth needs to be at least 16 bits for each color component), gray-scale input, etc. need to be supported for HEVC’s adoption for medical image compression.
It is recommended that JCT-VC consider the improvement of HEVC lossless coding performance in a future profile.

## Slide 8
THANK YOU
Inspire the World, Create the Future