## Slide 1
Syntax and semantics of Dual-coder Mixed Chroma-sampling-rate (DMC) coding for 4:4:4 screen content
JCTVC-J0233
11 July – 20 July 2012
Tao Lin

## Slide 2
Screen picture has two types of content
  Continuous-tone content + Discontinuous-tone content
Hybrid coding is not discontinuous-tone oriented
  Even 444 has bad quality (due to high QP) at low bit-rate
Non-hybrid coder can do a much better job
  Using a super-large predictor set (dictionary)
  Hash table based quick string search can code the picture at much lower bitrate
Motivation


## Slide 3
DMC Coding
For reference, prediction or dictionary
S
Original Input Macroblock O
Full-chroma Prediction
Full-chroma Dictionary-entropy Coder
Constructed Pixel Buffer 1 (Full-chroma)
R-D Performance Based Selector
DMC Bitstream
Chroma Upsampler
O
P1
b1
b2
P2
O
Full-chroma Input
Transform, Quantiza-tion, CABAC, etc.
S2
Chroma Subsampler
= Full-chroma
= Chroma-subsampled
The existing HEVC YUV420 syntax and semantics are used AS IS
Coder 1
Coder 2

## Slide 4
Dual-coder Mixed Chroma-sampling-rate (DMC)
  An extension of HEVC 420 hybrid coding (used AS IS)
  Add 444 Dictionary coding (three new syntax elements)
Overall CODEC Landscape
420
444
Hybrid Coder
Dictionary Coder
Most Applications
Broadcast, Production
High end equipments
Screen Contents
DMC
Too high bit-rate,High cost
No Need

## Slide 5
DMC Bitstream Syntax
coding_unit( x0, y0, log2CbSize ) { | Descriptor
if(profile_idc!=DMC) | 
{the current YUV420 HEVC hybrid coder syntax is used AS IS} | 
else { | 
dmc_coder_type_flag | ae(v)
if(dmc_coder_type_flag = = 0) //HYBRID_CODER | 
{the current YUV420 HEVC hybrid coder syntax is used AS IS} | 
else //DICTIONARY_ENTROPY_CODER | 
dictionary_entropy_coder( x0, y0, log2CbSize ) | 
} | 
} | 

## Slide 6
DMC Bitstream Syntax
dictionary_entropy_coder( x0, y0, log2CbSize ) { | Descriptor
decoded_sample_count = 0 | 
NumSamplesInCU = (3 << (log2CbSize << 1)) | 
while(decoded_sample_count < NumSamplesInCU) { | 
matching_string_flag | ae(v)
if(matching_string_flag = = 1) { | 
matching_string_distance | ae(v)
matching_string_length_minus2 | ae(v)
decoded_sample_count += length | 
} | 
else { | 
unmatchable_sample_residual_abs | ae(v)
unmatchable_sample_residual_sign | ae(v)
decoded_sample_count += 1 | 
} | 
} | 
} | 

## Slide 7
DMC Bitstream Semantics
dmc_coder_type_flag specifies which coder is used to code the CU. If dmc_coder_type_flag = 0, hybrid coder is used to code the CU, otherwise, dictionary-entropy coder is used to code the CU.
matching_string_flag specifies whether the succeeding dictionary coding element is a matching string or an unmatchable (luma or chroma) sample residual.
If matching_string_flag = 1, the succeeding dictionary coding element is a matching string, otherwise, the succeeding dictionary coding element is an unmatchable (luma or chroma) sample residual.
matching_string_distance specifies the distances between the first sample of current sample-string to be decoded/constructed and the first sample of matching sample-string previously decoded/constructed in the dictionary, which is actually DPB and the current decoded picture reordered in a “dictionary-scan” format defined as a column-wise-packed-pixel CU-by-CU format.
matching_string_length_minus2 + 2 specifies the length of the matching sample-string. The value of matching_string_length_minus2 shall be in the range of 0 to 271, inclusive.
unmatchable_sample_residual_abs is the absolute difference between the unmatchable sample (y or u or v component of a pixel) to be decoded and its predictor that is the same component (y or u or v) of the previous pixel in the dictionary. The value of unmatchable_sample_residual_abs shall be in the range of 0 to (256<< bit_depth_luma_minus8) – 1 for luma component or (256<< bit_depth_chroma_minus8) – 1 for chroma component, inclusive.
unmatchable_sample_residual_sign specifies the sign of an unmatchable sample residual. If unmatchable_sample_residual_sign is equal to 0, the corresponding unmatchable sample residual has a positive value. Otherwise (unmatchable_sample_residual_sign is equal to 1), the corresponding unmatchable sample residual has a negative value.

## Slide 8
Conclusions
DMC coding is a straightforward yet very effective extension of the state of the art HEVC for SCC
Just adding three new syntax elements
Significant BD-rate and subjective improvement
Plan to integrate DMC to HM7.x and HM8.x and let more people to join further investigation, cross-check and other activities

## Slide 9
THANK YOU