## Slide 1: Inter transform skipping
Xiulian Peng, Cuiling Lan, Jizheng Xu, Gary J. Sullivan
Microsoft Corp.
Xidian University

## Slide 2: InterTS
IntraTS was adopted in May
  7.5% gain for class F
InterTS
  Unification and text simplification to intraTS

## Slide 3: Proposed text modification
residual_coding( x0, y0, log2TrafoWidth, log2TrafoHeight, scanIdx, cIdx ) { | Descriptor
if( log2TrafoWidth = = 1 ¦ ¦ log2TrafoHeight = = 1 ) { | 
log2TrafoWidth = 2 | 
log2TrafoHeight = 2 | 
} | 
If( transform_skip_enabled_flag && !cu_ transquant_bypass _flag && (PredMode = = MODE_INTRA) && ( log2TrafoWidth = = 2) && (log2TrafoHeight = = 2) ) | 
transform_skip_flag[ x0 ][ y0 ][ cIdx ] | ae(v)
…… | ……

## Slide 4: Compared with HM7 anchor
Both intraTS and interTS are on
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Overall | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | 0.0%
Class F | -7.5% | -7.4% | -8.0% | 0.0% | 0.0% | 0.0%
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Overall | -0.1% | -0.3% | -0.4% | -0.1% | -0.1% | -0.1%
Class F | -7.2% | -7.7% | -8.3% | -1.8% | -1.1% | -1.2%
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Overall | -0.1% | 0.5% | 0.3% | -0.2% | 0.2% | 0.2%
Class F | -6.5% | -6.0% | -6.3% | -3.0% | -2.1% | -1.4%

## Slide 5: Compared with IntraTS
Anchor – HM7 with intraTS always on
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Overall | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
Class F | -1.9% | -1.4% | -1.6% | -1.8% | -1.1% | -1.2%
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Overall | -0.2% | 0.3% | 0.2% | -0.2% | 0.2% | 0.2%
Class F | -3.3% | -2.3% | -3.0% | -3.0% | -2.1% | -1.4%

## Slide 6: On quantization matrix for TS
Flat quantization should be applied to TS
Suggest to disable QM on TS
Direct implementation of de-quantization for TS TUs
  Avoid frequently switching QM at 4x4 level
Cost
  Additional de-quantization implementation for 4x4 TUs.

## Slide 7: Proposed text modification

## Slide 8: Summary
InterTS
  Text simplification
  Intra/inter unification
  Provide lossless coding capability (JCTVC-J0238)
  1.8% and 3.0% gain for class F
Quantization handling for TS
Thanks to TI for cross-check