## Slide 1: Consistent coding of motion information for B slices with identical reference picture lists
Bin Li, Jizheng Xu, Houqiang Li
University of Science and Technology of China
Microsoft Corp.

## Slide 2: Problem statement
In B-frame with l0=l1 coding
  The decision to use l0 or l1 is implicitly made
    Encoder’s decision
    Adopted at the 9th meeting
  The decision of mvd=0 for l1 is explicitly made
    Normative behavior
Propose to unify the design
if( mvd_l1_zero_flag && inter_pred_idc[ x0 ][ y0 ] = = Pred_BI ) {
mvd_l1[ x0 ][ y0 ][ 0 ] = 0
mvd_l1[ x0 ][ y0 ][ 1 ] = 0
} else

## Slide 3: Explicitly signal the decision
Add use_l0_only_flag
 | RA-Main | RA-HE10 | LD-Main | LD-HE10
Class A | 0.0% | 0.0% |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0%
Class E |  |  | 0.1% | 0.1%
Overall | 0.0% | 0.0% | 0.0% | 0.0%
Enc. Time | 100% | 100% | 100% | 100%
Dec. Time | 100% | 100% | 100% | 100%

## Slide 4: Decision by encoder
Remove mvd_l1_zero_flag
  Always code l1 mvd when l1 is used
Use different contexts for abs_mvd_greater0_flag of l0 and l1
 | RA-Main | RA-HE10 | LD-Main | LD-HE10
Class A | 0.0% | 0.0% |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0%
Class E |  |  | -0.1% | 0.1%
Overall | 0.0% | 0.0% | 0.0% | 0.0%
Enc. Time | 100% | 100% | 100% | 100%
Dec. Time | 100% | 100% | 100% | 100%

## Slide 5: Conclusions
Solution 1
  Always signal the decision
Solution 2
  Leave both decision to encoder
Suggest adoption of one solution
  Solution 2 may be preferable
Thanks to MediaTek for cross-check