## Slide 1
On Temporal Layer Access Pictures
Byeongdoo Choi, Youngo Park, Ilkoo Kim, Jaehyun Kim, Jeonghoon Park
Samsung Electronics Co., Ltd
July, 2012
Notes: <number>

## Slide 2: Introduction
BLA picture
  CRA picture with ‘broken link’
  TFD pictures associated with the BLA cannot be correctly decoded
  -> will be discarded
Temporal layer switching
  TLA picture : temporal layer access (from lower layer to higher layer)
  Leading pictures associated with the TLA pictures are present, those pictures cannot be correctly decoded when the temporal layer switching is performed.
  Needs on new picture type for temporal layer access with broken link or temporal layer switching
<number>

## Slide 3: Leading pictures associated with TLA picture
The leading pictures, which are associated with the previous TLA picture in decoding order and precedes the TLA picture in output order, can be present.
<number>
I
P
B
P
B
TLA
temporal_id > 0
temporal_id = 0
P
B
P
B
B
P
Leading picture of TLA

## Slide 4: Proposal
TLA picture with ‘broken link’ : BLT picture
  The leading pictures associated with the TLA picture are marked as the TFD pictures
  When a temporal layer switching is performed, the TLA picture is changed to the BLT picture
  In decoders, the TFD pictures associated with the BLT pictures will be discarded.
<number>

## Slide 5: BLT picture and the associated TFD pictures
The leading pictures, which are associated with the previous TLA picture in decoding order and precedes the TLA picture in output order, can be present.
<number>
I
P
B
temporal_id > 0
temporal_id = 0
P
B
P
B
B
P
temporal layer switching
TFD
BLT

## Slide 6: Syntax
<number>
A BLT picture having nal_unit_type equal to 9 may have associated TFD pictures present in the bitstream. A BLT picture having nal_unit_type equal to 10 does not have associated TFD pictures present in the bitstream.
NAL unit type codes and NAL unit type classes

## Slide 7: Conclusion
<number>
New picture type for temporal layer access with ‘broken link’
  When the temporal layer switching is performed, the upper layer may have a broken link.
  Similarly to the CRA picture, the leading pictures associated with the TLA picture are marked as the TFD pictures for easy discarding in systems.
  The TLA picture when the temporal layer switching occurs is marked as the BLT picture.
  In decoders, the TFD pictures can be discarded before decoding.

## Slide 8
Thank you !
<number>