## Slide 1
On Frame Packing Arrangement SEI
Byeongdoo Choi, Chanyul Kim, Jaehyun Kim, Jeonghoon Park
Samsung Electronics Co., Ltd
July, 2012
Notes: <number>

## Slide 2: Introduction
Needs on full resolution frame compatible 3D delivery
  Compatible with ‘legacy 3D service’ :
    Base only : Half resolution 3D (frame compatible, e.g. Side-by-Side format)
    Base + enhancement layer : Full resolution 3D
  Requirement from DVB-3DTV
    DVB-3DTV phase 2b : ‘Legacy 3D service (frame-compatible) compatibility’
    Phase 1 receiver : frame-compatible 3D video using the same broadcast Phase 2b receiver : enhanced quality 3D video.
  MPEG frame compatible (MFC)
    Preparing the CfP for full resolution 3D compatible with the legacy 3D system.
    High-efficiency 3D solution with a lot of new coding tools will be investigated, however the standardization will be finished 2 years later.
  We propose a Frame Packing Arrangement SEI for full resolution 3D as a prompt/simple solution in respond to DVB-3DTV Phase 2b.
<number>

## Slide 3: Frame compatible full resolution 3D delivery in the scalable manner
This figure illustrates conceptually how to arrange the base and enhancement layers for scalable frame packing 3D data to support the full resolution.
<number>

## Slide 4: Proposal
New SEI message for frame compatible full resolution 3D
  Utilization of temporal layer id:
    Half resolution 3D data is transmitted in the base temporal layer (temporal_id = 0)
    If the base layer is only received and decoded, the half resolution 3D data is reconstructed.
    The complementary half resolution 3D data is transmitted in the second temporal layer (temporal_id = 1).
    If all two layers are received and decoded, the full resolution 3D data can be reconstructed.
<number>

## Slide 5: Scalable arrangement using temporal layer ID in case of Side-by-Side frame packing method
<number>

## Slide 6: Syntax
<number>

## Slide 7: Semantics
use_temporal_layer_for_fullresolution_flag equal to 1 indicates the temporal layers are used for the frame packing for full resolution 3D. In the base temporal layer (temporal_id = 0), the half resolution 3D is frame-packed. In the second temporal layer (temporal_id = 1), the complementary data of the base layer is frame-packed in the same way. The second temporal layer can be extracted or not for full or half resolution 3D.
temporal_id_one_is_complementary_data_flag equal to 1, when frame_packing_arrangement is not equal to 5, indicates that the decoded frame in the second temporal layer (temporal_id = 1) is the complementary data of the previous frame in the base temporal layer (temporal_id = 0). The complementary data is used for the full resolution 3D reconstruction. temporal_id_one_is_complementary_data_flag equal to 0 indicates the decoded frame in the second temporal layer (temporal_id = 1) is associated with the upper-left sample of the original video when frame_packing_arrangement is not equal to 5, and the decoded frame in the base temporal layer (temporal_id = 0) is the complementary data. When frame_packing_arrangement is equal to 5, temporal_id_one_is_complementary_data_flag shall be equal to 0.
temporal_id_one_is_frame1_flag equal to 1, when frame_packing_arrangement is equal to 5, indicates that the decoded frame in the second temporal layer (temporal_id = 1) is constituent frame 1 and the previous decoded frame in the base temporal layer (temporal_id = 0) is constituent frame 0, and the display time of the constituent frame 0 should be delayed to coincide with the display time of constituent frame 1. temporal_id_one_is_frame1_flag equal to 1, when frame_packing_arrangement is equal to 5, indicates that the current decoded frame in the second temporal layer is constituent frame 1 and the previous decoded frame in the base temporal layer (temporal_id = 0) is constituent frame 0, and the display time of the constituent frame 1 should not be delayed for purposes of stereo-view pairing. When frame_packing_arrangement_type is not equal to 5, it is a requirement of bitstream conformance that temporal_id_one_is_frame1_flag shall be equal to 0.
temporal_id_one_is_self_contained_flag equal to 1 indicates that no inter prediction operations within the decoding process for the samples of the second temporal layer (temporal_id = 1) refer to samples of the base temporal layer (temporal_id = 0). frame1_self_contained_flag equal to 0 indicates that some inter prediction operations within the decoding process for the samples of the second temporal layer (temporal_id = 1) may or may not refer to samples of the base temporal layer (temporal_id = 0).
current_frame_is_complementary_data_flag equal to 1, when frame_packing_arrangement is not equal to 5, indicates that the current decoded frame is the complementary data of the same POC frame in another bitstream which is also frame-packed 3D video stream. The complementary data is used for the full resolution 3D reconstruction. current_frame_is_complementary_data_flag equal to 0 indicates the current frame-packed data is associated with the upper-left sample of the original video when frame_packing_arrangement is not equal to 5. When frame_packing_arrangement is not equal to 5, current_frame_is_complementary_data_flag shall be equal to 0.
<number>

## Slide 8: Conclusion
<number>
New Frame Packing Arrangement SEI message
  Support the full resolution 3D
  Support the compatibility with the frame compatible 3D (side-by-side)
  For simplicity, the temporal_id is used for the resolution scalability
  Respond to the requirement of DVB 3DTV phase 2b with only change of the SEI message.

## Slide 9
Thank you !
<number>