## Slide 1: Removal of the 8×2 / 2×8 coefficient groups JCTVC-J0256
Joel Sole, Rajan Joshi, Marta Karczewicz

## Slide 2: Introduction
Coefficient group (CG) is a set of 16 consecutive coefficients in scan order
  Coefficient data is processed in 4×4 sub-blocks (5 scan passes per CG)
  Exception: 8×8 TU with horizontal and vertical scans require 8×2 / 2×8 CG
8×2 / 2×8 CG introduce irregularity in the design
  Different processing unit shape than the regular 4×4 coefficient coding groups
  Additional logic for CG multi-level coding
  Different context derivation of coefficient group flag

## Slide 3: Introduction
Additional conditions in the syntax table are required for the 8×2 / 2×8 CG
for( i = numLastSubset; i >= 0; i− − ) {
offset = i << 4
if( scanIdx = = 1 && log2TrafoWidth = = 3 && log2TrafoHeight = = 3 ) {
xCG = 0
yCG = i
} else if( scanIdx = = 2 && log2TrafoWidth = = 3 && log2TrafoHeight = = 3 ) {
xCG = i
yCG = 0
} else {
xCG = ScanOrder[ log2TrafoWidth ][ log2TrafoHeight ][ scanIdx ][ i << 4 ][ 0 ] >> 2
yCG = ScanOrder[ log2TrafoWidth ][ log2TrafoHeight ][ scanIdx ][ i << 4 ][ 1 ] >> 2
}
implicitNonZeroCoeff = 0
if( (i < numLastSubset) && (i > 0) ) {
significant_coeff_group_flag[ xCG ][ yCG ]
implicitNonZeroCoeff = 1
}

## Slide 4: Introduction
Ticket #609 related to 8×2 / 2×8 CG
  The significant_coeff_group_flag semantics cover only diagonal scan, and do not cover horizontal (8×2 CG) and vertical (2×8 CG) scans
  Possible corrections:
    For 8x2 CG, ( LastSignificantCoeffX, LastSignificantCoeffY ) should be ( 0, yCG <<1 )
    For 2x8 CG ( LastSignificantCoeffX, LastSignificantCoeffY ) should be ( xCG<<1, 0 )
    For 8x2 CG ( xCG, yCG ) is equal to ( 0, LastSignificantCoeffY >> 1 )
    For 2x8 CG ( xCG, yCG ) is equal to ( LastSignificantCoeffX >> 1, 0 )
Ticket #617 also related to 8×2 / 2×8 CG
  The significant_coeff_flag semantics cover only 4x4 coefficient groups, and do not cover 8×2 CG and 2×8 cases. It is assumed 4x4 coefficient groups in the following statement:
    ( xC, yC ) is equal to ( xCG << 2, yCG << 2 )

## Slide 5: Proposal: removal of 8×2 / 2×8 CG
Removal of 8×2 / 2×8 CG by using 4×4-based horizontal / vertical scans
  This change has a BD-rate loss of 0.3% for AI-Main
8×8 TU significance map coding is unified with large TU
Two large TU methods tested:
  Method 1 use different significance map patterns (same ones as in JCTVC-J0068)
  Method 2 use significance map patterns in JCTVC-J0354

## Slide 6: Proposal: unification of 8x8 and large TU
Large TU and 8×8 use the same context derivation for significance map
  All the scans use the same context derivation
  8×8 TU does not share contexts with other TU sizes
    Diagonal scan and horizontal / vertical scan do not share contexts
    Horizontal / vertical scans share contexts
  Number of contexts is reduced by 3 with method 1
  Number of contexts is increased by 5 with method 2
  Initial probabilities are not trained
Context derivation for coefficient group flag is the same for all TU sizes and all scans
8×8 significance map table is removed

## Slide 7: BD-rates
Cross-checked by Canon (JCTVC-J0421)
Common conditions
Results for following additional tests are included:
  8×8 scans are turned off
  Apply the 4x4 horizontal / vertical sub-block scans only
  Test 2 + applying current large TU method to 8×8
 | AI-Main | RA-Main | LB-Main | AI-HE | RA-HE | LB-HE
1: 8×8 scans off | 0.50% | 0.17% | 0.07% | 0.52% | 0.16% | 0.10%
2: 8×8 TU with 4×4 sub-block scans | 0.29% | 0.07% | 0.04% | 0.30% | 0.07% | 0.04%
3: sub-block scan + large TU & 8x8 unified | 0.24% | 0.06% | 0.05% | 0.26% | 0.05% | 0.00%
Proposal M1 | 0.06% | -0.03% | -0.04% | 0.09% | 0.00% | 0.02%
Proposal M2 | 0.02% | -0.06% | -0.02% | 0.06% | -0.04% | 0.07%

## Slide 8: BD-rates
  RDOQ off
  Low QP (12, 17, 22, 27):
 | AI-Main | RA-Main | LB-Main | AI-HE | RA-HE | LB-HE
M1 | 0.00% | -0.05% | -0.03% | -0.01% | -0.04% | 0.01%
M2 | -0.04% | -0.08% | -0.04% | -0.05% | -0.06% | 0.01%
 | AI-Main | RA-Main | LB-Main | AI-HE | RA-HE | LB-HE
M1 | 0.00% | -0.07% | 0.00% | 0.01% | -0.05% | 0.06%
M2 | -0.05% | -0.09% | 0.00% | -0.04% | -0.06% | 0.05%

## Slide 9: Conclusions
Unification of the 8×8 TU coefficient coding
  Removal of the 8×2 / 2×8 CG and all its associated logic
    Reduction in software and working draft text
    Unification of CG flag context derivation
    8×8 significance map table removed
Simplification comes at no performance loss

## Slide 10
Thank you!

## Slide 11: Significance Map Patterns
HM7.0
Method 1 (as in JCTVC-J0068)
Method 2 (JCTVC-J0354)