## Slide 1: JCTVC-J0261: Signaling of VPS Activation
- 1 -
Mobile Research Activites of ETRI
Truong Cong Thang, UoA
&
Jung Won Kang, ETRI

## Slide 2: Introduction
Extractor just needs info in NAL unit header and VPS only
However, to know which VPS is active, an extractor must parse slice headers, PPS, and SPS as well.
That is, an extractor must understand the syntax elements in parameter sets and slice headers.
We propose a direct signaling of active VPS
Extractor will just parse
  the proposed signaling message (simply indicating the id of active VPS)
  NAL unit header
  VPS

## Slide 3: Current operation
VPS
SPS
PPS
Slice header
SPS
SPS
PPS
PPS
NAL unit header
SEI mess-ages

## Slide 4: Proposal for an additional way of signaling
VPS
SPS
PPS
Slice header
SPS
SPS
PPS
PPS
NAL unit header
SEI mess-ages
vps_id
Several options for this signaling:
using access_unit_delimiter
using a new SEI message
using recovery_point SEI

## Slide 5: Proposed syntax
Option 1: AUD
Option2: a new SEI message
Option 3: Recovery point SEI message
access_unit_delimiter_rbsp( ) { | Descriptor
pic_type | u(3)
vps_id_present_flag | u(1)
if( VPS_id_present_flag ) | 
vps_id | ue(v)
rbsp_trailing_bits( ) | 
} | 
parameter_set_reference( payloadSize ) { | Descriptor
vps_id | ue(v)
} | 
recovery_point( payloadSize ) { | Descriptor
vps_id_present_flag | u(1)
if( vps_id_present_flag ) | 
vps_id | ue(v)
recovery_poc_cnt | ue(v)
exact_match_flag | u(1)
broken_link_flag | u(1)
} | 

## Slide 6: Conclusion
An additional way for direct signaling of active VPS is necessary
  the signaling is present only when there is an update of VPS
We propose to adopt at least one option for this signaling