## Slide 1: JCTVC-J0265 Intra Transform Skipping: Smallest CU and Implicit Chroma
Geert Van der Auwera, Marta Karczewicz

## Slide 2: Summary
This contribution proposes two topics on intra transform skipping:
Part 1 proposes to restrict transform skipping for 4x4 intra TUs further to the SCU level. This eliminates needless signalling of the transform_skip_flags for the larger CU sizes and speeds up the encoder in normal mode by about 8% and in fast mode by about 4% without significant coding efficiency loss.
The experiments in part 2 of this proposal indicate that the coding efficiency of chroma 4x4 intra TU transform skipping is a rather modest 2.5% on average for class F, while doubling the encoding time increase of luma transform skipping. Part 2 of this contribution proposes to define the HEVC transform skipping for 4x4 TUs on the fast encoder mode and eliminate signalling of transform_skip_flags for chroma, while implicitly deriving them from the luma flags as is performed in the fast encoder mode.

## Slide 3: Part 1: Transform Skipping for 4x4 Intra TUs at SCU Level
It is proposed to restrict the signalling of the transform_skip_flag to the SCU size only, which is determined by the SPS syntax parameter log2_min_coding_block_size_minus3.
residual_coding( x0, y0, log2TrafoWidth, log2TrafoHeight, scanIdx, cIdx ) { | Descriptor
if( log2TrafoWidth = = 1 ¦ ¦ log2TrafoHeight = = 1 ) { | 
log2TrafoWidth = 2 | 
log2TrafoHeight = 2 | 
} | 
If( transform_skip_enabled_flag && !cu_ transquant_bypass _flag && PredMode = = MODE_INTRA && log2CbSize = = Log2MinCbSize && ( log2TrafoWidth = = 2) && (log2TrafoHeight = = 2) ) | 
transform_skip_flag[ x0 ][ y0 ][ cIdx ] | ae(v)
…… | 

## Slide 4: Part 1: Transform Skipping for 4x4 Intra TUs Restricted to SCU Level
BD-rate results for reference HM7.0 Main with TS enabled and HM7.0 HE10
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.00% | 0.00% | -0.02% | 0.00% | -0.06% | -0.01%
Class B | 0.00% | 0.00% | 0.01% | 0.00% | 0.02% | -0.02%
Class C | 0.01% | -0.01% | 0.02% | 0.01% | -0.02% | -0.01%
Class D | 0.01% | 0.03% | 0.00% | 0.01% | 0.02% | -0.03%
Class E | -0.01% | 0.02% | -0.02% | 0.00% | -0.02% | 0.01%
Class F | 0.07% | 0.10% | 0.05% | 0.06% | -0.08% | 0.13%
Overall | 0.01% | 0.02% | 0.01% | 0.01% | -0.02% | 0.01%
 | 0.01% | 0.02% | 0.01% | 0.01% | -0.02% | 0.02%
Enc Time[%] | 94% |  |  | 99% |  | 
Dec Time[%] |  |  |  |  |  | 
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.07% | 0.17% | 0.02% | 0.01% | 0.20% | -0.08%
Class B | 0.01% | -0.07% | 0.01% | -0.01% | -0.04% | 0.03%
Class C | 0.02% | 0.14% | 0.01% | 0.01% | 0.11% | -0.06%
Class D | -0.01% | 0.01% | -0.14% | 0.01% | -0.14% | -0.25%
Class E |  |  |  |  |  | 
Class F | 0.07% | 0.19% | 0.17% | 0.04% | 0.16% | -0.08%
Overall | 0.03% | 0.08% | 0.01% | 0.01% | 0.05% | -0.08%
 | 0.03% | 0.06% | 0.03% | 0.01% | 0.02% | -0.06%
Enc Time[%] | 101% |  |  | 102% |  | 
Dec Time[%] |  |  |  |  |  | 

## Slide 5: Part 1: Transform Skipping for 4x4 Intra TUs Restricted to SCU Level
 | Low delay P Main |  |  | Low delay P HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.00% | 0.01% | 0.03% | -0.02% | 0.30% | -0.07%
Class C | 0.00% | -0.10% | -0.41% | -0.01% | -0.08% | 0.19%
Class D | -0.06% | 0.02% | 0.16% | 0.00% | 0.51% | -0.79%
Class E | -0.04% | -0.57% | -1.70% | -0.08% | -0.20% | 0.13%
Class F | 0.04% | 0.05% | 0.54% | 0.09% | 0.31% | -0.30%
Overall | -0.01% | -0.09% | -0.19% | 0.00% | 0.19% | -0.18%
 | -0.01% | -0.10% | -0.24% | 0.00% | 0.18% | 0.00%
Enc Time[%] | 101% |  |  | 100% |  | 
Dec Time[%] |  |  |  |  |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.03% | -0.05% | -0.06% | 0.00% | 0.07% | 0.05%
Class C | 0.02% | 0.05% | -0.14% | -0.03% | -0.11% | 0.11%
Class D | -0.02% | 0.37% | 0.59% | -0.06% | 0.30% | 0.06%
Class E | -0.08% | -0.79% | -1.14% | 0.09% | -0.23% | 0.08%
Class F | 0.16% | 0.64% | 0.60% | 0.10% | -0.03% | 0.73%
Overall | 0.01% | 0.08% | 0.02% | 0.02% | 0.02% | 0.21%
 | 0.01% | 0.10% | -0.05% | 0.01% | 0.16% | 0.33%
Enc Time[%] | 102% |  |  | 100% |  | 
Dec Time[%] |  |  |  |  |  | 

## Slide 6: Part 1: Transform Skipping for 4x4 Intra TUs Restricted to SCU Level
Encoder speedup:
It is proposed to adopt the SCU restriction for intra transform skipping:
  Eliminates needless signalling for larger CU
  Encoder speedup
Encoder Mode | TS = off | TS = on | TS-SCU = on
Normal | 100% | 133% | 125%
Fast | 100% | 115% | 111%

## Slide 7: Part 2: Intra Transform Skipping With Chroma Flags From Luma
It is proposed to disable signalling of the chroma transform_skip_flag and implicitly assign the value that is derived from the corresponding luma transform_skip_flags.
Based on fast encoder transform skip mode
Syntax change:
residual_coding( x0, y0, log2TrafoWidth, log2TrafoHeight, scanIdx, cIdx ) { | Descriptor
… | 
If( transform_skip_enabled_flag && !cu_ transquant_bypass _flag && (PredMode = = MODE_INTRA) && (cIdx == 0) && ( log2TrafoWidth = = 2) && (log2TrafoHeight = = 2) ) | 
transform_skip_flag[ x0 ][ y0 ][ cIdx ] | ae(v)
... | 

## Slide 8: Part 2: Intra Transform Skipping With Chroma Flags From Luma
BD-rate results for reference HM7.0 Main with TS enabled and HM7.0 HE10
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.03% | 0.11% | 0.19% | -0.02% | 0.00% | 0.10%
Class B | -0.03% | 0.12% | 0.25% | -0.03% | 0.11% | 0.19%
Class C | -0.07% | 0.31% | 0.42% | -0.05% | 0.25% | 0.33%
Class D | -0.08% | 0.27% | 0.48% | -0.05% | 0.17% | 0.32%
Class E | -0.05% | 0.09% | 0.41% | -0.04% | 0.04% | 0.43%
Class F | 0.36% | 2.30% | 3.08% | 0.28% | 1.49% | 2.23%
Overall | 0.02% | 0.53% | 0.80% | 0.01% | 0.35% | 0.59%
 | 0.02% | 0.56% | 0.80% | 0.01% | 0.36% | 0.60%
Enc Time[%] | 88% |  |  | 91% |  | 
Dec Time[%] |  |  |  |  |  | 
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.03% | 0.14% | 0.29% | -0.01% | 0.63% | 0.13%
Class B | -0.02% | 0.10% | 0.40% | -0.03% | 0.15% | 0.09%
Class C | -0.04% | 0.64% | 0.49% | 0.00% | 0.50% | 0.51%
Class D | -0.07% | 0.27% | 0.56% | -0.03% | 0.25% | 0.27%
Class E |  |  |  |  |  | 
Class F | 0.32% | 3.28% | 3.65% | 0.25% | 2.74% | 2.97%
Overall | 0.04% | 0.85% | 1.04% | 0.03% | 0.82% | 0.76%
 | 0.04% | 0.85% | 1.09% | 0.03% | 0.79% | 0.76%
Enc Time[%] | 97% |  |  | 99% |  | 
Dec Time[%] |  |  |  |  |  | 

## Slide 9: Part 2: Intra Transform Skipping With Chroma Flags From Luma
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.03% | 0.08% | -0.04% | -0.01% | 0.11% | -0.07%
Class C | -0.04% | 0.12% | -0.25% | -0.05% | -0.16% | 0.13%
Class D | -0.07% | 0.09% | -0.29% | -0.01% | 0.72% | -0.08%
Class E | 0.03% | -0.96% | 0.13% | 0.05% | 0.24% | -0.43%
Class F | 0.43% | 1.37% | 1.46% | 0.48% | 1.27% | 2.92%
Overall | 0.06% | 0.19% | 0.19% | 0.09% | 0.43% | 0.51%
 | 0.06% | 0.20% | 0.17% | 0.09% | 0.42% | 0.55%
Enc Time[%] | 99% |  |  | 98% |  | 
Dec Time[%] |  |  |  |  |  | 
 | Low delay P Main |  |  | Low delay P HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.01% | 0.25% | 0.21% | 0.00% | 0.08% | -0.31%
Class C | -0.05% | 0.05% | -0.38% | 0.03% | -0.11% | 0.18%
Class D | -0.04% | -0.06% | -0.17% | -0.04% | 0.31% | -0.92%
Class E | -0.03% | -0.98% | -0.20% | 0.13% | 0.61% | -0.78%
Class F | 0.42% | 1.65% | 1.49% | 0.36% | 1.18% | 1.74%
Overall | 0.06% | 0.24% | 0.21% | 0.09% | 0.39% | 0.01%
 | 0.06% | 0.23% | 0.17% | 0.09% | 0.37% | 0.08%
Enc Time[%] | 98% |  |  | 98% |  | 
Dec Time[%] |  |  |  |  |  | 

## Slide 10: Part 2: Intra Transform Skipping With Chroma Flags From Luma
Conclusion:
Since the overall coding loss is negligible and the coding loss for class F sequences is acceptable compared with the total gain of intra transform skipping, it is recommended to adopt the proposed intra transform skipping with implicit chroma into HEVC