## Slide 1: AHG6: Modification to loop filtering across slice boundaries
Semih Esenlik
Matthias Narroschke
Thomas Wedi
Panasonic Corporation
10th JCT-VC meeting, Stockholm 10-20 July 2012

## Slide 2: Summary
Background: slice_loop_filter_across_slices_enabled_flag in the slice header controls
  Deblocking Filter only at top/left slice boundaries
  ALF & SAO at all (top/left/bottom/right) slice boundaries
Problem: Gradual Decoder Refresh operation requires that all filters are controlled only at the top/left slice boundaries.
Proposal:
Control all loop filters only at the top/left slice boundaries.

## Slide 3: Gradual Decoder Refresh (GDR)
slice_loop_filter_across_slices_enabled_flag was introduced in the slice header in order to control loop filtering across the top/left boundaries of a slice.
The flag is used in GDR operation for isolating refreshed region from the non-refreshed region.
Meeting Notes from San Jose meeting:
“We should have similar control capability as in AVC – able at slice level to turn off deblocking entirely, or only at boundaries (top/left), or not turned off. When disabled at the SPS level, no filter control should be sent at the slice header level. When deblocking is turned off only at slice boundaries, ALF and SAO should also be turned off at slice boundaries.”

## Slide 4
Loop filter control across slice boundaries in HM7.1
Deblocking: slice_loop_filter_across_slices_enabled_flag controls top/left slice boundaries.
Slice 2:
slice_loop_filter_across_slices_enabled_flag = 0
Slice 1
Slice 3
Deblocking filter off
Slice 2:
slice_loop_filter_across_slices_enabled_flag = 0
Slice 1
Slice 3
ALF/SAO apply padding
ALF/SAO: slice_loop_filter_across_slices_enabled_flag controls at all top/left/bottom/right slice boundaries.
Notes: Jul 31, 2026
<number>

## Slide 5
Gradual Decoder Refresh Example
Example:
  4 slices are used in the frame.
  Slices 1 and 2 are refreshed in the GDR operation
  Slices 3 and 4 are not refreshed.
Loop filters need to be disabled across the boundary between slices 2 and 3.
Slice 1, REFRESHED
Slice 2, REFRESHED
Slice 3, not-refreshed
Slice 4, not-refreshed
Loop filters need to be disabled across slices 2&3

## Slide 6
Gradual Decoder Refresh in HM7.1
Problems:
Loop filters are disabled at unnecessary slice boundaries.
  DF and ALF/SAO are disabled across slices 1 and 2.
  ALF/SAO are disabled across slices 3 and 4.
Complex encoder implementation.
  slice_loop_filter_across_slices_enabled_flag in the slice header controls bottom/right slice boundaries. Need to be modified after encoding of the slice is complete.
  Slice 2 need to be filtered by all loop filters twice.
Slice 1, REFRESHED: cross_slice_flag = 1
Slice 2, REFRESHED:
cross_slice_flag = 0
Slice 3, not-refreshed: cross_slice_flag = 0
Slice 4, not-refreshed: cross_slice_flag = 1
DF off, ALF&SAO use padding
DF off, ALF&SAO use padding
ALF&SAO use padding
DF off

## Slide 7
Gradual Decoder Refresh with Proposal
Proposal:
Align ALF and SAO with deblocking filter at slice boundaries:
  ALF and SAO are controlled at the top/left slice boundaries, same as DB.
  ALF and SAO apply usual boundary padding operations at the top/left boundaries.
No change for Deblocking filter.
Slice 1, REFRESHED: cross_slice_flag = 1
Slice 2, REFRESHED:
cross_slice_flag = 1
Slice 3, not-refreshed: cross_slice_flag = 0
Slice 4, not-refreshed: cross_slice_flag = 1
DF off, ALF&SAO use padding
DF off

## Slide 8: Summary
Background: slice_loop_filter_across_slices_enabled_flag in the slice header controls
  Deblocking Filter only at top/left slice boundaries
  ALF & SAO at all (top/left/bottom/right) slice boundaries
Problem: Gradual Decoder Refresh operation require that all filters are controlled at the top/left slice boundaries.
Proposal:
Control all loop filters at the top/left slice boundaries.