## Slide 1: JCTVC-J0267 Non-CE1: DCT/DST adaptation for Chroma of 4x4 TU
Jun Xu, Cheung Auyeung, Ali Tabatabai
SONY

## Slide 2: Introduction
HM7.0 employs adaptive combinations of DCT and DST for 4x4 TU of MODE_INTRA for Luma
  DCT and DST are available for both row and column transforms
  Based on IntraPredMode, DST and DCT are selected for row and column transforms.
  4 types of 2D transforms for 4x4 TU of MODE_INTRA
  2D DCT for chroma
CE1 is setup to test simplification of DCT-DST adaptation for Luma
  Simplification 1: All 2D DST for all Luma modes
  Simplification 2: DC mode uses 2D DCT and all others use 2D DST.

## Slide 3: Proposal
  Extend the DCT/DST adaptation to Chroma
    Same selection logic as CE1
Solution A
  Based on CE1 Simplification 1
  All 2D DST for all 4x4 TU
Solution B
  Chroma modes
    LM: replace chroma mode with luma mode
    DM: replace chroma mode with luma mode
    Planar, DC, Hor and Ver stay the same
  Selection of DCT/DST adaptation for chroma share the same logic as CE1 simplification 2
    DC mode uses 2D DCT
    all others use 2D DST.

## Slide 4: Results
Thanks to Samsung and Qualcomm for cross-checking
CE1 test conditions, anchor is HM7.0
 | CE1 test 1 |  |  | CE1 test 2 |  |  | CE1 test 3 |  |  | CE1 test 3 vs HM7.0+TS |  | 
 | All Intra Main |  |  | All Intra Main |  |  | All Intra Main |  |  | All Intra Main |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | -0.1% | 0.8% | 0.9% | -0.1% | -0.4% | -0.4% | 0.0% | 0.7% | 0.7% | -0.1% | 0.7% | 0.9%
Class B | 0.0% | 1.2% | 1.3% | -0.1% | -0.3% | -0.3% | 0.0% | 1.2% | 1.1% | -0.1% | 1.2% | 1.3%
Class C | -0.1% | 1.0% | 1.1% | -0.1% | -0.2% | -0.2% | -0.1% | 0.9% | 1.0% | -0.1% | 1.0% | 1.2%
Class D | 0.0% | 1.3% | 1.3% | 0.0% | -0.1% | -0.1% | 0.0% | 1.2% | 1.1% | 0.0% | 1.3% | 1.3%
Class E | -0.2% | 2.0% | 0.9% | -0.1% | -0.5% | -0.6% | -0.1% | 2.0% | 0.6% | -0.2% | 2.0% | 0.9%
Overall | -0.1% | 1.2% | 1.1% | -0.1% | -0.3% | -0.3% | -0.1% | 1.1% | 0.9% | -0.1% | 1.2% | 1.1%
 | -0.1% | 1.2% | 1.1% | 0.0% | 0.0% | 0.2% | -0.1% | 1.1% | 0.9% | -0.1% | 1.1% | 1.1%
Class F | 0.3% | 1.2% | 1.0% | 0.6% | 0.3% | 0.4% | -7.3% | -6.2% | -6.8% | 0.2% | 1.3% | 1.3%
Enc Time[%] | 100% |  |  | 100% |  |  | 129% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 98% |  |  | 101% |  |  |  |  | 
 | CE1 test 1 |  |  | CE1 test 2 |  |  | CE1 test 3 |  |  | CE1 test 3 vs HM7.0+TS |  | 
 | All Intra Main |  |  | All Intra Main |  |  | All Intra Main |  |  | All Intra Main |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | -0.1% | 0.2% | 0.2% | -0.1% | -0.5% | -0.5% | 0.0% | 0.2% | 0.1% | -0.1% | 0.2% | 0.2%
Class B | 0.0% | 0.4% | 0.3% | -0.1% | -0.5% | -0.5% | 0.0% | 0.4% | 0.2% | 0.0% | 0.4% | 0.3%
Class C | -0.2% | -0.2% | -0.3% | -0.1% | -0.4% | -0.5% | -0.2% | -0.3% | -0.4% | -0.2% | -0.2% | -0.2%
Class D | -0.1% | -0.3% | -0.5% | -0.1% | -0.5% | -0.5% | -0.2% | -0.2% | -0.6% | -0.2% | -0.2% | -0.4%
Class E | -0.2% | 1.1% | 0.0% | -0.2% | -1.1% | -1.3% | -0.2% | 1.1% | -0.3% | -0.2% | 1.1% | 0.1%
Overall | -0.1% | 0.2% | 0.0% | -0.1% | -0.5% | -0.6% | -0.1% | 0.2% | -0.2% | -0.1% | 0.2% | 0.0%
 | -0.1% | 0.2% | 0.0% | -0.1% | -0.2% | -0.1% | -0.1% | 0.2% | -0.2% | -0.1% | 0.2% | 0.0%
Class F | 0.1% | 0.2% | -0.2% | 0.3% | -0.2% | -0.3% | -7.5% | -7.1% | -7.8% | 0.0% | 0.4% | 0.2%
Enc Time[%] | 100% |  |  | 100% |  |  | 128% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 99% |  |  | 101% |  |  |  |  | 
Solution A
Solution B

## Slide 5: Solution A
DST
DST
4x4 TU
Coefficients
Row transform
Column transform

## Slide 6: Solution B
Mode
DCT
DST
DCT
DST
4x4 TU
Luma/Chroma
Coefficients
Row transform
Column transform
Luma
Chroma
Chroma mode mapping
Chroma | Mapped mode
LM | Luma mode
DM | Luma mode
Planar | Planar
DC | DC
HOR | HOR
VER | VER

## Slide 7: Conclusion
Proposed to extend DCT/DST adaptation to chroma of 4x4 TU
Unified logic for luma and chroma
Recommend for adoption.