## Slide 1: JCTVC-J0269 AHG6: SAO on/off flags coding
Jun Xu, Ali Tabatabai
SONY

## Slide 2: Introduction
SAO in HM7.0
  Signal at LCU level
    Merge Up or left flags
    If no merges, SAO offset information
    SAO offsets
      SAO type(i.e. on/off, BO, EO classes)
      BO bandposition
      BO/EO offsets
JCTVC-I0193
  Decouple SAO on/off from SAO type
  Combine SAO on/off flags from luma and chroma and signal together

## Slide 3: JCTVC-I0193
SAO on/off flags
  Combination
  Look-up table to get code index
  Unary binarization for code index
  One context for all bins
Combination index = (lcu_sao_enable_flagY<<2) + (lcu_sao_enable_flagCb<<1) + lcu_sao_enable_flagCr

## Slide 4: Proposal(Solution A)
Simplify JCTVC-I0193 on SAO on/off flags coding
  Remove the look-up table and new code index:
  Truncated unary binarization
    JCTVC-I1093 uses unary binarization
  Context modeling
    One context for the first bin
    By-pass for other bins
Code index = (lcu_sao_enable_flagCr<<2) + (lcu_sao_enable_flagCb<<1) + lcu_sao_enable_flagY

## Slide 5: Comparison
Binarization and context modeling
LCU SAO enable flag |  |  | JCTVC-I0193 |  | Proposed solution A | 
Y | U | V | Code index | Binary | Code index | Binary
0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 10 | 1 | 10
0 | 1 | 0 | 6 | 1111110 | 2 | 110
1 | 1 | 0 | 3 | 1110 | 3 | 1110
0 | 0 | 1 | 5 | 111110 | 4 | 11110
1 | 0 | 1 | 2 | 110 | 5 | 111110
0 | 1 | 1 | 7 | 11111110 | 6 | 1111110
1 | 1 | 1 | 4 | 11110 | 7 | 1111111
Context 0
By-pass
Context 0

## Slide 6: Results (Solution A)
Thanks to TI for cross-checking
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | -0.2% | -0.2% | 0.1% | -0.1% | -0.2%
Class B | 0.1% | -0.1% | -0.2% | 0.1% | -0.1% | -0.2%
Class C | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0%
Class D | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0%
Class E | 0.1% | -0.1% | -0.2% | 0.1% | -0.1% | -0.1%
Overall | 0.1% | 0.0% | -0.1% | 0.1% | 0.0% | -0.1%
 | 0.1% | 0.0% | -0.1% | 0.1% | 0.0% | -0.1%
Class F | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0%
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.2% | -0.7% | -0.5% | 0.0% | -0.2% | -0.4%
Class B | -0.1% | -0.4% | -0.5% | -0.1% | -0.3% | -0.3%
Class C | -0.2% | -0.2% | -0.2% | -0.2% | -0.2% | -0.2%
Class D | -0.5% | -0.4% | -0.2% | -0.4% | -0.3% | -0.3%
Class E |  |  |  |  |  | 
Overall | -0.3% | -0.4% | -0.3% | -0.2% | -0.2% | -0.3%
 | -0.3% | -0.4% | -0.3% | -0.2% | -0.2% | -0.3%
Class F | -0.2% | -0.1% | -0.1% | -0.2% | -0.2% | -0.2%
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.1% | -1.0% | -1.1% | -0.1% | -0.6% | -0.6%
Class C | -0.2% | -0.2% | -0.4% | -0.1% | -0.3% | -0.1%
Class D | -0.3% | 0.0% | 0.3% | -0.2% | 0.1% | -0.1%
Class E | -0.6% | -2.2% | -2.5% | -0.7% | -0.8% | -0.7%
Overall | -0.3% | -0.8% | -0.9% | -0.3% | -0.4% | -0.4%
 | -0.3% | -0.7% | -0.8% | -0.3% | -0.4% | -0.3%
Class F | -0.3% | -0.9% | -0.6% | -0.1% | -0.7% | -0.3%

## Slide 7: Proposal (Solution B)
Solution B
  Combine Solution A and JCTVC-J0268
Results
  Anchor is HM7.0
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | -0.4% | -0.5% | 0.1% | -0.3% | -0.4%
Class B | 0.1% | -0.3% | -0.5% | 0.1% | -0.3% | -0.5%
Class C | 0.1% | -0.1% | -0.2% | 0.1% | -0.2% | -0.3%
Class D | 0.1% | -0.3% | -0.4% | 0.0% | -0.1% | -0.2%
Class E | 0.1% | -0.7% | -0.9% | 0.1% | -0.4% | -0.6%
Overall | 0.1% | -0.4% | -0.5% | 0.1% | -0.3% | -0.4%
 | 0.1% | -0.3% | -0.5% | 0.1% | -0.3% | -0.4%
Class F | 0.1% | -0.2% | -0.2% | 0.0% | -0.3% | -0.3%
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.2% | -1.2% | -1.1% | -0.1% | -0.6% | -0.8%
Class B | -0.1% | -0.7% | -0.8% | -0.1% | -0.5% | -0.7%
Class C | -0.3% | -0.4% | -0.5% | -0.2% | -0.3% | -0.5%
Class D | -0.5% | -0.5% | -0.5% | -0.5% | -0.5% | -0.6%
Class E |  |  |  |  |  | 
Overall | -0.3% | -0.7% | -0.7% | -0.2% | -0.5% | -0.7%
 | -0.3% | -0.7% | -0.7% | -0.2% | -0.5% | -0.7%
Class F | -0.2% | -0.3% | -0.5% | -0.3% | -0.5% | -0.8%
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.1% | -1.5% | -1.6% | -0.2% | -0.7% | -1.1%
Class C | -0.2% | -0.5% | -0.7% | -0.2% | -0.7% | -0.4%
Class D | -0.4% | -0.3% | 0.1% | -0.3% | -0.2% | -0.1%
Class E | -0.6% | -3.0% | -3.2% | -0.7% | -1.1% | -0.6%
Overall | -0.3% | -1.3% | -1.3% | -0.3% | -0.7% | -0.6%
 | -0.3% | -1.2% | -1.2% | -0.3% | -0.6% | -0.5%
Class F | -0.3% | -1.5% | -0.6% | -0.2% | -0.6% | 0.2%

## Slide 8: Conclusion
Proposed to improve SAO signalling
  Decouple SAO on/off
  0.2~0.3% BD-gains for Inter cases
Recommend for adaption of Solution B.