## Slide 1
JCTVC-J0270: HEVC VUI Parameters with Extension Hooks
M. Haque, K. Sato, A. Tabatabai, T. Suzuki
July 12, 2012

## Slide 2: Current HEVC VUI Syntax Structure
vui_parameters( ) { | Descriptor
aspect_ratio_info_present_flag | u(1)
if( aspect_ratio_info_present_flag ) { | 
aspect_ratio_idc | u(8)
if( aspect_ratio_idc = = Extended_SAR ) { | 
sar_width | u(16)
sar_height | u(16)
} | 
} | 
overscan_info_present_flag | u(1)
if( overscan_info_present_flag ) | 
overscan_appropriate_flag | u(1)
video_signal_type_present_flag | u(1)
if( video_signal_type_present_flag ) { | 
video_format | u(3)
video_full_range_flag | u(1)
colour_description_present_flag | u(1)
if( colour_description_present_flag ) { | 
colour_primaries | u(8)
transfer_characteristics | u(8)
matrix_coefficients | u(8)
} | 
} | 
chroma_loc_info_present_flag | u(1)
if( chroma_loc_info_present_flag ) { | 
chroma_sample_loc_type_top_field | ue(v)
chroma_sample_loc_type_bottom_field | ue(v)
} | 
neutral_chroma_indication_flag | u(1)
field_seq_flag | u(1)
timing_info_present_flag | u(1)
if( timing_info_present_flag ) { | 
num_units_in_tick | u(32)
time_scale | u(32)
fixed_pic_rate_flag | u(1)
} | 
nal_hrd_parameters_present_flag | u(1)
if( nal_hrd_parameters_present_flag ) | 
hrd_parameters( ) | 
vcl_hrd_parameters_present_flag | u(1)
if( vcl_hrd_parameters_present_flag ) | 
hrd_parameters( ) | 
if( nal_hrd_parameters_present_flag ¦ ¦ vcl_hrd_parameters_present_flag ) { // ed - missing ? | 
low_delay_hrd_flag | u(1)
sub_pic_cpb_params_present_flag | u(1)
if( sub_pic_cpb_params_present_flag ) | 
num_units_in_sub_tick | u(32)
} | 
bitstream_restriction_flag | u(1)
if( bitstream_restriction_flag ) { | 
tiles_fixed_structure_flag | u(1)
motion_vectors_over_pic_boundaries_flag | u(1)
max_bytes_per_pic_denom | ue(v)
max_bits_per_mincu_denom | ue(v)
log2_max_mv_length_horizontal | ue(v)
log2_max_mv_length_vertical | ue(v)
} | 
} | 

## Slide 3: VUI Extension for Temporal Scalability: Option-1
vui_parameters( ) { | Descriptor
..... edited out .... | .......
vui_num_temporal_layers_minus1 | u(3)
for (i=0; i<vui_num_temporal_layers_minus1; i++ ) { // iterative loop starts | 
vui_temporal_id[i] | u(3)
field_seq_flag[i] | u(1)
timing_info_present_flag[i] | u(1)
if( timing_info_present_flag[i] ) { | 
num_units_in_tick[i] | u(32)
time_scale[i] | u(32)
fixed_pic_rate_flag[i] | u(1)
} | 
nal_hrd_parameters_present_flag[i] | u(1)
if( nal_hrd_parameters_present_flag[i] ) | 
hrd_parameters( ) | 
vcl_hrd_parameters_present_flag[i] | u(1)
if( vcl_hrd_parameters_present_flag[i] ) | 
hrd_parameters( ) | 
if( nal_hrd_parameters_present_flag[i] ¦ ¦ vcl_hrd_parameters_present_flag[i] ) { // ed - missing ? | 
low_delay_hrd_flag[i] | u(1)
sub_pic_cpb_params_present_flag[i] | u(1)
if( sub_pic_cpb_params_present_flag[i] ) | 
num_units_in_sub_tick[i] | u(32)
} | 
} // iterative loop ends for temporal layers | 
bitstream_restriction_flag | u(1)
if( bitstream_restriction_flag ) { | 
tiles_fixed_structure_flag | u(1)
motion_vectors_over_pic_boundaries_flag | u(1)
max_bytes_per_pic_denom | ue(v)
max_bits_per_mincu_denom | ue(v)
log2_max_mv_length_horizontal | ue(v)
log2_max_mv_length_vertical | ue(v)
} | 
vui_extension_flag | u(1)
if( vui_extension_flag ) { | 
while( more_rbsp_data() ) | 
vui_extension_data_flag | u(1)
} | 
rbsp_trailing_bits() | 
} | 

## Slide 4
VUI Extension for Temporal Scalability: Option-2
vui_parameters( ) { | Descriptor
..... edited out .... | .......
field_seq_flag | u(1)
timing_info_present_flag | u(1)
if( timing_info_present_flag ) { | 
num_units_in_tick | u(32)
time_scale | u(32)
fixed_pic_rate_flag | u(1)
} | 
vui_num_temporal_layers_minus1 | u(3)
for (i=0; i<=vui_num_temporal_layers_minus1; i++ ) { // iterative loop starts | 
vui_temporal_id[i] | u(3)
nal_hrd_parameters_present_flag[i] | u(1)
if( nal_hrd_parameters_present_flag[i] ) | 
hrd_parameters( ) | 
vcl_hrd_parameters_present_flag[i] | u(1)
if( vcl_hrd_parameters_present_flag[i] ) | 
hrd_parameters( ) | 
if( nal_hrd_parameters_present_flag[i] ¦ ¦ vcl_hrd_parameters_present_flag[i] ) { // ed - missing ? | 
low_delay_hrd_flag[i] | u(1)
sub_pic_cpb_params_present_flag[i] | u(1)
if( sub_pic_cpb_params_present_flag[i] ) | 
num_units_in_sub_tick[i] | u(32)
} | 
} // iterative loop ends for temporal layers | 
bitstream_restriction_flag | u(1)
if( bitstream_restriction_flag ) { | 
tiles_fixed_structure_flag | u(1)
motion_vectors_over_pic_boundaries_flag | u(1)
max_bytes_per_pic_denom | ue(v)
max_bits_per_mincu_denom | ue(v)
log2_max_mv_length_horizontal | ue(v)
log2_max_mv_length_vertical | ue(v)
} | 
vui_extension_flag | u(1)
if( vui_extension_flag ) { | 
while( more_rbsp_data() ) | 
vui_extension_data_flag | u(1)
} | 
rbsp_trailing_bits() | 
} | 

## Slide 5: Backup

## Slide 6: SVC & MVC VUI Extensions
svc_vui_parameters_extension( ) { | Descriptor
vui_ext_num_entries_minus1 | ue(v)
for( i = 0; i <= vui_ext_num_entries_minus1; i++ ) { | 
vui_ext_dependency_id[ i ] | u(3)
vui_ext_quality_id[ i ] | u(4)
vui_ext_temporal_id[ i ] | u(3)
vui_ext_timing_info_present_flag[ i ] | u(1)
if( vui_ext_timing_info_present_flag[ i ] ) { | 
vui_ext_num_units_in_tick[ i ] | u(32)
vui_ext_time_scale[ i ] | u(32)
vui_ext_fixed_frame_rate_flag[ i ] | u(1)
} | 
vui_ext_nal_hrd_parameters_present_flag[ i ] | u(1)
if( vui_ext_nal_hrd_parameters_present_flag[ i ] ) | 
hrd_parameters( ) | 
vui_ext_vcl_hrd_parameters_present_flag[ i ] | u(1)
if( vui_ext_vcl_hrd_parameters_present_flag[ i ] ) | 
hrd_parameters( ) | 
if( vui_ext_nal_hrd_parameters_present_flag[ i ] ¦ ¦ vui_ext_vcl_hrd_parameters_present_flag[ i ] ) | 
vui_ext_low_delay_hrd_flag[ i ] | u(1)
vui_ext_pic_struct_present_flag[ i ] | u(1)
} | 
} | 
mvc_vui_parameters_extension( ) { | Descriptor
vui_mvc_num_ops_minus1 | ue(v)
for( i = 0; i <= vui_mvc_num_ops_minus1; i++ ) { | 
vui_mvc_temporal_id[ i ] | u(3)
vui_mvc_num_target_output_views_minus1[ i ] | ue(v)
for( j = 0; j <= vui_mvc_num_target_output_views_minus1[ i ]; j++ ) | 
vui_mvc_view_id[ i ][ j ] | ue(v)
vui_mvc_timing_info_present_flag[ i ] | u(1)
if( vui_mvc_timing_info_present_flag[ i ] ) { | 
vui_mvc_num_units_in_tick[ i ] | u(32)
vui_mvc_time_scale[ i ] | u(32)
vui_mvc_fixed_frame_rate_flag[ i ] | u(1)
} | 
vui_mvc_nal_hrd_parameters_present_flag[ i ] | u(1)
if( vui_mvc_nal_hrd_parameters_present_flag[ i ] ) | 
hrd_parameters( ) | 
vui_mvc_vcl_hrd_parameters_present_flag[ i ] | u(1)
if( vui_mvc_vcl_hrd_parameters_present_flag[ i ] ) | 
hrd_parameters( ) | 
if( vui_mvc_nal_hrd_parameters_present_flag[ i ] ¦ ¦ vui_mvc_vcl_hrd_parameters_present_flag[ i ] ) | 
vui_mvc_low_delay_hrd_flag[ i ] | u(1)
vui_mvc_pic_struct_present_flag[ i ] | u(1)
} | 
} |