## Slide 1
Cheung Auyeung
Sony Electronics Inc
July 1, 2012
Luma Intra Planar Prediction Filter
Notes: 1

## Slide 2: HM7 Luma Intra Prediction
Apply FIR Filter Here
PredIntraPlanar
PredIntraAng
DCPredFiltering
mode == planar
mode == DC
& above & left
available
yes
no
yes
no
Predicted WxH
Apply FIR Filter Here
DCPredFiltering filters the top row and the left columns of an intra predicted area with
FIR filters

## Slide 3: Luma Intra Prediction Experiments
PredIntraPlanar
PredIntraAng
DCPredFiltering
mode == planar
mode ≤ DC
& above & left
available
yes
no
yes
no
Apply HM7 DC prediction filtering to both DC and Planar prediction
PredIntraPlanar
PredIntraAng
mode == planar
yes
no
Removed prediction filtering to both DC and Planar prediction

## Slide 4: BDR Results
Apply filter to both Planar and DC prediction:
  BDR = -0.1%
No Filter to both Planar and DC prediction:
  BDR = 0.1 %
Planar prediction filter is complementary to DC prediction filter with similar gain and complexity.
DC prediction filter is not effective for Class F.
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.109% | -0.113% | -0.142% | -0.132% | -0.156% | -0.198%
Class B | -0.057% | -0.108% | -0.145% | -0.089% | -0.133% | -0.198%
Class C | -0.080% | -0.133% | -0.112% | -0.068% | -0.122% | -0.120%
Class D | -0.085% | -0.102% | -0.070% | -0.064% | -0.124% | -0.181%
Class E | -0.227% | -0.197% | -0.190% | -0.182% | -0.204% | -0.109%
Overall | -0.103% | -0.126% | -0.129% | -0.102% | -0.144% | -0.166%
 | -0.104% | -0.129% | -0.122% | -0.103% | -0.142% | -0.156%
Class F | -0.096% | -0.030% | -0.113% | -0.066% | -0.191% | -0.067%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 101% |  |  | 100% |  | 
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.207% | 0.344% | 0.341% | 0.237% | 0.288% | 0.302%
Class B | 0.113% | 0.210% | 0.230% | 0.149% | 0.217% | 0.200%
Class C | 0.085% | 0.117% | 0.175% | 0.076% | 0.143% | 0.175%
Class D | 0.069% | 0.132% | 0.134% | 0.057% | 0.172% | 0.131%
Class E | 0.086% | 0.114% | 0.101% | 0.053% | 0.118% | 0.170%
Overall | 0.113% | 0.188% | 0.203% | 0.119% | 0.193% | 0.197%
 | 0.117% | 0.187% | 0.204% | 0.123% | 0.192% | 0.199%
Class F | -0.182% | -0.001% | 0.021% | -0.200% | -0.326% | -0.114%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 5: Summary
The DC prediction filter and the proposed planar prediction filter is the same filter.
Planar prediction filter is complementary to DC prediction filter with similar gain and complexity trade-off.
  When DC prediction filter is removed from HM7, intra BDR = 0.1%
  When Planar prediction filter is added to HM7, intra BDR = -0.1%
No additional implementation complexity to HM7 software and hardware.
Propose to adopt luma intra planar prediction filter in WD8 and HM8.