## Slide 1: JCTVC-J0297: AHG5: High throughput binarization method for reference index coding
Seung-Hwan Kim, Louis Kerofsky,
Andrew Segall
<number>
Notes: <number>

## Slide 2: Motivation
HM 7.0 requires 15 context bins in worst case scenario
- Truncated unary binarization
- Maximum reference index is 15
- All bins are context coded
Important to reduce the worst case number of context bins
- Hardware is designed considering the worst case-scenario
<number>
Notes: <number>

## Slide 3
Proposed Method
ref_index | HM 7.0 | Method1 | Method2
0 | 0 | 0 | 0
1 | 10 | 10 | 10
2 | 110 | 110 | 110
3 | 1110 | 1110 | 1110
4 | 11110 | 1111 xxxx | 1111 xxxx
5 | 111110 | 1111 xxxx | 1111 xxxx
6 | 1111110 | 1111 xxxx | 1111 xxxx
7 | 11111110 | 1111 xxxx | 1111 xxxx
8 | 111111110 | 1111 xxxx | 1111 xxxx
9 | 1111111110 | 1111 xxxx | 1111 xxxx
10 | 11111111110 | 1111 xxxx | 1111 xxxx
11 | 111111111110 | 1111 xxxx | 1111 xxxx
… | … | … | …
15 | 1111111 … 11111 | 1111 xxxx | 1111 xxxx
Propose TUFLC (Truncated Unary-Fixed Length Code) binarization
* context coded bins are marked with red color
* Method 2 employs the same context model used in JCTVC-I352 JCTVC-J0098, and JCTVC-J0176

## Slide 4: Invention
Worst case bin number
Improved worst case bin number
 | HM7.0 | Method1 | Method2
Max_total_bins | 15 | 8 | 8
Max_ctx_bins | 15 | 4 | 2
Max_bypass_bins | 0 | 4 | 6

## Slide 5: Results: Method 1
<number>
Implemented into HM 7.0
No coding performance change
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class B | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class C | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class D | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class E |  |  |  |  |  | 
Overall | 0.000% | 0.000% | 0.000% | 0.00% | 0.00% | 0.00%
 | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class F | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class C | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class D | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class E | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Overall | 0.000% | 0.000% | 0.000% | 0.00% | 0.00% | 0.00%
 | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class F | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%

## Slide 6: Results: Method 2
<number>
Implemented into HM 7.0
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.01% | -0.17% | -0.15% | 0.01% | -0.13% | 0.03%
Class B | 0.01% | -0.02% | 0.00% | 0.00% | 0.01% | 0.02%
Class C | -0.01% | 0.05% | 0.06% | 0.01% | -0.03% | -0.06%
Class D | 0.02% | -0.04% | -0.02% | -0.02% | 0.04% | -0.01%
Class E |  |  |  |  |  | 
Overall | 0.00% | -0.05% | -0.02% | 0.00% | -0.03% | 0.00%
 | 0.01% | -0.04% | -0.03% | 0.00% | -0.02% | -0.01%
Class F | 0.01% | 0.06% | 0.02% | -0.01% | 0.00% | 0.04%
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.02% | 0.23% | 0.09% | -0.01% | 0.13% | 0.07%
Class C | 0.01% | -0.01% | 0.00% | 0.00% | 0.06% | 0.25%
Class D | 0.01% | 0.21% | 0.06% | -0.03% | 0.03% | 0.04%
Class E | -0.04% | 0.05% | -0.27% | 0.09% | -0.34% | 0.15%
Overall | 0.00% | 0.13% | -0.01% | 0.01% | 0.00% | 0.13%
 | 0.00% | 0.07% | -0.02% | 0.01% | 0.06% | 0.19%
Class F | -0.07% | 0.17% | 0.09% | 0.09% | 0.44% | 0.77%

## Slide 7: Conclusion
Improve high throughput performance
No coding loss
Suffix part (fixed length code) is efficiently coded because the number of bypass coded bits are fixed/known
<number>
 | HM7.0 | Method1 | Method2
Max_total_bins | 15 | 8 | 8
Max_ctx_bins | 15 | 4 | 2
Max_bypass_bins | 0 | 4 | 6
Notes: <number>