## Slide 1: JCTVC-J0297: AHG5: High throughput binarization method for reference index coding
Seung-Hwan Kim, Louis Kerofsky,
Andrew Segall
<number>
Notes: <number>

## Slide 2: Motivation
HM 7.0 requires 15 context bins in worst case scenario
- Truncated unary binarization
- Maximum reference index is 15
- All bins are context coded
Important to reduce the worst case number of context bins
- Hardware is designed considering the worst case-scenario
<number>
Notes: <number>

## Slide 3
Proposed Method
ref_index | HM 7.0 | TUFLC
0 | 0 | 0
1 | 10 | 10
2 | 110 | 110
3 | 1110 | 1110
4 | 11110 | 1111 xxxx
5 | 111110 | 1111 xxxx
6 | 1111110 | 1111 xxxx
7 | 11111110 | 1111 xxxx
8 | 111111110 | 1111 xxxx
9 | 1111111110 | 1111 xxxx
10 | 11111111110 | 1111 xxxx
11 | 111111111110 | 1111 xxxx
… | … | …
15 | 1111111 … 11111 | 1111 xxxx
Propose TUFLC (Truncated Unary-Fixed Length Code) binarization
to improve throughput performance in the worst case
* context coded bins are marked with red color

## Slide 4: Invention
Worst case bin number
Improved worst case bin number
 | HM7.0 | Proposed Method (TUFLC)
Max_total_bins | 15 | 8
Max_ctx_bins | 15 | 4
Max_bypass_bins | 0 | 4

## Slide 5: Results
<number>
Implemented into HM 7.0
No coding performance change
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class B | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class C | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class D | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class E |  |  |  |  |  | 
Overall | 0.000% | 0.000% | 0.000% | 0.00% | 0.00% | 0.00%
 | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class F | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class C | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class D | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class E | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Overall | 0.000% | 0.000% | 0.000% | 0.00% | 0.00% | 0.00%
 | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class F | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%

## Slide 6: Conclusion
Improve high throughput performance
No coding loss
Suffix part (fixed length code) is efficiently coded because the number of bypass coded bits are fixed/known
<number>
 | HM7.0 | Proposed Method (TUFLC)
Max_total_bins | 15 | 8
Max_ctx_bins | 15 | 4
Max_bypass_bins | 0 | 4
Notes: <number>