## Slide 1: JCTVC-J0298: AHG5: High throughput binarization for cu_qp_delta coding
Seung-Hwan Kim, Louis Kerofsky,
Andrew Segall
<number>
Notes: <number>

## Slide 2: Motivation
HM 7.0 requires 26 context bins and 1 bypass bin in worst case scenario (main profile)
- Truncated unary binarization
Important to reduce the worst case number of context bins
- Hardware is designed considering the worst case-scenario
<number>
Notes: <number>

## Slide 3
Proposed Method
Propose TUFLC (Truncated Unary-Fixed Length Code) binarization
to improve throughput performance in the worst case
* context coded bins are marked with red color
cu_delta_qp | HM 7.0 (TU) | TUFLC
0 | 0 | 0
1 | 10 | 10
2 | 110 | 110
3 | 1110 | 1110
4 | 11110 | 11110
5 | 111110 | 111110
6 | 1111110 | 1111110
7 | 11111110 | 11111110
8 | 111111110 | 111111110
9 | 1111111110 | 111111111 xxxxx
10 | 11111111110 | 111111111 xxxxx
11 | 111111111110 | 111111111 xxxxx
… | … | …
26 | 1111111 … 11111 | 111111111 xxxxx

## Slide 4: Invention
Worst case bin number
Improved worst case bin number
 | HM7.0 | Proposed Method (TUFLC)
Max_total_bins | 27 | 16
Max_ctx_bins | 26 | 4
Max_bypass_bins | 1 (sign bit) | 12

## Slide 5: Results
<number>
Implemented into HM 7.0
Coding performance changes (Y) from -0.02% to 0.02%
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.02% | 0.01% | 0.00% | 0.02% | 0.00% | 0.06%
Class B | 0.00% | 0.00% | -0.01% | 0.01% | 0.00% | 0.01%
Class C | 0.00% | 0.02% | 0.02% | 0.00% | 0.01% | 0.02%
Class D | -0.01% | 0.00% | 0.04% | 0.01% | -0.03% | -0.02%
Class E | 0.05% | 0.03% | 0.04% | 0.05% | 0.09% | 0.07%
Overall | 0.01% | 0.01% | 0.02% | 0.02% | 0.01% | 0.02%
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.02% | -0.10% | 0.10% | -0.07% | 0.15% | 0.26%
Class B | -0.01% | -0.06% | 0.08% | 0.00% | 0.03% | -0.05%
Class C | 0.02% | -0.03% | 0.17% | 0.00% | 0.00% | 0.13%
Class D | 0.02% | 0.28% | 0.12% | 0.01% | 0.30% | -0.12%
Class E |  |  |  |  |  | 
Overall | 0.00% | 0.02% | 0.11% | -0.02% | 0.11% | 0.05%
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.02% | -0.28% | -0.09% | 0.00% | -0.04% | 0.51%
Class C | -0.02% | 0.24% | 0.23% | 0.01% | 0.20% | -0.05%
Class D | -0.01% | 0.06% | 0.64% | -0.08% | 0.09% | -0.08%
Class E | -0.01% | -0.31% | -0.25% | -0.04% | -0.30% | 0.61%
Overall | -0.01% | -0.07% | 0.14% | -0.02% | 0.00% | 0.24%

## Slide 6: Conclusion
Improved throughput performance
No coding loss (-0.02% ~0.02%)
Suffix part (fixed length code) is efficiently coded because the number of bypass coded bits are fixed/known
<number>
 | HM7.0 | Proposed Method (TUFLC)
Max_total_bins | 27 | 16
Max_ctx_bins | 26 | 4
Max_bypass_bins | 1 (sign bit) | 12
Notes: <number>