## Slide 1: JCTVC-J0299: AHG4: On entry point coding
Seung-Hwan Kim, Kiran Misra,
Andrew Segall
<number>
Notes: <number>

## Slide 2: Proposed Entry point offset coding
Two methods to further improve the coding efficiency of entry point offset information
Modify binarization process for the entry point information
- Use a combination of quotient and remainder coding
- The Quotient and the remainder are coded ue(v) and u(v), respectively
- The divisor is sent in the bit-stream (transmit the power of 2 of the divisor)
Modify the meaning of entry point offset
- Use minimum entry point offset as a predictor
- Difference between each entry point offset and minimum entry point
offset is transmitted
<number>
Notes: <number>

## Slide 3: Proposed Method
slice_header( ) { | Descriptor
… | …
if( tiles_or_entropy_coding_sync_idc > 0 ) { | 
num_entry_point_offsets | ue(v)
if( num_entry_point_offsets > 0 ) { | 
min_offst_minus1 | ue(v)
divisor_power_of_two_minus1 | ue(v)
for( i = 0; i < num_entry_point_offsets; i++ ) | 
entry_point_quotient[i] | ue(v)
entry_point_remainder[i] | u(v)
} | 
} | 
} | 

## Slide 4: Results: Experiment 1: 32 Tiles
<number>
Implemented into HM 7.0
32 Tiles (Tested sequence: Class A, Class B, Class E)
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class B | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class E | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.02% | -0.01% | -0.01% | -0.02% | -0.01% | -0.01%
Class B | -0.06% | -0.05% | -0.04% | -0.06% | -0.05% | -0.04%
Class E |  |  |  |  |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.04% | -0.03% | -0.03% | -0.04% | -0.03% | -0.03%
Class E | -0.82% | -0.72% | -0.73% | -0.81% | -0.72% | -0.71%

## Slide 5: Results: Experiment 2
<number>
Implemented into HM 7.0
Exp 2 (in JCTVC-F335)
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class E | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class E |  |  |  |  |  | 
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class E | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%

## Slide 6: Conclusion
This contribution reports coding efficiency improvements for entry point offset coding (-0.8% for class E)
Proposed method is designed to deal with all the variations of the entry point offset by sending the divisor information
It is recommended to adopt this method into the draft text.
<number>
Notes: <number>