## Slide 1: Slice Header Syntax Cleanup JCTVC-J0300
Yue Yu, Jian Lou and Limin Wang
Motorola Mobility

## Slide 2
In the current slice header design, some syntax and function calls, even under the same logic conditions spread in different locations in slice header. Such design is not only messy for presentation of slice header syntax, but also requires more logic condition checking.
The syntax in the current slice header
Notes: <number>

## Slide 3: New Design for Slice Header
All syntax elements and function calls under slice type not equal to I are grouped together.
slice_temporal_mvp_enable_flag instead of pic_temporal_mvp_enable_flag make the standard more readable.
Nine Syntax Elements: slice_temporal_mvp_enable_flag, num_ref_idx_active_override_flag, num_ref_idx_l0_active_minus1, num_ref_idx_l1_active_minus1, mvd_l1_zero_flag, cabac_init_flag, collocated_from_l0_flag, collocated_ref_idx, five_minus_max_num_merge_cand
Two Function Calls: ref_pic_list_modification( ), pred_weight_table( )

## Slide 7
Reference picture list modification syntax

## Slide 9: Conclusion
All syntax elements and function calls under slice type not equal to I are grouped together.
Suggest to use slice_temporal_mvp_enable_flag instead of pic_temporal_mvp_enable_flag to make standard more readable.
It is recommended to adopt this syntax cleanup.
Thanks mental cross check: JCTVC-J0495 from Qualcomm