## Slide 1: J0306: On Sub-picture Based CPB
Sachin Deshpande
Sharp Labs of America
<number>
Notes: <number>

## Slide 2: Introduction & Proposals
HEVC Draft 7 supports sub-picture based CPB operation in addition to access unit based CPB operation
We describe three proposed changes to the sub-picture based CPB operation.
  Proposal1: A simplified syntax for picture timing SEI message for sub-picture based CPB related parameters.
  Proposal 2: When sub_pic_cpb_params_present_flag equals to 1 then sub-picture level CPB removal delay parameters are present and the CPB may operate at access unit level or sub-picture level. We proposes a bitstream conformance requirement, which guarantees that the operation of CPB operating at sub-picture level and CPB operating at access unit level results in the same timing of decoding unit removal.
  Proposal 3: When sub-picture level CPB removal delay parameters are present we proposes a change in the removal time of decoding unit when low_delay_hrd_flag is 1 and tr,n( m ) < taf( m ) to compensate for difference that can arise due to clock tick counter and sub-picture clock tick counter.
<number>
Notes: <number>

## Slide 3: Proposal 1: Simplified Syntax for Picture Timing SEI
We propose modification to Picture Timing SEI message
The proposed simplified syntax allows signaling a single decoding unit CPB removal delay parameter (common_du_cpb_removal_delay) instead of separate parameters (du_cpb_removal_delay[ i ] for each of the num_decoding_units_minus1+1 decoding units) that currently must be signaled for each decoding unit.
Proposed syntax is more efficient when each sub-picture is removed from CPB at a regular interval.
Also for this the proposed CPB removal delay parameter signals delay (common_du_cpb_removal_delay ) after removal of last decoding unit.
<number>

## Slide 4: Proposal 1: Simplified Syntax for Picture Timing SEI
common_du_cpb_removal_delay_flag equal to 1/0 specifies that the syntax element common_du_cpb_removal_delay is present/ not present.
common_du_cpb_removal_delay specifies how many sub-picture clock ticks (see subclause E.2.1) to wait after removal from the CPB of the last decoding unit before removing from the CPB the current decoding unit in the access unit associated with the picture timing SEI message.
C.2.2. Timing of decoding unit removal and decoding of decoding unit
If SubPicCpbFlag is equal to 1 and common_du_cpb_removal_delay_flag is 1 the variable CpbRemovalDelay( m ) is set to the value of (m+1)*common_du_cpb_removal_delay for decoding unit m (with m ranging from 0 to num_decoding_units_minus1) in the picture timing SEI message associated with the access unit that contains decoding unit m, and the variable Tc is set to tc_sub.

## Slide 5: Proposal 2: Bitstream Conformance Requirement
When sub_pic_cpb_params_present_flag equals to 1 then sub-picture level CPB removal delay parameters are present and the CPB may operate at access unit level or sub-picture level.
We propose following: bitstream conformance requirement, which guarantees that the operation of sub picture based CPB operating at sub-picture level and CPB operating at access unit level results in the same timing of decoding unit removal.
Option1: If sub_pic_cpb_params_present_flag is 1 then it is a requirement of the bitstream conformance that following constraint is obeyed when signaling the values for cpb_removal_delay and du_cpb_removal_delay.
Option2: If sub_pic_cpb_params_present_flag is 1 then it is a requirement of the bitstream conformance that following constraint is obeyed when signaling the values for cpb_removal_delay and du_cpb_removal_delay.
<number>
cpb_removal_delay*tc=(du_cpb_removal_delay[num_decoding_units_minus1])*tc_sub
-1<= (cpb_removal_delay* num_units_in_tick - du_cpb_removal_delay[num_decoding_units_minus1] * num_units_in_sub_tick ) <= 1
where tc = num_units_in_tick ÷time_scale, tc_sub = num_units_in_sub_tick ÷time_scale

## Slide 6: Proposal 3: Change in Timing of Decoding Unit Removal
When sub-picture level CPB removal delay parameters are present the CPB may operate at access unit level or sub-picture level.
We propose a change in the removal time of decoding unit when low_delay_hrd_flag is 1 and tr,n( m ) < taf( m ) to compensate for difference that can arise due to clock tick counter and sub-picture clock tick counter discrepancy.
<number>

## Slide 7: Proposal 3: Change in Timing of Decoding Unit Removal
<number>
Sub-picture based
Access Unit based
  C.2.2. Timing of decoding unit removal and decoding of decoding unit

## Slide 8: Proposal
The document proposed following modifications to sub-picture based CPB
  Proposal1: A simplified syntax for picture timing SEI message for sub-picture based CPB related parameters.
  Proposal 2: A bitstream conformance requirement, which guarantees that the operation of sub picture based CPB operating at sub-picture level and CPB operating at access unit level results in the same timing of decoding unit removal.
  Proposal 3: A change in the removal time of decoding unit when low_delay_hrd_flag is 1 and tr,n( m ) < taf( m ) to compensate for difference that can arise due to clock tick counter and sub-picture clock tick counter.
We propose to adopt our proposals in HEVC.
<number>