## Slide 1
Redundancy removal on InterDir Syntax
(JCTVC-J0312)
Chanyul Kim, Tammy Lee, Elena Alshina
(Samsung)
Notes: <number>

## Slide 2: Background
In the previous meeting, the restriction of bi-prediction by 4x8/8x4 PU was adopted in order to reduce memory bandwidth (I0297).
the encoder still signals the bi-prediction of 4x8/8x4 PU, the decoder ignores it.
Removal of syntax for bi-prediction of small PU is recommended in terms of fixing redundancy (It is a sort of bug-fix for adopting of I0297).
It gives -0.1% gain for LB cases.
(It is noted that I0267 reported 0.4% loss for LDB compared to HM6.0)
<number>

## Slide 3: SW change
<number>
if(!pcCU->isBipredRestriction(uiAbsPartIdx))
{
m_pcBinIf->encodeBin( uiInterDir == 2 ? 1 : 0, *( pCtx + uiCtx ) );
}
m_pcBinIf->encodeBin( uiInterDir == 2 ? 1 : 0, *( pCtx + uiCtx ) );

## Slide 4: Results
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.1%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1%
Class D | -0.1% | 0.1% | -0.2% | -0.1% | 0.0% | -0.1%
Class E |  |  |  |  |  | 
Overall | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1%
Class F | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.1%
Enc Time[%] | 99% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | 0.1% | 0.2% | 0.0% | 0.1% | 0.2%
Class C | -0.1% | 0.1% | -0.1% | -0.1% | -0.2% | 0.2%
Class D | -0.1% | -0.2% | 0.3% | -0.2% | -0.2% | -0.2%
Class E | 0.0% | 0.2% | 0.0% | 0.1% | 0.0% | 0.4%
Overall | -0.1% | 0.0% | 0.1% | -0.1% | -0.1% | 0.1%
 | -0.1% | 0.0% | 0.1% | -0.1% | 0.0% | 0.2%
Class F | -0.1% | 0.7% | 0.0% | 0.0% | -0.1% | 0.9%
Enc Time[%] | 100% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 103% |  | 
<number>

## Slide 5: Conclusion
Removal of syntax for bi-prediction of small PU
It gives -0.1% gain for LB cases.
It is a sort of bug-fix for previous adopting of I0297.
<number>