## Slide 1
Context reduction for MVD coding
(JCTVC-J0315)
Chanyul Kim, Tammy Lee, Elena Alshina
(Samsung)
Notes: <number>

## Slide 2: Background
The two flags, abs_mvd_greater0_flag, and abs_mvd_greater1_flag, are used for context for MVD in the current HM
The distribution between ‘0’ and ‘1’ is similar, so, the use of context is not much benefit for separating ‘0’ and ‘1’.
abs_mvd_greater1_flag is coded as context and abs_mvd_greater0_flag is coded with bypass mode.
The proposed method reduces contexts from 2 to 1. No loss and complexity is observed.
<number>

## Slide 3: Proposed
<number>

## Slide 4: Results(1)
<number>
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.05% | -0.15% | -0.09% | 0.04% | -0.14% | 0.23%
Class B | 0.00% | 0.06% | 0.04% | 0.03% | 0.03% | 0.03%
Class C | 0.00% | 0.06% | 0.06% | 0.05% | 0.06% | 0.05%
Class D | 0.00% | -0.01% | -0.02% | -0.01% | -0.03% | -0.13%
Class E |  |  |  |  |  | 
Overall | -0.01% | 0.00% | 0.00% | 0.03% | -0.02% | 0.04%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class F | 0.15% | 0.16% | 0.20% | 0.13% | 0.05% | 0.12%
Enc Time[%] | 99% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.02% | 0.14% | 0.16% | 0.01% | 0.07% | 0.19%
Class C | -0.02% | 0.03% | 0.03% | -0.05% | -0.08% | -0.14%
Class D | -0.02% | 0.28% | -0.06% | -0.05% | -0.04% | 0.27%
Class E | -0.12% | -0.20% | -0.07% | 0.10% | -0.42% | 0.36%
Overall | -0.02% | 0.08% | 0.03% | 0.00% | -0.09% | 0.16%
 | 0.0% | 0.1% | 0.0% | 0.0% | -0.1% | 0.2%
Class F | 0.03% | -0.04% | 0.20% | 0.09% | -0.04% | 0.86%
Enc Time[%] | 99% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 102% |  | 

## Slide 5: Results(2) : AHG5
<number>
 | Bins relative to total bins |  |  |  | Total bins reduction ration
 | Test |  |  |  | 
 | ctx | bp |  |  | 
AI Main |  |  |  |  | 
RA Main | 98.57% | 103.39% |  |  | -0.10%
LB Main | 98.51% | 105.44% |  |  | -0.09%
LP Main |  |  |  |  | 
Average | 98.54% | 104.42% |  |  | -0.09%
 | Bins relative to total bins |  |  |  | Total bins reduction ration
 | Test |  |  |  | 
 | ctx | bp |  |  | 
AI HE10 |  |  |  |  | 
RA HE10 | 98.56% | 103.40% |  |  | -0.11%
LB HE10 | 98.50% | 105.40% |  |  | -0.07%
LP HE10 |  |  |  |  | 
Average | 98.53% | 104.40% |  |  | -0.09%

## Slide 6: Conclusion
One context is removed for MVD coding.
From the statistical analysis, it is desirable to code between ‘0’ and ‘1’ with bypass mode.
No loss is observed. Moreover -0.12% gain for main LDB E class.
Contexts are reduced from 2 to 1.
<number>