## Slide 1: Further Unification of Luma/Chroma Context Derivation for Last Position Coding (JCTVC-J0319)
Liwei Guo, Marta Karczewicz, Wei-Jung Chien

## Slide 2: Introduction
Context derivation for last significant position (LAST) in HM7
  Equation based approach
    ctx_idx = m + (bin_idx>>n)
  Luma and Chroma are unified using the same equation but with different parameter values
Proposed: further unification of context derivation for LAST
  Same value of parameter n for Luma and Chroma

## Slide 3: LAST context derivation in HM7
Equation based context derivation
  ctx_idx = m+ (bin_idx>>n)
    m: offset parameter; n: shift parameter
Parameter values for Luma and Chroma
  k = log2TUSizeMinus2
  Chroma context assignment
bin_idx | 0 | 1 | 2 | 3 | 4 | 5 | 6
TU 4x4 | 15 | 16 | 17 |  |  |  | 
TU 8x8 | 15 | 15 | 16 | 16 | 17 |  | 
TU 16x16 | 15 | 15 | 15 | 15 | 16 | 16 | 16
 | Luma | Chroma
m | 3* k + ((k+1)>>2) | 15
n | (k+3)>>2 | k

## Slide 4: Proposed change:
 | Luma | Chroma
m | 3* k + ((k+1)>>2) | 15
n | (k+3)>>2 | (k+3)>>2
bin_idx | 0 | 1 | 2 | 3 | 4 | 5 | 6
TU 4x4 | 15 | 16 | 17 |  |  |  | 
TU 8x8 | 15 | 15 | 16 | 16 | 17 |  | 
TU 16x16 | 15 | 15 | 16 | 16 | 17 | 17 | 18
Using the same value of n for Luma and Chroma
Chroma context assignment with the proposed change
  The number of contexts increases by 2 (1 for X, 1 for Y)

## Slide 5: WD Text Change

## Slide 6: Simulation results – Summary
All Intra Main |  |  | All Intra HE10 |  | 
Y | U | V | Y | U | V
0.00% | 0.07% | 0.04% | 0.00% | 0.05% | 0.03%
Random Access Main |  |  | Random Access HE10 |  | 
Y | U | V | Y | U | V
-0.02% | 0.01% | -0.02% | -0.02% | 0.07% | 0.01%
Low delay B Main |  |  | Low delay B HE10 |  | 
Y | U | V | Y | U | V
0.00% | 0.16% | 0.28% | 0.02% | 0.08% | -0.04%
Low delay P Main |  |  | Low delay P HE10 |  | 
Y | U | V | Y | U | V
-0.02% | 0.21% | 0.19% | -0.03% | 0.26% | -0.39%
Common test conditions.
Results averaged over all sequences including Class F.
Cross-checked by LG.

## Slide 7: Simulation - AI
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.01% | 0.01% | -0.01% | 0.01% | -0.02% | 0.01%
Class B | 0.01% | 0.09% | 0.05% | 0.00% | 0.10% | 0.02%
Class C | 0.00% | 0.06% | 0.05% | 0.00% | 0.07% | 0.04%
Class D | -0.01% | 0.14% | 0.09% | 0.00% | 0.09% | 0.00%
Class E | 0.00% | 0.05% | 0.05% | 0.00% | 0.00% | 0.07%
Class F | -0.01% | 0.08% | 0.02% | -0.02% | 0.04% | 0.03%
Overall | 0.00% | 0.07% | 0.04% | 0.00% | 0.05% | 0.03%
 | 0.00% | 0.07% | 0.04% | 0.00% | 0.04% | 0.04%
Enc Time[%] | 98.30% |  |  | 99.25% |  | 
Dec Time[%] | 101.14% |  |  | 99.69% |  | 

## Slide 8: Simulation - RA
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.03% | -0.36% | -0.05% | 0.01% | 0.12% | 0.10%
Class B | -0.02% | 0.06% | -0.07% | 0.00% | 0.03% | -0.02%
Class C | -0.04% | 0.13% | -0.05% | 0.00% | 0.10% | -0.02%
Class D | 0.02% | 0.24% | 0.14% | -0.04% | 0.06% | -0.15%
Class E |  |  |  |  |  | 
Class F | -0.04% | -0.01% | -0.05% | -0.05% | 0.08% | 0.12%
Overall | -0.02% | 0.01% | -0.02% | -0.02% | 0.07% | 0.01%
 | -0.03% | 0.02% | -0.03% | -0.02% | 0.05% | 0.01%
Enc Time[%] | 101.17% |  |  | 99.67% |  | 
Dec Time[%] | 101.38% |  |  | 98.43% |  | 

## Slide 9: Simulation – LD
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.00% | 0.26% | 0.39% | -0.01% | 0.21% | 0.07%
Class C | -0.04% | 0.11% | -0.04% | 0.03% | 0.05% | 0.22%
Class D | 0.00% | 0.28% | 0.20% | -0.07% | 0.13% | -0.25%
Class E | -0.06% | 0.24% | 0.05% | 0.03% | -0.36% | -1.18%
Class F | 0.06% | -0.10% | 0.71% | 0.11% | 0.20% | 0.63%
Overall | 0.00% | 0.16% | 0.28% | 0.02% | 0.08% | -0.04%
 | 0.00% | 0.16% | 0.25% | 0.02% | 0.09% | 0.12%
Enc Time[%] | 99.83% |  |  | 99.62% |  | 
Dec Time[%] | 99.81% |  |  | 99.91% |  | 

## Slide 10: Simulation – LDP
 | Low delay P Main |  |  | Low delay P HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.03% | 0.32% | -0.27% | 0.00% | 0.33% | -0.46%
Class C | -0.01% | -0.10% | -0.32% | -0.01% | -0.09% | 0.20%
Class D | 0.09% | 0.42% | 0.51% | -0.02% | 0.24% | -0.30%
Class E | -0.07% | -0.11% | 0.82% | 0.00% | 0.22% | -1.71%
Class F | -0.07% | 0.41% | 0.51% | -0.13% | 0.57% | 0.01%
Overall | -0.02% | 0.21% | 0.19% | -0.03% | 0.26% | -0.39%
 | -0.02% | 0.19% | 0.16% | -0.03% | 0.30% | -0.30%
Enc Time[%] | 99.27% |  |  | 100.16% |  | 
Dec Time[%] | 98.84% |  |  | 97.81% |  | 

## Slide 11: Conclusions
Proposed further unification of context derivation for LAST
  The value of shift parameter n is unified for Luma and Chroma.
0.0% Y BD-rate change.
Recommended adoption of the proposed method.
Thanks to LG (JCTVC-J0395) for cross-checking

## Slide 12
Thank you!