## Slide 1: JCTVC-J0342 Chroma QP range extension
Gary J. Sullivan, Sandeep Kanumuri, Ji-Zheng Xu, Yongjun Wu
Microsoft Corporation

## Slide 2: Issue in current HEVC design
Chroma QP is limited to the range [0, 39] whereas luma QP has a larger range [0, 51] (for a bit-depth of 8)
Chroma QP saturates at a much smaller value than luma QP
  Causes rate-control issues in low bit-rate applications
  May not be well-suited for some color formats
QPs used for chroma (QPCb and QPCr) are derived from the QP used for luma (QPY) using the equations and Table (8-11) below:
qPICb = Clip3( −QpBdOffsetC, 51, QPY + cb_qp_offset) (8‑255)
qPICr = Clip3( −QpBdOffsetC, 51, QPY + cr_qp_offset) (8‑256)
qPI | <30 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51
QPC | =qPI | 29 | 30 | 31 | 32 | 32 | 33 | 34 | 34 | 35 | 35 | 36 | 36 | 37 | 37 | 37 | 38 | 38 | 38 | 39 | 39 | 39 | 39

## Slide 3: Proposed solution
Extend chroma QP range using modifications shown in green qPICb = Clip3( −QpBdOffsetC, 57, QPY + cb_qp_offset) (8‑255)
qPICr = Clip3( −QpBdOffsetC, 57, QPY + cr_qp_offset) (8‑256)
Table above equivalent to the piece-wise linear function below:
if ( qPI < 30 )
QPC = qPI
else if ( qPI >= 30 && qPI <= 34 )
QPC = qPI − 1
else if ( qPI > 34 && qPI < 44 )
QPC = 33 + (qPI – 34) >> 1
else
QPC = qPI − 6
qPI | <30 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | >43
QPC | =qPI | 29 | 30 | 31 | 32 | 33 | 33 | 34 | 34 | 35 | 35 | 36 | 36 | 37 | 37 | = qPI – 6

## Slide 4: Graphical illustration of mapping from input QP (qPI) to output QP (QPC)
The above graph illustrates the effect of Table 8‑11, for HM7.0 and the proposal, in terms of the QP mapping from input QP (qPI) to output QP (QPC). The proposed scheme extends the chroma QP range to 51 with a slope of 1 at high QPs.

## Slide 5: Quantization Step-size ratio between input QP (qPI) and output QP (QPC)
The above graph illustrates the effect of Table 8‑11, for HM7.0 and the proposal, in terms of the ratio of quantization step-sizes represented by input QP (qPI) and output QP (QPC) as we vary the input QP (qPI). The ratio increases exponentially for HM7.0 while the ratio saturates at 2 for the proposed scheme.

## Slide 6: Advantages
Enables the use of higher chroma QP values
  Maximum possible QP for chroma is now 51 instead of 39
Mapping can be implemented with simple formulas/logic
Maximum default ratio reduced from 4 to 2
  Ratio between luma and chroma step sizes for default offsets
A slope of 1 is enabled at high QPs
A fixed offset of 6 enables equal step sizes for luma and chroma at high QPs
Offsets needed are much smaller
  To achieve a desired relative relationship between the quantization step size for luma and chroma

## Slide 7: Experimental results
No significant impact under common conditions
  Most changes are for QP values outside the range used in the common conditions
  See slides with additional information at the end
High QP values (40, 43, 46 and 49)
  Gain in luma with a loss in chroma
  Gain in luma is better than just offsetting the loss in chroma
  Sample results in next slide
    More results at the end

## Slide 8: Sample results for High QPs
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -3.2% | 27.2% | 24.5% | -2.9% | 25.5% | 23.2%
Class B | -4.3% | 24.4% | 25.2% | -4.2% | 22.3% | 24.8%
Class C | -6.3% | 23.2% | 24.2% | -6.0% | 22.6% | 24.0%
Class D | -5.0% | 22.2% | 22.4% | -5.0% | 21.8% | 23.4%
Class E |  |  |  |  |  | 
Overall | -4.7% -4.7% | 24.3% 23.3% | 24.1% 23.1% | -4.5% -4.5% | 23.0% 22.1% | 23.9% 22.7%
Class F | -4.5% | 17.9% | 17.8% | -3.9% | 15.6% | 15.3%
Enc Time [%] Dec Time [%] | 99% 100% |  |  | 101% 105% |  | 
BD bit-rate comparison of proposal with HM7.0 for high QPs (40, 43, 46 and 49)

## Slide 9: Slice-level chroma QP offsets
Enable the encoder with a greater ability to precisely control the chroma QP
When unused, slice-level syntax overhead should be avoided
Proposal
  slicelevel_chroma_qp_flag in PPS
    controls the signaling of slice-level chroma QP offsets
  Slice-level offsets are applied in the same manner as the PPS-level offsets (shown below)
qPICb = Clip3( −QpBdOffsetC, 57, QPY + cb_qp_offset + slice_qp_delta_cb) (8‑255)
qPICr = Clip3( −QpBdOffsetC, 57, QPY + cr_qp_offset + slice_qp_delta_cr) (8‑256)

## Slide 10: Limits for chroma QP offsets
AVC limits the value of chroma QP offsets to [−12, +12]
Similar range limits are useful for HEVC to simplify decoding
  HM software imposes the range limit from AVC
  WD text does not express any range limit
Proposal
  Adopt the range limit from AVC
    Impose the range limit on cb_qp_offset and cr_qp_offset
  If slice-level chroma QP offsets are supported, impose the range limit on the following also:
    slice_qp_delta_cb
    slice_qp_delta_cr
    (cb_qp_offset + slice_qp_delta_cb)
    (cr_qp_offset + slice_qp_delta_cr)

## Slide 11: Conclusion
We recommend that JCT-VC make the following modifications to current HEVC design:
  Extend the QP range for chroma
  Support slice-level QP offsets
  Place range limits for chroma QP offsets

## Slide 12: Additional Info: Experimental results
 | All Intra Main |  |  | Low delay B Main |  | 
 | Y | U | V | Y | U | V
Class A | -2.7% | 19.1% | 18.3% |  |  | 
Class B | -3.5% | 16.5% | 17.3% | -3.7% | 34.1% | 37.2%
Class C | -4.8% | 15.1% | 15.1% | -6.3% | 29.1% | 29.7%
Class D | -4.6% | 13.6% | 14.5% | -4.9% | 27.0% | 26.4%
Class E | -2.6% | 13.4% | 15.3% | -2.2% | 17.9% | 22.8%
Overall | -3.7% -3.7% | 15.7% 12.2% | 16.2% 12.2% | -4.4% -4.4% | 28.0% 27.8% | 29.9% 30.3%
Class F | -3.3% | 12.9% | 13.8% | -4.9% | 23.5% | 22.9%
Enc Time [%] Dec Time [%] | 101% 102% |  |  | 100% 99% |  | 
BD bit-rate comparison of proposal with HM7.0 for high QPs (40, 43, 46 and 49)

## Slide 13: Additional Info: Experimental results (cont.)
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.02% | 0.33% | 0.34% | -0.04% | 0.25% | 0.24%
Class B | -0.04% | 0.33% | 0.26% | -0.04% | 0.39% | 0.31%
Class C | -0.07% | 0.38% | 0.41% | -0.05% | 0.39% | 0.47%
Class D | -0.06% | 0.37% | 0.44% | -0.07% | 0.34% | 0.39%
Class E |  |  |  |  |  | 
Overall | -0.05% -0.04% | 0.35% 0.27% | 0.36% 0.26% | -0.05% -0.05% | 0.35% 0.26% | 0.35% 0.25%
Class F | -0.05% | 0.19% | 0.23% | -0.04% | 0.24% | 0.27%
Enc Time [%] Dec Time [%] | 100% 101% |  |  | 100% 100% |  | 
BD bit-rate comparison of proposal with HM7.0 for common conditions

## Slide 14: Additional Info: Experimental results (cont.)
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.03% | 0.23% | -0.04% | -0.03% | 0.27% | 0.16%
Class C | -0.04% | 0.38% | 0.42% | -0.08% | 0.26% | 0.52%
Class D | -0.02% | 0.34% | 0.13% | -0.05% | -0.02% | 0.21%
Class E | 0.05% | 0.16% | 0.16% | 0.13% | -0.24% | -0.16%
Overall | -0.01% -0.01% | 0.28% 0.19% | 0.16% 0.10% | -0.02% -0.01% | 0.10% 0.08% | 0.20% 0.11%
Class F | -0.06% | 0.39% | 0.27% | -0.00% | 0.23% | 1.10%
Enc Time [%] Dec Time [%] | 101% 103% |  |  | 101% 101% |  | 
BD bit-rate comparison of proposal with HM7.0 for common conditions