## Slide 1: AHG5, AHG6: Coding of SAO merge left and merge up flags (JCTVC-J0355)
Koohyar Minoo and David Baylon
Motorola Mobility
7/12/12

## Slide 2
7/12/2012
© 2010 Motorola Mobility, Inc.
LCU-level SAO parameter pseudo-syntax
HM 7.0 | JCTVC-J0355
for (cIdx=0; cIdx<3; cIdx++) { merge-Left (ae(v, cIdx)); if(!merge-Left) { Merge-Up(ae(v)); if (!merge-Up) { SAO-On/Off(ae(v)); if (SAO-On) { SAO-Type (ae(v)); if (SAO-Type == BO) sao_band_position(); for (i=0; i<4; i++) sao_offset(ae(v(i))); } // SAO-On } // !merge-Up } // !merge-Left } | merge-Left (ae(v)); if(!merge-Left) { Merge-Up(ae(v)); if (!merge-Up) { for (cIdx=0; cIdx<3; cIdx++) { SAO-On/Off(ae(v)); if (SAO-On) { SAO-Type (ae(v)); if (SAO-Type == BO) sao_band_position(); for (i=0; i<4; i++) sao_offset(ae(v(i))); } // SAO-On } // for(cIdx) } // !merge-Up } // !merge-Left

## Slide 3
7/12/2012
© 2010 Motorola Mobility, Inc.
Coding Order of SAO parameters
SAO Parameters HM7.0 |  |  |  |  | 
Y |  | U |  | V | 
1 | Merge Left | 7 | Merge Left | 13 | Merge Left
2 | Merge Up | 8 | Merge Up | 14 | Merge Up
3 | SAO-On/Off | 9 | SAO-On/Off | 15 | SAO-On/Off
4 | SAO-Type (E0-B0) | 10 | SAO-Type (E0-B0) | 16 | SAO-Type (E0-B0)
5 | sao_bo_position | 11 | sao_bo_position | 17 | sao_bo_position
6 | SAO-Offset X 4 | 12 | SAO-Offset X 4 | 18 | SAO-Offset X 4
SAO Parameters JCTVC-J0355 |  |  |  |  | 
1 | Merge-Left |  |  |  | 
2 | Merge-Up |  |  |  | 
Y |  | U |  | V | 
3 | SAO-On/Off | 7 | SAO-On/Off | 11 | SAO-On/Off
4 | SAO-Type (E0-B0) | 8 | SAO-Type (E0-B0) | 12 | SAO-Type (E0-B0)
5 | sao_bo_position | 9 | sao_bo_position | 13 | sao_bo_position
6 | SAO-Offset X 4 | 10 | SAO-Offset X 4 | 14 | SAO-Offset X 4

## Slide 4
7/12/2012
© 2010 Motorola Mobility, Inc.
Complexity Reductions
HM7.0 uses 3 context model for Merge-Left
JCTVC-J0355 uses 1 context model for Merge-Left
HM7.0 codes 3(per-color) x 2 (merge-Left/Up) bins
JCTVC-J0355 code 2 (merge-Left/Up)
Due to the high spatial-correlation of the SAO parameters, it was observed that most of the time, the merge flag is the only SAO parameter syntax which is signaled. AHG5 data affirms this observation.

## Slide 5
7/12/2012
© 2010 Motorola Mobility, Inc.
AHG5 statistics on Context-coded bin savings
JCTVC-J0355 compared to HM7.0
(Informative) Bins relative to total bins |  |  |  |  | 
 | SAO |  |  |  | 
 | Bins relative to total bins |  |  |  | Delta rates %
 | Reference |  | Tested |  | 
 | ctx | bp | ctx | bp | 
AI Main | 1.06% | 0.14% | 0.76% | 0.14% | -5.55%
RA Main | 3.57% | 0.18% | 1.21% | 0.17% | -20.25%
LB Main | 3.76% | 0.36% | 1.28% | 0.33% | -18.78%
LP Main | 4.10% | 0.23% | 1.53% | 0.22% | -19.98%
Average | 3.12% | 0.23% | 1.19% | 0.21% | -16.14%
 | SAO |  |  |  | 
 | Bins relative to total bins |  |  |  | Delta rates %
 | Reference |  | Tested |  | 
 | ctx | bp | ctx | bp | 
AI HE10 | 0.80% | 0.05% | 0.43% | 0.05% | -12.43%
RA HE10 | 2.50% | 0.06% | 0.66% | 0.05% | -28.56%
LB HE10 | 2.96% | 0.08% | 0.68% | 0.07% | -31.51%
LP HE10 | 3.03% | 0.06% | 0.76% | 0.06% | -30.28%
Average | 2.32% | 0.06% | 0.63% | 0.06% | -25.69%
(Informative) Bins relative to reference |  |  |  | 
 | Total |  | SAO | 
 | ctx | bp | ctx | bp
AI Main | 99.70% | 100.00% | 78.63% | 102.33%
RA Main | 97.60% | 99.98% | 38.75% | 95.30%
LB Main | 97.49% | 99.97% | 43.35% | 93.04%
LP Main | 97.34% | 99.86% | 47.91% | 95.66%
Average | 98.03% | 99.95% | 52.16% | 96.58%
 | Total |  | SAO | 
 | ctx | bp | ctx | bp
AI HE10 | 99.64% | 100.00% | 61.73% | 90.93%
RA HE10 | 98.15% | 99.99% | 29.15% | 88.91%
LB HE10 | 97.68% | 100.02% | 31.42% | 88.28%
LP HE10 | 97.72% | 99.99% | 34.28% | #DIV/0!
Average | 98.30% | 100.00% | 39.14% | #DIV/0!

## Slide 6
7/12/2012
© 2010 Motorola Mobility, Inc.
Simulation Results and BDR gains
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | 0.2% | 0.2% | 0.0% | 0.2% | 0.2%
Class B | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% | 0.3%
Class C | 0.0% | 0.1% | 0.1% | 0.0% | 0.3% | 0.3%
Class D | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.1%
Class E | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.1%
Overall | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% | 0.2%
 | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% | 0.2%
Class F | 0.0% | 0.3% | 0.2% | 0.0% | 0.4% | 0.4%
Enc Time[%] | 106% |  |  | 104% |  | 
Dec Time[%] | 115% |  |  | 122% |  | 
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.1% | -0.2% | -0.1% | -0.1% | 0.3% | 0.3%
Class B | -0.1% | -0.1% | -0.2% | -0.1% | 0.1% | 0.1%
Class C | -0.2% | -0.1% | -0.2% | -0.2% | 0.0% | 0.1%
Class D | -0.4% | -0.2% | -0.2% | -0.3% | -0.1% | -0.2%
Class E |  |  |  |  |  | 
Overall | -0.2% | -0.1% | -0.2% | -0.2% | 0.1% | 0.1%
 | -0.2% | -0.1% | -0.1% | -0.2% | 0.1% | 0.1%
Class F | -0.2% | 0.1% | 0.0% | -0.2% | 0.1% | 0.2%
Enc Time[%] | 83% |  |  | 84% |  | 
Dec Time[%] | 164% |  |  | 134% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.1% | -0.2% | -0.5% | -0.1% | 0.1% | 0.2%
Class C | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | 0.3%
Class D | -0.3% | -0.3% | 0.8% | -0.3% | 0.5% | 0.2%
Class E | -0.3% | -1.3% | -1.7% | -0.3% | -1.2% | -0.6%
Overall | -0.2% | -0.4% | -0.3% | -0.2% | -0.1% | 0.1%
 | -0.2% | -0.4% | -0.3% | -0.2% | 0.0% | 0.2%
Class F | -0.4% | -0.7% | -0.3% | -0.1% | 0.5% | 0.5%
Enc Time[%] | 81% |  |  | 81% |  | 
Dec Time[%] | 127% |  |  | 138% |  | 
 | Low delay P Main |  |  | Low delay P HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.4% | -0.4% | -0.6% | -0.2% | 0.0% | -0.2%
Class C | -0.2% | -0.3% | -0.3% | -0.1% | 0.0% | 0.3%
Class D | -0.3% | -0.1% | 0.4% | -0.3% | 0.0% | -0.5%
Class E | -0.5% | -2.1% | -2.0% | -0.4% | -0.4% | -0.1%
Overall | -0.3% | -0.6% | -0.6% | -0.2% | -0.1% | -0.1%
 | -0.3% | -0.6% | -0.6% | -0.2% | 0.0% | 0.0%
Class F | -0.5% | -0.8% | -0.4% | -0.2% | 0.2% | 0.1%
Enc Time[%] | 88% |  |  | 90% |  | 
Dec Time[%] | 90% |  |  | 102% |  | 
Note: Encoder and Decoder Times are not reliable since a random mix of machines were used to generate the results.

## Slide 7
7/12/2012
© 2010 Motorola Mobility, Inc.
Summary for BOG on SAO
 | HM 7.0 |  |  |  | JCTVC-J0355 |  |  |  | bin saving |  | 
 | 8 bits | 9 bits | 10+ bits | ctx/bp | 8 bits | 9 bits | 10+ bits | ctx/bp | 8 bits | 9 bits | 10+ bits
Merge Left | 3 | 3 | 3 | ctx | 1 | 1 | 1 | ctx | 66.7% | 66.7% | 66.7%
Merge Up | 3 | 3 | 3 | ctx | 1 | 1 | 1 | ctx | 66.7% | 66.7% | 66.7%
SAO-On/Off | 3 | 3 | 3 | ctx | 3 | 3 | 3 | ctx | 0.0% | 0.0% | 0.0%
SAO-Type (E0-B0) | 15 | 15 | 15 | ctx | 15 | 15 | 15 | ctx | 0.0% | 0.0% | 0.0%
sao_bo_position | 15 | 15 | 15 | bp | 15 | 15 | 15 | bp | 0.0% | 0.0% | 0.0%
SAO-Offset_abs X 4 | 96 | 192 | 384 | ctx | 96 | 192 | 384 | ctx | 0.0% | 0.0% | 0.0%
SAO-Offset_sign X 4 | 12 | 12 | 12 | bp | 12 | 12 | 12 | bp | 0.0% | 0.0% | 0.0%
worst case contxt bins | 120 | 216 | 408 |  | 116 | 212 | 404 |  | 3.3% | 1.9% | 1.0%
worst case all bins | 147 | 243 | 435 |  | 143 | 239 | 431 |  | 2.7% | 1.6% | 0.9%
Number of context models:
HM7.0 : 8 context model JCTVC-J0355 : 6 context model
Worst case coded-bins:
Software changes:
1- removal of color dependent context model for merge left
2- encoder side modification to perform RD based on new signaling
Text changes: 6 syntax lines and 3 tables.
 | Main |  |  | He10 |  | 
 | BDR-average | Max-Loss | Max-Gain | BDR-average | Max-Loss | Max-Gain
AI | 0.0% | 0.10% | 0.00% | 0.0% | 0.00% | 0.10%
RA | -0.2% | 0.00% | 0.60% | -0.2% | Always gain | 0.50%
LD | -0.2% | 0.00% | 0.70% | -0.2% | 0.00% | 0.50%
LP | -0.3% | Always gain | 0.80% | -0.2% | 0.10% | 0.40%

## Slide 8
7/12/2012
© 2010 Motorola Mobility, Inc.
JCTVC-J0355: Summary and highlights
context model reduction for Merge-Left (from 3 to 1)
reduction in bins for Merge-Left/Up (from 3 to 1)
reduction in context-entropy-coded bins for all SAO syntaxes (by 48% to 61%)
coding efficiency improvement (about 0.2%)
proposed last meeting (JCTVC-I0507)
small changes to current text and software
       recommend for adoption