## Slide 1: JCTVC-J0435: Lossless Coding and Loop Filter Control for Transform Skip
Geert Van der Auwera, Rajan Joshi, Vadim Seregin, Marta Karczewicz

## Slide 2: Proposal A: Lossless Coding Via Transform Skipping & QP=4
It is proposed to define a “slice_transquant_bypass_flag” and signal it in the slice header.
If the slice_transquant_bypass_flag value is equal to 1, then within the slice, all loop filters (deblocking, SAO, ALF) are bypassed on samples of the 4x4 TUs with transform_skip_flag equal to 1 within the quantization group that has QPY value equal to 4. In addition, if slice_transquant_bypass_flag is equal to 1, then cu_delta_qp shall be signalled at the beginning of the CU or minimum CU quantization group size.

## Slide 3: Proposal A: Lossless Coding Via Transform Skipping & QP=4
Problem: signalling of transform_skip_flag cannot be guaranteed
Prop. A.1: If the slice_transquant_bypass_flag is equal to 1 and if QPY value is equal to 4, then the signaling of the transform_skip_flag for 4x4 TUs is enforced even if the coded block flag is equal to 0. The syntax changes are specified in Section 4.1.
Prop. A.2: If the slice_transquant_bypass_flag is equal to 1, it is enforced that only 4x4 TUs are allowed within a CU (or minimum CU quantization group) that has QPY value equal to 4 and that the transform_skip_flag value of each 4x4 TU shall be equal to 1. If the transform_skip_flag is not present (cbf = 0), then transform_skip_flag value is inferred equal to 1. No syntax table changes are required.
A.2 is recommended (less syntax change) if QP=4 is preferred for lossless coding together with transform skipping

## Slide 4: Proposal B: Unification of “TransQuantBypass” Lossless Coding and Transform Skipping
Proposed to signal “transform_skip_lossless_flag” for a CU (or group of coding units or linked with allowed IPCM block sizes). cu_transquant_bypass_flag may be reused
If the transform_skip_lossless_flag (cu_transquant_bypass_flag) is equal to 1 for a coding unit, the steps of quantization, sign hiding and loop filtering (deblocking, SAO, ALF) are bypassed in addition to the transform for the 4x4 intra (or potentially inter TUs) with transform_skip_flag equal to 1
Similar to proposal A, signalling of transform_skip_flag is not guaranteed, therefore, approach similar to A.2 is also recommended

## Slide 5
ts_lossless = 0
ts_lossless = 0
ts_lossless = 1
ts_lossless = 0
ts_lossless = 0
ts_lossless = 1
ts_lossless = 0
ts_lossless = 1
ts_lossless = 1
ts_lossless = 0
CU
Minimum CU group size for signalling ts_lossless
Lossless region consisting of 4x4 TUs with ts_flag = 1