## Slide 1: JCTVC-J0559 AHG6: Report of ALF viewing results
T. Yamakage
Notes: <number>

## Slide 2: Viewing Conditions
Date and time: 12 July 2012, 16:40 – 20:40
Place: Room 359
Viewers: 17
Sequences:
  Common test condition sequences (Classes A, B and E)
  Some KTA sequences (see next slide)
Coding conditions:
  Random Access and Low Delay B, Qp = 32, 37
Viewing equipment:
  Monitor: Samsung LE46B65
  PC: Intel i7 2.67GHz, raid of 4 hard drives 8TB total and 8GB RAM, running on Windows 7
Randomized viewing order
5-grade scale
  -2: A is worse, -1: A is slightly worse, 0: Equal, 1: A is slightly better, 2: A is better than B

## Slide 3: File Size Comparison
LDB |  | qp32 |  |  |  | qp37 |  |  | 
 |  | Num | off | on | ratio | Num | off | on | ratio
1280x720 | FourPeople_1280x720_60 | 25 | 551,887 | 552,882 | 100.2% | 1 | 298,336 | 296,505 | 99.4%
 | Johnny_1280x720_60 | 26 | 253,413 | 251,790 | 99.4% | 2 | 143,414 | 141,000 | 98.3%
 | KristenAndSara_1280x720_60 | 27 | 414,424 | 412,864 | 99.6% | 3 | 224,866 | 222,530 | 99.0%
 | Night_1280x720_60 | N/A |  |  |  | 4 | 963,710 | 962,222 | 99.8%
 | Spincalendar_1280x720_60 |  |  |  |  | 5 | 447,210 | 448,056 | 100.2%
1920x1080 | Kimono_1920x1080_24 | 28 | 1,444,580 | 1,442,576 | 99.9% | 6 | 710,779 | 710,133 | 99.9%
 | ParkScene_1920x1080_24 | 29 | 1,670,513 | 1,676,764 | 100.4% | 7 | 727,469 | 727,007 | 99.9%
 | Cactus_1920_1080_50 | 30 | 3,224,875 | 3,235,586 | 100.3% | 8 | 1,600,904 | 1,602,967 | 100.1%
 | BasketballDrive_1920x1080_50 | 31 | 3,906,790 | 3,889,875 | 99.6% | 9 | 1,993,294 | 1,988,326 | 99.8%
 | BQTerrace_1920x1080_60 | 32 | 2,493,573 | 2,446,483 | 98.1% | 10 | 974,869 | 960,455 | 98.5%
 | riverbed_1920x1080_60 | N/A |  |  |  | 11 | 3,577,413 | 3,575,548 | 99.9%
 | walking_couple_1920x1080_60 |  |  |  |  | 12 | 1,287,668 | 1,287,664 | 100.0%
RA |  | qp32 |  |  |  | qp37 |  |  | 
 |  | Num | off | on | ratio | Num | off | on | ratio
2560x1600 | Traffic_2560x1600_30 | 33 | 1,595,806 | 1,593,188 | 99.8% | 13 | 830,475 | 830,115 | 100.0%
 | PeopleOnStreet_2560x1600_30 | 34 | 5,164,635 | 5,151,451 | 99.7% | 14 | 2,894,209 | 2,888,553 | 99.8%
 | NebutaFestival_2560x1600_60 | 35 | 18,256,897 | 18,102,075 | 99.2% | 15 | 4,466,743 | 4,434,852 | 99.3%
 | SteamLocomotiveTrain_2560x1600_60 | 36 | 1,534,241 | 1,536,081 | 100.1% | 16 | 746,676 | 745,426 | 99.8%
1920x1080 | Kimono_1920x1080_24 | 37 | 1,344,999 | 1,345,451 | 100.0% | 17 | 685,671 | 683,116 | 99.6%
 | ParkScene_1920x1080_24 | 38 | 1,931,871 | 1,933,571 | 100.1% | 18 | 905,715 | 905,120 | 99.9%
 | Cactus_1920_1080_50 | 39 | 3,357,272 | 3,362,676 | 100.2% | 19 | 1,730,277 | 1,730,500 | 100.0%
 | BasketballDrive_1920x1080_50 | 40 | 3,539,540 | 3,555,641 | 100.5% | 20 | 1,859,629 | 1,868,086 | 100.5%
 | BQTerrace_1920x1080_60 | 41 | 2,830,554 | 2,811,240 | 99.3% | 21 | 1,234,122 | 1,225,264 | 99.3%
 | riverbed_1920x1080_60 | N/A |  |  |  | 22 | 2,906,303 | 2,910,976 | 100.2%
 | walking_couple_1920x1080_60 |  |  |  |  | 23 | 1,151,447 | 1,150,553 | 99.9%
 | rush_hour_1920x1080_60 |  |  |  |  | 24 | 894,773 | 893,122 | 99.8%
Total bitstream size of ALF on is 99.7% of Main profile.

## Slide 4: Viewing Results
Number corresponds to sequence name. 42 is average.
Bars are 95% Confidence Interval.