## Slide 1: JCT-VC K0031: Description of scalable video coding technology proposal by Sharp (proposal 1)
Kiran Misra, Jie Zhao, Seung-Hwan Kim, Sachin Deshpande, Andrew Segall
Presenter: Andrew Segall

## Slide 2: Outline
Introduction
Algorithms
  Motion data:
    Merge process
    Motion vector prediction
  Pixel data:
    Up-sampling of base layer picture for reference
    High frequency prediction in pixel difference domain
  CABAC Initialization
Compression Performance
Summary

## Slide 3: Introduction
Idea:
  Use correlated pixel and motion data in base layer for enhancement layer prediction and coding
  Extend existing tools – merge process, motion vector prediction, difference coding mode for intra/inter prediction
No ALF, No IBDI

## Slide 4: Introduction - Architecture
Modified blocks labeled in red
All remaining blocks are same as base layer

## Slide 5: Inter-frame prediction structure
Use of up-sampled base layer picture for inter-prediction

## Slide 6: Motion data: Mapping base layer data
(X_EL, Y_EL) maps to (X_BL = X_EL/ScaleX, Y_BL = Y_EL/ScaleY).
Establishing a correspondence between (CTU_BL, PU_BL) and (CTU_EL, PU_EL)

## Slide 7: Motion data: Skip/Merge - Merge list modification
Scaled base layer motion vector and enhancement picture co-located with base layer reference is added as a candidate
Each merge candidate carries an up-sampler index
Use uncompressed motion data
Temporal merge list candidate is not allowed to reference co-located up-sampled base layer picture
Add candidates with different up-sampler index if space available

## Slide 8: Motion data: Motion vector prediction
Scale base layer motion vector and use as primary predictor
If pointing to up-sampled base layer picture infer zero motion vector
Replace AMVP candidates pointing to up-sampled base layer picture
Signal up-sampler index when in difference coding mode or when referencing up-sampled base layer picture

## Slide 9: Pixel data: Up-sampling base layer picture
DCTIF based up-sampler
  2x : Same tap values as base layer (HEVC)
  1.5x :
2-D smoothing filter
Luma:
h0 = { 0, 0, 0, 0, 64, 0, 0, 0 } h1 = { -1, 5, -12, 52, 26, -9, 4, -1 } h2 = { -1, 4, -9, 26, 52, -12, 5, -1 } v0 = { 0, 0, 0, 0, 64, 0, 0, 0 } v1 = { -1, 5, -12, 52, 26, -9, 4, -1 } v2 = { -1, 4, -9, 26, 52, -12, 5, -1 }
Chroma:
h0 = { 0, 0, 64, 0 } h1 = { -7, 51, 25, -5 } h2 = { -5, 25, 51, -7 } v0 = { 0, 0, 64, 0 } v1 = { -7, 51, 25, -5 } v2 = { -5, 25, 51, -7 }

## Slide 10: Pixel data: Adaptive up-sampling
An up-sampler is chosen from multiple up-samplers if:
  In Difference Coding Mode, or
  In Pixel Coding Mode and co-located base layer picture is used for reference
prediction_unit( x0, y0, nPbW, nPbH ) { | Descriptor
if( skip_flag[ x0 ][ y0 ] ) { | 
if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} else { /* MODE_INTER */ | 
… | 
if( inter_pred_idc[ x0 ][ y0 ] != Pred_L1 ) { | 
if( num_ref_idx_l0_active_minus1 > 0 ) | 
ref_idx_l0[ x0 ][ y0 ] | ae(v)
if( diff_coding_flag ¦¦ ColocatedBLPic( 0 , ref_idx_l0[ x0 ][ y0 ] ) ) | 
upsampler_idx_l0[ x0 ][ y0 ] | ae(v)
... | 
} | 
if( inter_pred_idc[ x0 ][ y0 ] != Pred_L0 ) { | 
if( num_ref_idx_l1_active_minus1 > 0 ) | 
ref_idx_l1[ x0 ][ y0 ] | ae(v)
if( diff_coding_flag ¦¦ ColocatedBLPic( 1 , ref_idx_l1[ x0 ][ y0 ] ) ) | 
upsampler_idx_l1[ x0 ][ y0 ] | ae(v)
... | 
} | 
} | 

## Slide 11: Pixel data: Inter prediction difference coding mode
Prediction is done in pixel difference domain relative to the base layer
The motion search and motion interpolation process is the same as pixel coding mode (PxCM)
The predictor in difference coding mode (DCM) is based on the difference of reference enhancement layer decoded pixel data and co-located reference base layer decoded pixel data
The current base layer decoded pixel data is up-sampled and added back during reconstruction

## Slide 12: Pixel data: Intra prediction difference coding mode
Similar to inter-prediction:
The secondary predictor is based on the difference of decoded neighboring enhancement layer sample values (to be used as reference) and co-located decoded neighboring base layer sample values.
Once the secondary predictor is determined the current decoded base layer sample values which form the primary predictor are added back during reconstruction.

## Slide 13: CABAC Initialization
Enhancement Layer Slice Type | Use BaseLayer Frame for Reference | cabac_init_flag | Selected Table
I_SLICE | - | - | As in HEVC
P/B_SLICE | Y | - | Enh0
P_SLICE | N | 0/1 | Enh 1/2
B_SLICE | N | 0/1 | Enh 2/1
Different CABAC initialization values for enhancement layer
Re-define the semantics for cabac_init_flag

## Slide 14: Compression Performance versus simulcast anchors
EL-only actual rate:
RA HEVC 2x -30.4%(Y) -18.4%(U) -18.1%(V)
RA HEVC 1.5x -47.8%(Y) -41.0%(U) -40.1%(V)
EL-only target rate:
RA HEVC 2x -28.4%(Y) -16.0%(U) -15.7%(V)
RA HEVC 1.5x -45.8%(Y) -38.7%(U) -37.8%(V)
EL+BL actual rate:
RA HEVC 2x -20.5%(Y) -10.2%(U) -9.9%(V)
RA HEVC 1.5x -28.4%(Y) -22.0%(U) -21.3%(V)
EL+BL target rate:
RA HEVC 2x -19.0%(Y) -8.5%(U) -8.2%(V)
RA HEVC 1.5x -27.0%(Y) -20.5%(U) -19.8%(V)
Based on EL only actual rate, BD bitrate improvement of 30.4% and 47.8% for 2x and 1.5x configurations, respectively are observed. Larger improvements for Class A+ sequences in the 2x scenario.

## Slide 15: Supplemental Information
EL-only actual rate:
RA HEVC 2x -33.7%(Y) -27.0%(U) -27.6%(V)
RA HEVC 1.5x -50.5%(Y) -48.3%(U) -47.5%(V)
EL-only target rate:
RA HEVC 2x -33.3%(Y) -26.6%(U) -27.2%(V)
RA HEVC 1.5x -49.8%(Y) -47.6%(U) -46.8%(V)
EL+BL actual rate:
RA HEVC 2x -23.6%(Y) -17.9%(U) -18.4%(V)
RA HEVC 1.5x -31.2%(Y) -29.1.0%(U) -28.4%(V)
EL+BL target rate:
RA HEVC 2x -23.3%(Y) -17.6%(U) -18.1%(V)
RA HEVC 1.5x -30.8%(Y) -28.6%(U) -27.9%(V)
Enabling IBDI and ALF in enhancement layer results in an average Y BD rate improvement of 3.1% to 4.9% for 2x; and 2.7% to 4% for 1.5x

## Slide 16: Summary
The Sharp response to the CfP on scalable video coding extension for HEVC has been described
Proposed design extends existing techniques
Average object gains of:
  EL only Actual Rate: 30.4% and 47.8% for 2x and 1.5x
  EL only Target Rate: 28.4% and 45.8% for 2x and 1.5x