## Slide 1: Scalable video coding technology proposal by SHARP (proposal 2)
10 Oct. 2012
Tomoyuki Yamamoto, Yukinobu Yasugi Hisao Kumai, Maki Takahashi
SHARP Corporation
JCTVC-K0032:

## Slide 2: Overall summary
SHARP codec (proposal 2)
  Only base layer reconsted pixel values are used for inter-layer information
   Coding tools in EL is independent of BL codec
  Main coding tools
  Inter-layer texture prediction
  Hybrid intra and inter-layer prediction
  Adaptive filter prior to inter-layer prediction
  Performance (luma bd-rate)
    HEVC 2x -- RA: 34.1%, AI: 26.5%
    HEVC 1.5x -- RA: 53.7%, AI: 44.3%
    Hybrid 2x -- RA: 23.0% (vs HEVC), 49.4% (vs AVC)
    Hybrid 1.5x -- RA: 37.3% (vs HEVC), 61.9% (vs AVC)

## Slide 3: Decoder structure
Up-sample
Adaptive Filter
Base decode
Intra Pred.
Inter Pred.
Inter-layer Texture Pred.
Hybrid Intra & Inter-layer Pred.
Picture Buffer
Loop Filter
Syntax Parse
+
Inv. Quant. & Transform
Enh. layer bitstream
Base layer bitstream
Enh. layer recon.
Base layer recon.
Base layer reference picture
Pred. info
Pred. image
Reference picture
Up-sampled base layer recon.

## Slide 4: Up-sampling
Separable FIR filter
  Luma
    1/2: {-1, 4, -11, 40, 40, -11, 4, -1}
    1/4 : {-1, 4, -9, 26, 52,-12,5,-1}
  Chroma
    1/2 : {-4,36,36,-4}
    1/4 : {-5,25,51,-7}

## Slide 5: Adaptive filter
Adaptive filter is applied to up-sampled base-layer reconstruction prior to inter-layer texture prediction
Filter on/off signaling
  Quad-tree structure
    Max depth is 3
Filter Shape
  5x5 square
Filter coeff. signaling
  One filter per picture per color component
  12 coefficients per filter
a
b
c
d
e
f
g
h
i
j
k
l
x
l
k
j
i
h
g
f
e
d
c
b
a

## Slide 6: Inter-layer prediction
Two additional prediction using inter-layer reference
  (1) Inter-layer texture prediction (ILTP)
  - simply use collocated base-layer reference
  (2) Hybrid intra and inter-layer prediction (HIILP)
  - HEVC intra pred. is adjusted using base-layer reference
  Mode signaling
    CU level flag (inter_layer_pred_flag) … CABAC with single context
inter_layer_pred_flag | IntraPredMode | Associated prediction mode
0 | 0 | Planar
0 | 1 | DC
0 | 2..34 | Angular
1 | 1 | ILTP
1 | 0, 2..34 | HIILP

## Slide 7: Hybrid Intra and Inter-Layer Prediction
Hybrid Intra & Inter-layer Pred.
divided into 4x4 unit
extract DC for each 4x4 unit
divided into 4x4 unit
extract DC for each 4x4 unit
－
+
+
＋
Intra pred.
Inter-layer ref. pic.
＋
＋
Replace DC component of intra pred. to that of base picture for each 4x4 unit

## Slide 8: Other configuration
Lambda value
  B Slice lambda value in HM-6.1 is applied even for I Slice
Adaptive Filter coeff and on/off decision
  1. calculate filter coeff using all pixel values
  2. decide quad-tree devision and on/off based on SAD
  3. re-calculate filter coeff using pixels in “on” regions
Intra prediction mode decision
  Simply test additional modes … about 2x modes tested
ALF and AMP in EL

## Slide 9: Coding efficiency
 | Random Access HEVC 2x |  |  | Random Access HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | -28.8% | -16.4% | -16.4% |  |  | 
Class B | -24.2% | -15.7% | -13.2% | -44.3% | -36.8% | -34.2%
Overall | -26.5% | -16.0% | -14.8% | -44.3% | -36.8% | -34.2%
 | -26.5% | -16.2% | -14.9% | -44.5% | -36.9% | -34.5%
 | Random Access HEVC 2x |  |  | Random Access HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | -18.8% | -8.4% | -8.4% |  |  | 
Class B | -15.8% | -8.5% | -6.3% | -25.4% | -19.0% | -16.9%
Overall | -17.3% | -8.4% | -7.3% | -25.4% | -19.0% | -16.9%
 | -17.3% | -8.5% | -7.4% | -25.4% | -19.0% | -16.9%
HEVC 2x/1.5x, RA
HEVC 2x/1.5x, AI
 | All Intra HEVC 2x |  |  | All Intra HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | -37.5% | -31.2% | -32.5% |  |  | 
Class B | -30.7% | -23.2% | -23.7% | -53.7% | -49.8% | -50.5%
Overall | -34.1% | -27.2% | -28.1% | -53.7% | -49.8% | -50.5%
 | -34.1% | -27.1% | -27.9% | -53.9% | -50.4% | -51.4%
 | All Intra HEVC 2x |  |  | All Intra HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | -25.7% | -20.5% | -21.6% |  |  | 
Class B | -20.9% | -14.5% | -15.0% | -31.8% | -28.5% | -29.2%
Overall | -23.3% | -17.5% | -18.3% | -31.8% | -28.5% | -29.2%
 | -23.3% | -17.4% | -18.2% | -31.8% | -28.6% | -29.4%
EL
EL+BL
EL
EL+BL

## Slide 10: Coding efficiency
Hybrid 2x/1.5x, RA (vs HEVC)
 | Hybrid vs HEVC 2x |  |  | Hybrid vs HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | -25.4% | -13.0% | -13.1% |  |  | 
Class B | -20.6% | -12.3% | -9.7% | -37.3% | -29.0% | -26.0%
Overall | -23.0% | -12.6% | -11.4% | -37.3% | -29.0% | -26.0%
 | -23.0% | -12.7% | -11.5% | -37.4% | -29.2% | -26.3%
 | Hybrid vs AVC 2x |  |  | Hybrid vs AVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | -47.3% | -36.2% | -37.2% |  |  | 
Class B | -51.5% | -47.0% | -45.1% | -62.1% | -58.1% | -56.1%
Overall | -49.4% | -41.5% | -41.2% | -61.9% | -58.0% | -56.0%
 | -49.4% | -41.6% | -41.2% | -62.1% | -58.1% | -56.1%
 | Hybrid vs HEVC 2x |  |  | Hybrid vs HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | -15.5% | -5.4% | -5.5% |  |  | 
Class B | -12.4% | -5.5% | -3.3% | -18.9% | -12.4% | -10.1%
Overall | -13.9% | -5.4% | -4.4% | -18.9% | -12.4% | -10.1%
 | -13.9% | -5.5% | -4.4% | -19.0% | -12.4% | -10.1%
 | Hybrid vs AVC 2x |  |  | Hybrid vs AVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | -33.0% | -22.7% | -23.6% |  |  | 
Class B | -38.7% | -34.1% | -32.4% | -41.3% | -36.9% | -35.0%
Overall | -35.8% | -28.4% | -28.0% | -41.3% | -36.9% | -35.0%
 | -35.9% | -28.4% | -28.0% | -41.3% | -37.0% | -35.0%
Hybrid 2x/1.5x, RA (vs AVC)
EL
EL+BL
EL
EL+BL

## Slide 11: Coding efficiency (Additional results)
MPEG-2 base layer 2x/1.5x (vs HEVC)
 | Hybrid(MPEG2) vs HEVC 2x |  |  | Hybrid(MPEG2) vs HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | -31.9% | -14.5% | -14.3% |  |  | 
Class B | -27.0% | -16.7% | -14.5% | -46.2% | -36.7% | -35.0%
Overall | -29.5% | -15.6% | -14.4% | -46.2% | -36.7% | -35.0%
 | -29.5% | -15.8% | -14.6% | -46.2% | -36.9% | -35.2%
 | Hybrid(MPEG2 interlaced) vs HEVC2x |  |  | Hybrid(MPEG2) vs HEVC 2x |  | 
 | Y | U | V | Y | U | V
Class B (*1) | -10.0% | -3.9% | -3.1% | -23.0% | -12.0% | -10.3%
 | *1: Cactus, BBDrive, BQTerrace |  |  |  |  | 
EL

## Slide 12: Encoding/Decoding time
Encoding time
  Compared proposed (lowest QP) with anchor (QP=22)
    AI: ~ 2.3 times
    RA: ~ 1.6 times
Decoding time
  Compared proposed (lowest QP) with anchor (QP=22)
    AI: ~1.8 times
    RA: ~3.0 times

## Slide 13: Support non-HEVC base layer
Proposed codec only use base-layer reconstruction (no motion/mode information are used)
 capable of supporting any base-layer (decoded) bitstream

## Slide 14: Conclusion
SHARP codec (proposal 2)
  Support non-HEVC base-layer bitstream (AVC, MPEG-2, etc.)
  Main coding tools
  Inter-layer texture prediction
  Hybrid intra and inter-layer prediction
  Adaptive filter prior to inter-layer prediction
  Recommendation
    Consider proposed codec in the development of HEVC scalable extension
    Especially, consider support of non-HEVC base layer