## Slide 1: Scalable video coding technology proposal by Nokia
JCTVC-K0040 / JCTVC-K0047
Oguz Bici, Done Bugdayci, Alireza Aminlou, Antti Hallapuro, Miska Hannuksela, Jani Lainema, Kemal Ugur

## Slide 2: Outline
Goal: Achieve high efficiency scalable video coding with:
  As small changes to HEVC as possible
  As low additional complexity to HEVC as possible
Three main tools:
  Enhancing the intra and motion prediction
    Add a base layer component to enhancement layer prediction
  Block based inter-layer prediction of samples
    Utilize base layer samples as prediction for coding EL samples
  Reuse BL syntax
    Use MV and intra mode from base layer to code enhancement layer
Results (EL bitrate reduction):
  RA: 40.05% (K0047), 38.3% (K0040)
  AI: 44.15%
  SNR (information): 36.4%
Software has been available for interested parties to study.

## Slide 3: Delta-bitrate vs. Decoding time
Chart: Delta bitrate vs. decoding time (AI+RA)
| 2.1800786094266198 | 2.0319984870250876 | 3.3636854574664925 | 1.6136254754387331 | 1.7695090092704571 | 1.461860813928912 | 1.41403201091777 | 1.6075591079302096 | 1.8785110672418681 | 5.6727104257435226 | 5.9636171741338426 | 2.2027081239379034 | 1.5491505423417413 | 1.6061357128510838 | 1.6647065640272238 | 3.755033680048284
Ave(AI, RA) | -0.39654 | -0.45123 | -0.39756 | -0.43847 | -0.45539 | -0.40144 | -0.3306 | -0.41224 | -0.4475 | -0.4269 | -0.43937 | -0.44293 | -0.41723 | -0.42087 | -0.18906 | -0.44192 | -0.20783
Nokia | -0.41224 | -0.42087

## Slide 4: Delta-bitrate vs. Encoding time
Chart: Delta bitrate vs. encoding time (AI+RA)
| 1.4827695527664642 | 2.468927256000728 | 2.1192216122125513 | 2.9360035658428942 | 1.9965925601937804 | 1.1441070956005104 | 1.1006861937459189 | 1.4996680818445738 | 2.4731405999658786 | 2.6048100259406617 | 3.0098685755732655 | 2.3653957675210977 | 1.0878399648995534 | 1.3783152635907423 | 0.89502710156660137
Ave(AI, RA) | -0.39654 | -0.45123 | -0.39756 | -0.43847 | -0.45539 | -0.40144 | -0.3306 | -0.41224 | -0.4475 | -0.4269 | -0.43937 | -0.44293 | -0.41723 | -0.42087 | -0.18906 | -0.44192 | -0.20783
Nokia | -0.41224 | -0.42087

## Slide 5
Enhancing the intra and motion prediction
Add a base layer component to enhancement layer prediction

## Slide 6: Intra prediction enhancement
Enhancement layer intra prediction is enhanced from base layer depending on the EL intra mode

## Slide 7: Intra prediction enhancement
Gradient based enhancement
Used for horizontal and vertical prediction modes
Measures how the base layer pixel values change in the corresponding direction and apply the generated differential values to EL intra prediction
Similar to intra prediction side smoothing process in HEVC

## Slide 8: Intra prediction enhancement
DC correction
Applied for large intra PUs (size 8x8 or larger) that don’t utilize the 0-angle horizontal and vertical modes.
Adds a constant value to each sample of the enhancement layer block so that the DC of the enhancement layer prediction equals to the DC of the co-located base layer block.

## Slide 9: Base-layer enhanced MCP
Perform motion compensation on the base layer with the motion information identical to the enhancement layer.
Full or half of the base layer component can be added to the enhancement layer prediction

## Slide 10
Block based inter-layer prediction of samples
Utilize base layer samples as prediction for coding EL samples

## Slide 11: Block based inter-layer prediction
Reconstructed samples of base layer could be used as prediction for enhancement layer.
  One of the most common tools in other contributions as well.
Intra slices:
  intra_skip_flag: signaled for the largest CU size. If 1, no other syntax is sent and upsampled base layer is copied
  pred_base_flag: Signaled for each PU. If the flag is 1, only upsampled base layer is the prediction and residual is further signaled.
Inter slices:
  pred_base_flag: Only parsed for inter PU.
(a) Example CU in an intra slice
(b) Example CUs in an inter slice

## Slide 12: Block based inter-layer prediction
cbf_luma and cbf_cb
The contexts of cbf_luma and cbf_cb flags depend on the value of pred_base_flag.
no_residual_syntax_flag
To remove redundancy parsing of no_residual_syntax_flag is modified for inter slices.

## Slide 13
Reuse BL syntax
Use MV and intra mode from base layer to code enhancement layer

## Slide 14: Motion from base
Modified AMVP mode
  If available, co-located MV in the base layer (BMVP) is placed as the first candidate in the AMVP list.
  BMVP does not participate in pruning process.
Merge mode
  To get maximal coding efficiency, it is found that both BMVP and TMVP need to be present in the list.
  Candidate list of an EL block is constructed in such a way that BMVP and TMVP are always present if they are both available and the list size is larger than two.
    BMVP is placed in the first position, TMVP the same position as in HEVC. Rest of the positions are filled with spatial candidates.
  A mapping process is defined to map the reference indexes of base layer motion information, as GOP structures could be different for BL and EL.

## Slide 15: Intra prediction mode prediction
Intra mode for EL blocks is coded as follows:
  First bin indicates whether the EL mode equals to corresponding BL mode.
  Second bin is coded if first bin is zero and it indicates the sign of the difference between EL mode and BL mode (coded in bypass mode)
  Third bin indicates whether the absolute value of the difference between EL mode and BL mode is equal to 1 or not.
  Fourth bin indicates whether the absolute value of the difference between EL mode and BL mode is equal to 2 or not.
  Remaining difference are coded with 5 bins in bypass mode.
Benefit of this approach over modifying mpm candidates:
  Less complex (no mpm list needs to be constructed)
  Better coding efficiency

## Slide 16
Other
Upsampling filter
High level syntax
Encoding configurations

## Slide 17: Upsampling filter
2x upsampling:
Same ½ sub-pixel interpolation filter in HEVC
  Luma: [-1, 4, -11, 40, 40, -11, 4, -1]
  Chroma: [-4, 36, 36, -4]
1.5x upsampling:
Obtained from the ½ and ¼ sub-pixel interpolation filters of HEVC.
  Luma: [-1, 4, -11, 52, 25, -7, 2, 0 ]
  Chroma: [-5, 49, 24, -4]
  (2/3 positions use the mirrored coefficients of above)

## Slide 18: High-level syntax
Multi-loop decoding
Picture marking as ”used/unused for inter-layer reference”
Picture removed from DPB when it is
  “unused for reference”,
  “unused for inter-layer reference”, and
  “not needed for output”
Support for uneven GOP lenghts and different decoding orders between layers
Additional compression when EL GOP longer than BL GOP
Smaller DPB memory use when EL GOP shorter than BL GOP

## Slide 19: Example of uneven GOP lengths
B4
B2
B1
B3
B8
B6
B5
B7
...
...
E4
E2
E1
E3
E8
E6
E5
E7
...
...
EL
BL
Output order
Decoding order: ..., B4, B2, B1, B3, B8, E8, E4, E2, E1, E3, B6, E6, B5, E5, B7, E7, ...
Addition memory use: 2 BL pictures in DPB (B1, B3)

## Slide 20: Encoding configurations
JCTVC-K0040 (encoding configuration 1)
  Same prediction structure as base layer (GOP size of 8) is used
JCTVC-K0047 (encoding configuration 2)
EL could use different GOP length:
  For sequences with a dyadic intra period (32,64), GOP length of 32 is chosen.
  For sequences with non-dyadic intra period (24,48), same GOP length as the corresponding intra period is chosen. GOPs are created by concatenating two dyadic hierarchies (i.e. for 24, GOP structure is combination of 16 and 8).

## Slide 21
Conclusions

## Slide 22: Delta-bitrate vs. Encoding time
Chart: Delta bitrate vs. encoding time (AI+RA)
| 1.4827695527664642 | 2.468927256000728 | 2.1192216122125513 | 2.9360035658428942 | 1.9965925601937804 | 1.1441070956005104 | 1.1006861937459189 | 1.4996680818445738 | 2.4731405999658786 | 2.6048100259406617 | 3.0098685755732655 | 2.3653957675210977 | 1.0878399648995534 | 1.3783152635907423 | 0.89502710156660137
Ave(AI, RA) | -0.39654 | -0.45123 | -0.39756 | -0.43847 | -0.45539 | -0.40144 | -0.3306 | -0.41224 | -0.4475 | -0.4269 | -0.43937 | -0.44293 | -0.41723 | -0.42087 | -0.18906 | -0.44192 | -0.20783
Nokia | -0.41224 | -0.42087
Better

## Slide 23: Conclusions
Goal: Achieve high efficiency scalable video coding with:
  As small changes to HEVC as possible
  As low additional complexity to HEVC as possible
Results:
  Proposal with one of the best complexity-coding efficiency tradeoff.
  No unnecessary coding tools, such as adaptive filtering included
    If ALF is used for EL an additional 1.9% gain is possible
  No parsing dependency between enhancement layer and base layer.
  A good point to start the scalable HEVC project:
    Small number of changes to HEVC but still high efficiency
    One of the lowest encoding/decoding complexities