## Slide 1
JCTVC-K0042 & JCTVC-K0043:
Scalable Video Coding Technology Proposal by Fraunhofer HHI
Heiko Schwarz, Christian Bartnik, Philipp Helle, Tobias Hinz, Ali Khairat, Heiner Kirchhoffer, Haricharan Lakshman, Detlev Marpe, Mischa Siekmann, Jan Stegemann, Karsten Sühring, Thomas Wiegand

## Slide 2: System Overview
Enhancement layer
encoder
Downsampler
Base layer
encoder
Inter layer
prediction
Base layer
bitstream
Enhancement layer
bitstream
Multiplexer
Scalable
bitstream
Input
video
Enhancement layer coding
    HEVC with additional tools (mainly inter-layer prediction tools)

## Slide 3: Coding Tools Overview
Inter-layer intra prediction
    (Upsampled) base layer as prediction signal
    (Upsampled) and filtered base layer as prediction signal
    Intra prediction using difference samples
    Weighting of spatial intra prediction and (upsampled) base layer
    Prediction of intra prediction modes
Inter-layer inter prediction
    Inter-layer residual prediction
    Motion-compensation with difference picture
    Inter-layer motion vector prediction (AMVP & Merge)
    Inter-layer motion parameter inference
Transform coefficient coding
    Adaptive scanning pattern in enhancement layer

## Slide 4: Prediction using reconstr. base bayer
reconstructed base
layer picture
(upsampled)
reconstructed base
layer picture
upsampling
current picture / block
prediction signal is directly formed by (upsampled) reconstructed base layer
Mode “BL_RECO_CPY“
    Uses reconstructed base layer as prediction signal
    Signaled at CU level
    Transform coding in the same way as for inter CUs
    Similar to inter-layer intra prediction in SVC
    Multi-loop decoding
Upsampling
    8-tap filters for luma
    2-tap filters for chroma
    1/16 phase shifts

## Slide 5: Prediction using filtered Base Layer
reconstructed base
layer picture
(upsampled)
reconstructed base
layer picture
upsampling
current picture / block
prediction signal is formed by filtering the (upsampled) reconstructed base layer
Mode “BL_RECO_CPY_FILT“
    Similar to “BL_RECO_CPY”
    Additional low-pass filtering of the reconstructed (and upsampled) base layer
    Signaled at CU level
Remarks
    The same smoothing effect can be obtained by using a different (and shorter) upsampling filter
additional low-pass filtering using the [1 2 1] filter

## Slide 6: Intra prediction with difference signal
reconstructed base layer
picture
upsampling
Mode “BL_INTRA_RECO“
    Spatial intra prediction using difference samples
    Add difference prediction to (upsampled) base layer
    Signaled at CU level
    Same intra prediction modes as in single-layer HEVC (same signaling)
final
prediction
current picture
+
+
-
difference signal
spatial intra prediction
using difference samples
+

## Slide 7: Frequency-weighted combined prediction
reconstructed base layer
picture
upsampling
Mode “BL_INTRA_COMB“
    Spatial intra prediction in enhancement layer
    Combined with (upsampled) base layer by frequency-based superposition
    Low frequency components are mainly taken from base layer
    Signaled at CU level
    Same intra prediction mode signaling
final
prediction
current picture
tp = (w1*t1 + w2*t2 + 32) >> 5
with w1/2 = f(x,y)
+
T
T
w1
w2
T-1

## Slide 8: Prediction of Intra Prediction Modes
X
B
A
enhancement
layer
C
co-loacted block
in base layer
Prediction of intra prediction modes
    Include intra prediction mode of co-located base layer block in derivation of most probable modes
    Syntax is not modified
    If C is directional mode and A is no directional mode,
         Replace A with C
    Otherwise, if C is directional mode and B is no directional mode,
         Replace B with C
    Predict as in HEVC

## Slide 9: Inter Residual Prediction Mode
reconstructed base layer
residual
upsampling
Mode “BL_INTER_RESI“
    For CUs coded in inter mode
    Adds (upsampled) reconstructed base layer residual to motion-compensated prediction signal
    Signaled at CU level
    Bi-linear filters for upsampling of both luma and chroma
    Residual clipped to 8 bit
final
prediction
reference picture
+
current picture / block
MCP

## Slide 10: Inter Difference Prediction Mode
rec. BL
upsampling
Mode “BL_INTER_RECO“
    Motion compensation using difference between EL reconstruction and (upsampled) BL
    Add rec. BL for current pic.
    Signaled at CU level
    Bi-linear filters for MCP of both luma and chroma
    Difference clipped to 8 bit
final
prediction
difference picture
+
current picture / block
reference picture
MCP
+
+
-

## Slide 11: Inter-layer Motion Vector Prediction
B
1
B
0
B
2
T
0
T
1
A
1
IL
IL
B
A
T
spatial
temporal
base layer
candidate
list
current
block
A
0
Motion vector prediction (AMVP)
    Use (scaled) motion vector of co-located base layer block as additional predictor
    Insert at first position of the candidate list
    Candidate list is extended by one entry
    Syntax is not changed

## Slide 12: Motion Parameters in Merge Mode
B
C
D
E
T
0
T
1
A
A
…
E
T
IL
spatial
temporal
max. 5
candidate
list
current
block
IL
base layer
Merge Candidate List
    Use (scaled) motion parameters of co-located base layer block as additional candidate
    Insert at first position of the candidate list
    Number of candidates is not increased
    Only added if merge_flag is equal to 0 in base layer
    If base layer merge_flag is equal to 1, the chosen base layer candidate is moved to the first position in the list

## Slide 13: Motion Parameter Inference
Infer all coding parameters for a CU
    Signaled at CU level
    Find co-located motion parameters for each 4x4 sub-block
    Scale motion vectors according to resolution ratio
    Summarize neighboring sub-blocks with the same motion parameters to large CUs and Pus
    Can be used with normal MCP as well as in difference mode
    Intra sub-blocks are predicted using the (upsampled) base layer signal

## Slide 14: Transform Coefficient / Entropy Coding
Additional scans in enhancement layer
    For 16x16 and 32x32 luma TUs
    Scan is signaled if last significant scanning position is outside the top-left 4x4 block
    Two additional scans are provided: horizontal and vertical scan
    Sub-blocks for horizontal and vertical scan are 1x16 and 16x1 samples, respectively
    Context modeling is slightly modified
CABAC initialization
    Different initialization tables for enh. layer

## Slide 15: Deblocking Filter Modifications
Boundary Filter Strength
    Modified for inter-layer intra predicted CUs
    When none of the blocks is “spatial intra-predicted”, but at least one is “inter-layer intra predicted”:
    If one of the blocks has non-zero transform coefficients, the boundary filter strength is set to1
    Otherwise, the boundary filter strength is set to 0

## Slide 16: Upsampling
Summary
    Implemented for arbitrary resolution ratios (1/16 phase)
    8-tap filters for reconstructed luma
    2-tap filters for chroma and residual
    Takes into account standard chroma sample locations (as defined in HEVC draft, subclause 6.1)
Phase offset | Filter coefficients
0/16 | [ 0, 0, 0, 64, 0, 0, 0, 0] / 64
1/16 | [ 0, 1, -3, 63, 4, -2, 1, 0] / 64
2/16 | [ -1, 3, -7, 63, 8, -3, 1, 0] / 64
3/16 | [ -1, 3, -8, 60, 14, -6, 3, -1] / 64
4/16 | [ -1, 4, -10, 57, 19, -7, 3, -1] / 64
5/16 | [ -1, 4, -11, 52, 26, -8, 3, -1] / 64
6/16 | [ -1, 4, -11, 49, 30, -10, 4, -1] / 64
7/16 | [ -1, 4, -11, 45, 34, -10, 4, -1] / 64
8/16 | [ -1, 4, -11, 40, 40, -11, 4, -1] / 64

## Slide 17: Encoder Control / Tool Selection
Coding/Prediction structure
    Same coding/prediction structure as for base layer
    Intra at the same access units
    Same type of random access
    Same QP cascading
Encoder decision algorithm
    Same as in HM, but with additional modes
    Lagrange techniques for mode decision, motion search, quantization
    QP is changed once for hitting the target rates
    Lagrange parameter is dependent on base layer QP
Difference between JCTVC-K0042 and JCTVC-K0043
    JCTVC-K0043 uses ALF (as in HM 6.1) for the enhancement layer

## Slide 18: Results (for all test cases)
 | JCTVC-K0042 |  |  | JCTVC-K0043 |  | 
 | Y | U | V | Y | U | V
All Intra 2.0 | -35.8% | -34.3% | -35.4% | -36.8% | -35.6% | -36.3%
All Intra 1.5 | -54.5% | -53.7% | -54.7% | -55.1% | -54.6% | -55.4%
HEVC Spatial 2.0 | -31.5% | -17.8% | -17.6% | -33.4% | -19.2% | -18.6%
HEVC Spatial 1.5 | -48.9% | -38.5% | -37.9% | -50.4% | -40.1% | -38.9%
HEVC SNR | -39.3% | -24.7% | -22.5% | -41.1% | -25.9% | -23.3%
Hybrid vs HEVC 2.0 | -30.0% | -17.1% | -16.8% | -31.9% | -18.6% | -17.8%
Hybrid vs HEVC 1.5 | -44.9% | -35.1% | -34.0% | -46.7% | -36.7% | -35.2%
Hybrid vs AVC 2.0 | -53.8% | -44.4% | -44.5% | -55.0% | -45.3% | -45.1%
Hybrid vs AVC 1.5 | -66.3% | -61.3% | -59.9% | -67.3% | -62.1% | -60.6%
Bjøntegaard delta rates (averaged over all sequences and test points)

## Slide 19: Summary
Coding Scheme
HEVC extension with additional tools
          Inter-layer intra prediction
          Inter-layer residual prediction
          Inter-layer coding parameter prediction
          Difference coding modes for intra and inter
          Adaptive scans in enhancement layer
Difference between JCTVC-K0042 and JCTVC-K0043
          JCTVC-K0043 includes ALF for the enhancement layer
Software
Extension of HM 6.1
Base layer bitstream can be read in encoder
Includes AVC decoder
Decoder update: Run time is about 1.5-2.5 x single-layer HEVC (RA 2x)