## Slide 1
Samsung and Vidyo response to CfP on Scalable Coding Extensions of HEVC
Jill Boyce (Vidyo)
Ken McCann (Samsung)

## Slide 2
Overview
Inspire the World, Create the Future
1
2
3
4
Introduction
Algorithm Description
Compression Performance
Complexity Analysis
5
Conclusions

## Slide 3
Introduction : Samsung/Vidyo Coding Framework
This presentation covers JCTVC-K0044 and JCT-VC-K0045
The Samsung/Vidyo coding framework provides the ability to trade off complexity and compression efficiency
  Inter-layer and single-layer tools
: low-complexity operating point focused on inter-layer tools,
with good compression efficiency
      Average luma BD-rate gains of 30.3% / 47.1% for RA 2x / 1.5x
      Decoding time about 1.8 relative to anchor
: higher efficiency operating point, with a moderate increase in
complexity
      Average luma BD-rate gains of 34.6% / 50.6% for RA 2x / 1.5x
      Decoding time about 2.9 relative to anchor
K0044
K0045

## Slide 4
Introduction : Key Features
Coding Tools |  |  | Notes
Intra_BL mode | √ | √ | Inter-layer Coding tool
Inter_BL mode | √ | √ | 
Difference mode | √ | √ | 
Inter-layer spatial MPM prediction | √ | √ | 
Inter-layer motion prediction | √ | √ | 
Inter-layer SAO | √ | √ | 
Asymmetric motion partitions in enhancement layer |  | √ | Main Profile Tool (HM8.0)
Bi-directional optical flow |  | √ | Single-layer coding tool
Adaptive loop filter in enhancement layer |  | √ | 
TU-based implicit dQP refinement |  | √ | 
Multi-parameter probability estimation in enhancement layer CABAC |  | √ | 
K0044
K0045

## Slide 5
Description: Units and Up-sampling
CTU/TU/PU
  Similar structure to non-scalable HEVC
  PU is inferred to be 2Nx2N for some CU modes
    Intra_BL
    Inter_BL
Up-sampling filter
  Separable 2D FIR filter: 8 taps for Luma, 4 taps for Chroma
  1/4 phase shift :
    the same DCT-IF as for HEVC motion compensation interpolation
  1/3 phase shift:
    { 1, 4, -11, 52, 26, -8, 3, -1}/64
    { -5, 50, 22,-3 }/64
K0044
K0045

## Slide 6
Inter-Layer Prediction
Prediction of Enhancement Layer (EL) from Base Layer (BL)
  Double loop decoding
  RD-optimized decision in encoder between various possible CU modes for EL
    Intra_BL: BL pixels are scaled to EL CU resolution
    Inter_BL: where BL motion vector is applied to EL
    Pixel Coding: non-scalable coding of EL
    Difference Coding: intra and inter prediction of EL incorporate the coded pixel values of the BL
K0044
K0045

## Slide 7
Proposed Scalable Encoder
K0044
K0045

## Slide 8
EL Intra CU Coding
Intra_BL mode
  BL pixel block scaled to EL resolution and used as predictor for EL CU
  Residual coded by HEVC inter residual coding with prediction set to intra DC mode
  Intra_BL Skip indicates that residual coefficients are zero
Difference Coding mode
  Combines intra prediction and inter-layer prediction
  Spatial intra directional prediction performed using previously coded difference values
  Add current BL pixel block scaled to EL resolution
K0044
K0045

## Slide 9
EL Intra Prediction Module
K0044
K0045

## Slide 10
EL Inter CU Coding
Inter_BL mode
  motion information for each 8x8 block of the CU is derived from corresponding BL block
Difference Coding mode
  Combines inter prediction and inter-layer prediction
  Motion compensated blocks consist of difference values
  Use bi-linear interpolation for sub-pel motion compensation
  Add current BL pixel block scaled to EL resolution
K0044
K0045

## Slide 11
EL Coding Tools
Motion vector prediction when Inter_BL mode not used
  For each PU, motion info from corresponding BL block is added as a candidate MV predictor, to the last position on the list
  BL MV’s stored for 4x4 blocks, EL selects position which corresponds to center of EL PU
Deblocking filter modification
  Additional condition to check for boundary between difference mode and non-difference mode blocks, set to Bs=1
  Setting filter edges for Inter_BL mode are based on 8x8 PU boundaries as well as transform unit boundaries
K0044
K0045

## Slide 12
EL Inter Prediction Module
K0044
K0045

## Slide 13
Inter Layer SAO
Re-use existing module:
  Sample processing part is equal to in-loop SAO in non-scalable HEVC spec.
No additional memory usage:
  Re-use memory buffer reserved for in-loop SAO on EL
Difference:
  EO and BO are both applied
K0044
K0045

## Slide 14
Inter Layer MPM Prediction (HE)
Using high texture similarity between different resolution images.
3-MPMs of EL are set from up-scaled BL picture.
K0044

## Slide 15
Inter Layer MPM Prediction (LC)
The current non-scalable HEVC design’s derivation process for MPMs yields three distinct MPMs
For the EL PU, if the corresponding BL PU is coded in intra mode,
  It is used as the very first MPM
  If the base layer is the same with one of the two target layer MPMs
    the base layer MPM is used as the first
    the different target layer MPM is used as the second
    the last third MPM derivation follows the process which is defined in the current HEVC for the case of two spatial intra modes having different intra prediction modes
  Otherwise if the first two target layer MPMs that is different from the base layer MPM is used as the second and third MPMs, respectively
K0045

## Slide 16
AMP in EL
Only enable it on EL
  AMP is HEVC main profile tool
BL
EL
K0044

## Slide 17
Bi-Directional Optical flow
Pixel-wise compensation without additional syntax considerably increases coding efficiency for B-slices.
K0044

## Slide 18
TU size based implicit dQP refinement
Implicit signaling of dQP based on transform size (TU based dQP)
The static areas have more possibility to be reference rather than moving region.
Relative higher QP is applied for small transform block size.
K0044

## Slide 19
ALF in EL
Enable ALF on EL
  ALF design follows HM 5.0 with minor modification:
  Block based adaptation with directional features classification
    Pixel directional features:
      H(i,j) = | X(i,j)<<1 - X(i,j-1) - X(i,j+1) |
      V(i,j) = | X(i,j)<<1 - X(i-1,j) - X(i+1,j) |
    block-wise features :
      HB = ∑i=1,2 ∑j=1,2 H(i,j)
      VB = ∑i=1,2 ∑j=1,2 V(i,j)
      LB = (HB + VB) >> 2
      1, if VB > 2×HB
      dir = 2, if HB > 2×VB
      0, otherwise
    norMag = max{ 7, LB >> 1 }
  Filter shapes:
    snowflake-5x5
    cross-9x9
 | norMag |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
dir=0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 2
dir=1 | 0 | 3 | 3 | 3 | 3 | 3 | 3 | 4
dir=2 | 0 | 5 | 5 | 5 | 5 | 5 | 5 | 6
Class label CB = classTab [dir][norMag]
K0044

## Slide 20
Multi-parameter probability estimation in EL
Multi-parameter probability estimation for CABAC in enhancement layer used the technique proposed in JCTVC-F254
K0044

## Slide 21
Compression Performance (1) : JCTVC-K0045
Random Access HEVC 2x |  |  | Random Access HEVC 1.5x |  | 
Y | U | V | Y | U | V
-32.7% | -24.3% | -25.3% |  |  | 
-27.1% | -21.0% | -19.4% | -46.9% | -41.4% | -40.3%
-29.9% | -22.7% | -22.4% | -46.9% | -41.4% | -40.3%
 | Random Access HEVC 2x |  |  | Random Access HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | -33.3% | -25.0% | -26.0% |  |  | 
Class B | -27.3% | -21.2% | -19.7% | -47.1% | -47.1% | -40.6%
Overall | -30.3% | -23.1% | -22.8% | -47.1% | -47.1% | -40.6%
<Actual Rate>
<Target Rate>
 | All Intra HEVC 2x |  |  | All Intra HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | -39.1% | -37.2% | -38.0% |  |  | 
Class B | -31.6% | -29.4% | -29.2% | -54.1% | -52.3% | -52.4%
Overall | -35.4% | -33.3% | -33.6% | -54.1% | -52.3% | -52.4%
All Intra HEVC 2x |  |  | All Intra HEVC 1.5x |  | 
Y | U | V | Y | U | V
-39.1% | -37.1% | -37.9% |  |  | 
-31.6% | -29.3% | -29.2% | -54.1% | -52.2% | -52.4%
-35.3% | -33.2% | -33.5% | -54.1% | -52.2% | -52.4%
1. Spatial scalability
2. SNR scalability
 | Actual rate |  |  | Target rate |  | 
 | Y | U | V | Y | U | V
Class A+ | -38.7% | -32.5% | -32.5% | -38.1% | -31.8% | -21.9%
Class B | -35.0% | -27.6% | -24.5% | -34.8% | -27.3% | -24.3%
Overall | -36.8% | -30.0% | -28.5% | -36.4% | -29.6% | -28.1%
 | Hybrid vs HEVC 2x |  |  | Hybrid vs HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | -32.3% | -23.6% | -24.5% |  |  | 
Class B | -25.5% | -19.9% | -17.9% | -43.2% | -38.0% | -36.2%
Overall | -28.9% | -21.7% | -21.2% | -43.2% | -38.0% | -36.2%
Hybrid vs HEVC 2x |  |  | Hybrid vs HEVC 1.5x |  | 
Y | U | V | Y | U | V
-31.9% | -23.1% | -24.1% |  |  | 
-25.3% | -19.6% | -17.6% | -43.0% | -37.8% | -35.9%
-28.6% | -21.4% | -20.8% | -43.0% | -37.8% | -35.9%
3. AVC scalability

## Slide 22
Compression Performance (2) : JCTVC-K0044
<Actual Rate>
<Target Rate>
1. Spatial scalability
2. SNR scalability
3. AVC scalability
 | Hybrid vs HEVC 2x |  |  | Hybrid vs HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | -36.5% | -24.8% | -25.3% |  |  | 
Class B | -30.2% | -20.9% | -17.7% | -47.1% | -39.0% | -36.1%
Overall | -33.4% | -22.8% | -21.5% | -47.1% | -39.0% | -36.1%
Hybrid vs HEVC 2x |  |  | Hybrid vs HEVC 1.5x |  | 
Y | U | V | Y | U | V
-36.0% | -24.2% | -24.8% |  |  | 
-30.0% | -20.6% | -17.4% | -46.8% | -38.7% | -35.8%
-33.0% | -22.4% | -21.1% | -46.8% | -38.7% | -35.8%
 | Actual rate |  |  | Target rate |  | 
 | Y | U | V | Y | U | V
Class A+ | -43.2% | -33.0% | -32.7% | -42.7% | -32.3% | -32.1%
Class B | -39.1% | -28.6% | -24.2% | -38.8% | -28.2% | -23.8%
Overall | -41.2% | -30.8% | -28.5% | -40.7% | -30.3% | -28.0%
 | All Intra HEVC 2x |  |  | All Intra HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | -40.6% | -39.0% | -39.8% |  |  | 
Class B | -33.2% | -30.4% | -29.9% | -55.2% | -53.0% | -52.9%
Overall | -36.9% | -34.7% | -34.8% | -55.2% | -53.0% | -52.9%
All Intra HEVC 2x |  |  | All Intra HEVC 1.5x |  | 
Y | U | V | Y | U | V
-40.6% | -38.9% | -39.7% |  |  | 
-33.1% | -30.4% | -29.9% | -55.2% | -52.9% | -52.9%
-36.9% | -34.6% | -34.8% | -55.2% | -52.9% | -52.9%
 | Random Access HEVC 2x |  |  | Random Access HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | -37.4% | -26.1% | -26.8% |  |  | 
Class B | -31.7% | -22.3% | -19.8% | -50.5% | -42.7% | -40.6%
Overall | -34.5% | -24.2% | -23.3% | -50.5% | -42.7% | -40.6%
Random Access HEVC 2x |  |  | Random Access HEVC 1.5x |  | 
Y | U | V | Y | U | V
-37.0% | -25.6% | -26.3% |  |  | 
-31.5% | -22.0% | -19.6% | -50.3% | -42.4% | -40.3%
-34.2% | -23.8% | -22.9% | -50.3% | -42.4% | -40.3%

## Slide 23
Complexity Analysis
Run time increment relative to HM6.1
test | K0044 Enc | K0044 Dec | K0045 Enc | K0045 Dec
RA HEVC spatial | 4.1 | 2.9 | 2.8 | 1.8
AI HEVC | 3.5 | 2.4 | 2.8 | 1.6
RA HEVC SNR | 4.9 | 3.3 | 3.4 | 2.4
Avg. | 4.2 | 2.9 | 3.0 | 1.9

## Slide 24
Conclusions
The Samsung/Vidyo coding framework has been described in some detail
CfP responses submitted in all test categories
  including BL encoded with AVC
Our responses to the CfP demonstrated two key operating points
  K0045: low-complexity operating point, with good compression efficiency
  K0044: higher efficiency operating point, with a moderate
  increase in complexity
We propose this coding framework as a candidate for
the Test Model to facilitate further work

## Slide 25
THANK YOU
Inspire the World, Create the Future