## Slide 1: Description of scalable video coding technology proposal by KDDI
K. Kawamura†, T. Yoshino†, L. Sun‡, T. Ikenaga‡, and S. Naito†
†KDDI Corp. (KDDI R&D Labs., Inc.)
‡ Waseda University
<number>
Notes: <number>

## Slide 2: Overview
Utilized base layer information
  Same coding scheme for AVC/HEVC base
Three tools
  Inter-layer intra prediction
  Inter-layer motion/mode prediction
  Inter-layer residual prediction
Finer granularity in chroma intra mode
  Only for “intra-only spatial scalability”
λ settings
<number>

## Slide 3: Utilized base layer information
Partial decoded image
  Full IQ/IDCT/Intra prediction
  No-motion compensation.
Each frame
  picture type, QP value, POC, number of L0 and L1 frames, and POCs of each ref_index.
Each 4x4 block
  PRED_MODE (intra/inter), ref_idx of L0 and L1, and motion vectors.
<number>

## Slide 4: Inter-layer intra prediction
Use of up-sampled image is an additional mode.
Up-sampling filter is the identical one of SVC
  The difference is assumption of zero phase.
All co-located blocks of base layer need to be intra coded.
<number>

## Slide 5: Inter-layer MV prediction
Base layer
  Motion vectors are assigned for each 4x4 block
  Predicted vector is assigned for intra coded blocks
Enhancement layer
  Scaled motion vectors are derived for each 4x4 blocks
IL_MV is added to a candidate list
  left, up, IL_MV, upper left, …
<number>

## Slide 6: Inter-layer residual prediction
Up-sampled residual signals of BL are added to the MC signals of EL
Up-sampling filter is the identical one of SVC
  The difference is assumption of zero phase.
One of co-located block of BL need to be inter coded.
  Residual signal of intra coded block is assumed zero.
<number>

## Slide 7: Inter-layer mode prediction
base_mode_flag is assigned for each CU
  If skip_flag is off, base_mode_flag is coded
base_mode_flag equal to 1 specifies that
  the prediction mode and the corresponding motion data (when applicable) are inferred from base layer.
<number>

## Slide 8: Finer granularity chroma intra mode
Only for “Intra only spatial scalability”
Chroma intra modes are both inter-layer intra and regular intra prediction
Condition
  If ( base_mode_flag == 1 ) and ( PredMode[ x0 ][ y0 ]==MODE_INTRA )
  then intra_chroma_pred_mode[ x0 ][ y0 ]
<number>

## Slide 9: λ settings
Increased λ for enhancement layers
Multiplier computation
  Depends on base layer QP, delta QP, b-frame, special scale, and base layer codec
  Intra only cases
  Random access cases
<number>

## Slide 10: Conclusion
Three tools are transferred from SVC
Same coding scheme for AVC/HEVC base
Finer granularity of chroma intra mode is introduced.
Average objective gains of Hybrid vs HEVC
  EL-only actual rate: 24% and 43% for 2x and 1.5x
  EL-only target rate: 9% and 23% for 2x and 1.5x
<number>