## Slide 1: HM-8.0 code speedup
University of Science and Technology of China

## Slide 2: Outline
Purpose
  Save simulation time
Methods
  HM-8.0 code level optimization
  4 modifications

## Slide 3: Interpolation filter
Let the compiler know the coefficients when compiling

About 10% encoding time saving and 5%~8% decoding time saving

## Slide 4: Avoid repeated calculation
“component bits” is calculated again and again in UInt TComRdCost::xGetComponentBits( Int iVal )
We use a look up table and this table only needs to be initialized once at the encoder side.
3% time saving at the encoder side
Redundant computing reduction

## Slide 5: Clip implementation
HM-8.0: min() and max()
  Always two comparisons
Proposed: if…else…
  Sometimes only one comparison
1%~3% encoding time saving and 4%~8% decoding time saving

## Slide 6: SAD calculation
Unroll the loops in TComRdCost::xCalcHADs4x4() and TComRdCost::xCalcHADs8x8()
  most of the functions in TComRdCost.cpp are with loop unrolling in some degree
1% encoding time saving

## Slide 7: Summary of modifications
 | Encoder related | Decoder related | Compiler related | Redundancy reduction
1 Modify the interpolation filter function |  |  |  | 
2 Remove redundant calculation in RD cost function |  |  |  | 
3 Implement clip operation as if…else… method |  |  |  | 
4 Unroll the loop operations in SAD calculation |  |  |  | 

## Slide 8: Experimental Results
 | Interpolation filter | Avoid repeated calculation | Clip implementation | SAD calculation | All (Enc. / Dec.)
AI_Main |  | 100% / 99% | 97% / 92% | 99% / 100% | 96% / 92%
AI_HE10 |  | 100% / 100% | 97% / 92% | 100% / 100% | 96% / 92%
RA_Main | 90% / 92% | 97% / 99% | 99% / 96% | 99% / 100% | 86% / 88%
RA_HE10 | 90% / 92% | 97% / 100% | 99% / 96% | 99% / 100% | 86% / 88%
LB_Main | 90% / 93% | 97% / 99% | 100% / 96% | 99% / 100% | 86% / 89%
LB_HE10 | 90% / 93% | 97% / 100% | 100% / 96% | 99% / 100% | 86% / 90%
LP_Main | 92% / 95% | 97% / 99% | 99% / 97% | 99% / 100% | 88% / 92%
LP_HE10 | 92% / 95% | 97% / 100% | 99% / 96% | 99% / 100% | 88% / 92%

## Slide 9: Conclusion
Suggest to include these modifications in the next release of HM to save simulation time
  Save more than 10% simulation time on Windows + Visual Studio
  Save about 7% simulation time on Linux + GCC
We would like to thank Intel Corporation for providing a crosscheck on a different platform.

## Slide 10
Thank you!