## Slide 1: JCTVC-K0106 On Tile Ordering
Pieter Kapsenberg Intel Corporation

## Slide 2: Problem Statement
Line buffers in HEVC behave like FIFOs, just like previous video codecs
  Data written in will be consumed in the same order
  FIFO mechanism is easy to implement and well understood
This mechanism is broken by tiles
  Data written out at the bottom of a tile is not consumed at the start of the next tile
The problem applies mainly to single threaded decoders

## Slide 3: Problem Statement (diagram)

## Slide 4: Non-normative solutions
Use explicit addressing for line buffer reads and writes
  More complex, requires address generation.
  Lost opportunity to pack odd-sized data, as reads and writes must fall on system data word granularity
Use a second independent line buffer FIFO for the tile boundary
  Larger memory footprint
  Duplication of logic
Process tiles out of natural order, by processing column-wise
  Bitstream pointer must jump around when moving to the next tile.
  Difficult to implement when there are multiple slices that contain more than one tile.

## Slide 5: Proposed Solution
Order tiles first by tile columns, then by tile rows (vertical raster scan).
  Single FIFO line buffer for the whole picture
  Simple change to Draft and HM
  No impact to coding efficiency
  No impact to vertical line buffer operation
  CTB X/Y counter position update logic is simplified.
  Overall line buffer reduction
    Nearly all common picture formats are wider than they are tall
    Max vertical line buffer increased to picture height
    Max horizontal line buffer reduced to widest tile

## Slide 6: Proposed Solution (diagram)

## Slide 7: Draft Text Changes
A corresponding update to the C++ source file from JCTVC-J0126 that validates this pseudo-code is included with the contribution.