## Slide 1: On a 10-bit consumer-oriented profile in HEVC
JCTVC-K109
  NGcodec, BSkyB, NHK, DirecTV, SVT, Motorola Mobility, Technicolor, Ericsson, Thomson Video Networks, BBC, ST, ATEME, CISCO, RAI, ViXS
Alberto Dueñas, Adam Malamy, Bo Olofsson, Atsuro Ichigaya, Shinichi Sakaida, Sassan Pejhan, Lars Haglund, Ajay Luthra, Pierre Andrivon, Philippe Bordes, Tony Jones, Xavier Ducloux, Patrick Gendron, Marta Mrak, Andrew Cofler, Jean-Marc Thiesse, Arturo Rodriguez, Paola Sunna, Indra Laksono

## Slide 2: Introduction
This is a contribution about the creation of a new 10 bit profile
This is a consumer orientated profile
There is a unfulfilled market requirement on the industry to support 10-bit bit-depth for 1080p and UDHTV services
No new coding tools or modifications to existing coding tools part of the current HEVC Draft Text and Reference Software are required
This new profile would extend the current Main Profile to support 10-bit bit-depth content and maintain the chroma format at 4:2:0
Notes: Raise the importance of 10 bit, this is not part of professional profiles.
UKNB has already indicated the importance of 10 bit support on HEVC
There is a unfulfilled market requirements
JNB and USNB request to support BT 2020 colorimetry on AVC
<number>

## Slide 3: Reason for this contribution
A number of broadcasters evaluating the creation of 1080p HD and UHDTV services have identified the need for a 10-bit profile to use HEVC
The current lack of a 10-bit profile in HEVC delays the deployment of these services or leads to consider other compression formats with 10-bit support
The goal of this contribution is accelerating the inclusion of this new profile on the HEVC International Standard
Creating a 10-bit profile will speed up HEVC acceptance by the broadcast industry and help to proliferate in HD 1080p services and UHDTV applications
Notes: Most likely UHDTV applications will not appear using 8 bit, and there is strong on interest on 1080p 10-bit, current ITU-R BT.220 recommendation for UHDTV does not support 8-bit
<number>

## Slide 4: On the importance of a new 10-bit profile
Support for 10-bit is becoming very important in many consumer applications:
  ITU-R BT. 2020 recommendation on UHDTV is 10 or 12 bits (8 bits is not supported at the moment) and this is under consideration for new consumer services
  Content producers are mastering and archiving 1080p HD and UHDTV content in 10-bit
  Support for 10-bit is becoming available on consumer display systems.
  The larger physical size of UHDTV displays, coupled with the wider color gamut and higher dynamic range expose more easily the visual artifacts of 8-bit video content
  Consumer interfaces support 10-bit (HDMI1.4a, DisplayPort)

## Slide 5: 10-bit bit-depth vs. 8-bit bit-depth examples
Notes: Banding and contouring is more apparent in the case of 8-bit content and it does become more important in the case of using
This is appearing on the uncompressed content and becoming worse when using ITU-R BT Rec. 2020 because of the extended gamut.
<number>

## Slide 6: Current state of 10 bits coding in the Text Specification Draft and Reference Software
Support for the coding of 10-bit bit-depth content has been part of the design and reference software (as part of the common test conditions) from the early stages of the development
From previous contributions submitted at previous JVT-VC meetings, including JCTVC-J0079 and JCT-VC-I0108, it is indicated that the current HEVC Draft Text and Reference Software successfully supports the coding of 10-bit video sequences
ITU-R BT Rec. 2020 proposes different chromaticity coordinates as well as gamut that is wider for UHDTV. Current Draft already mentions such colorimetry aspects using VUI

## Slide 7: Regarding 4:2:2/4:4:4 chroma format and beyond 10-bit bit-depth
This contribution does not recommend that either a 4:2:2 chroma format or bit-depths beyond 10 bits be supported in a new profile at this time
4:2:2/4:4:4 chroma have been coupled in the past with greater than 8-bit mostly looking at professional applications
There is a new trend in the delivery of video content that is requesting 10 bits in isolation from 4:2:2/4:4:4 chroma formats and leading to the creation on this consumer profile

## Slide 8: Conclusions and recommendations
This contribution identifies that the usage of HEVC on emerging 1080p and UHDTV broadcasting services will be delayed because of the current lack of a 10-bit profile
This contribution shows the technical benefits of using 10 bits bit-depth compared with 8 bits bit-depth
This contribution suggests the creation of a breakout group (BoG) in order to discuss the creation of a new consumer 10 bits profile in HEVC
This contribution supports the further study of the current Draft Specification Text and Reference Software for the inclusion of a new 10-bit profile the Draft Specification Text as soon as possible

## Slide 9: Thank you
  NGcodec, BSkyB, NHK, DirecTV, SVT, Motorola Mobility, Technicolor, Ericsson, Thomson Video Networks, BBC, ST, ATEME, CISCO, RAI, ViXS