## Slide 1: Comparison of Compression Performance of HEVC with AVC at different resolutions
JCTVC-K0110
Shanghai 10–19 October 2012

## Slide 2: Test Materials
ftp://vqeg.its.bldrdoc.gov/HDTV/SVT_MultiFormat/
Different resolutions and frame rate
  720p50
  1080i25
  1080p50
  2160p50
10 seconds per sequence
4:2:0 YCbCr color sampling with 8 bits per sample

## Slide 3: Test materials
DuksTakeOff
High motion Colour
Local texture
OldTownCross
Slow motion
Very textured Noise
CrowdRun
Cpx motion Texture Colour Noise
InToTree
Slow motion
Zoom
Texture
Noise
ParkJoy
High motion
Pan
Texture
Contrast

## Slide 4: Test settings
Comparison between HEVC Main Profile (HM-7.0) and AVC High Profile (JM-18.3)
Common test conditions
  Main Profile all-intra configuration
  Main Profile random-access configuration
  Main Profile low-delay configuration
Interlaced materials was encoded as:
  frame mode (i.e. progressive_source_flag equal to 1)
  field mode (i.e. progressive_source_flag equal to 0)
for both HEVC and AVC
Notes: <number>

## Slide 5: Average BD-Rate measurement
 | Average BD-Rate |  |  | 
 | All Intra | Random Access | Low Delay P | Low Delay B
720p50 | -13,0% | -22,1% | -28,5% | -32,0%
1080p50 | -15,1% | -26,6% | -29,0% | -33,3%
2160p50 | -16,8% | -31,4% | -23,7% | -29,8%
1080i25 frame mode | -15,8% | -25,3% | -24,2% | -33,0%
1080i25 field mode | -14,0% | -23,3% | -28,2% | -32,5%
Objective measurements shows that HEVC can save from 13% to 33% in bit rate when compared with AVC.
Notes: <number>

## Slide 6: HEVC versus AVC at different resolutions

## Slide 7: Subjective evaluations
Preliminary subjective expert viewings sessions performed on 720p50 video sequences
Reference:
  AVC at about 10 Mbps in random access configuration
Test:
  HEVC at different bitrate ranging from 3 Mbps to 10 Mbps in random access configuration
An average bitrate saving of 40% of HEVC against AVC was spotted

## Slide 8: Subjective evaluations

## Slide 9: Conclusions
Average bit rate saving for the SVT sequences:
  Main Profile all-intra configuration, HM-7.0 can save about 15%
  Main Profile random-access configuration, HM-7.0 can save about 26%
  Main Profile low-delay configuration, HM-7.0 can save about 32%
Preliminary subjective expert viewings revealed an average bitrate saving of 40% for 720p50 sequences in random access configuration

## Slide 10: Next steps
Further comparisons (objective and subjective) using the material available from the recent 4K EBU shootinghttp://tech.ebu.ch/docs/tech-i/ebu_tech-i_013.pdf

## Slide 11
Any questions?
Marco Arena
marco.arena@rai.it

## Slide 12
Additional slides

## Slide 13: HEVC versus AVC at different resolutions
Notes: <number>

## Slide 14: HEVC versus AVC at different resolutions
Notes: <number>

## Slide 15: HEVC versus AVC at different resolutions
Notes: <number>

## Slide 16: HEVC versus AVC at different resolutions
Notes: <number>

## Slide 17: HEVC versus AVC at different resolutions

## Slide 18: HEVC versus AVC at different resolutions
Notes: <number>

## Slide 19: HEVC versus AVC at different resolutions
Notes: <number>

## Slide 20: HEVC versus AVC at different resolutions
Notes: <number>

## Slide 21
HEVC versus AVC at different resolutions

## Slide 22: HEVC versus AVC at different resolutions
Notes: <number>

## Slide 23: HEVC versus AVC at different resolutions
Notes: <number>

## Slide 24: HEVC versus AVC at different resolutions
Notes: <number>

## Slide 25
HEVC versus AVC at different resolutions

## Slide 26: HEVC versus AVC at different resolutions
Notes: <number>

## Slide 27: HEVC versus AVC at different resolutions
Notes: <number>

## Slide 28: HEVC versus AVC at different resolutions
Notes: <number>

## Slide 29
HEVC versus AVC at different resolutions

## Slide 30: HEVC versus AVC at different resolutions
Notes: <number>

## Slide 31: HEVC versus AVC at different resolutions
Notes: <number>

## Slide 32: HEVC versus AVC at different resolutions
Notes: <number>

## Slide 33: HEVC versus AVC at different resolutions
Notes: <number>