## Slide 1: JCTVC-K0112 DQP Buffering fix
Pieter Kapsenberg Intel Corporation

## Slide 2: Problem Statement
Proposal JCTVC-I0219 was adopted at Geneva meeting
Allows for independent CU decode, however it does not address the worst case:
  CTB size 64x64
  CU is not split, size is 64x64
  CU is Intra predicted
  TU tree fully split down to 4x4
  All TUs except the last luma TU have cbf = 0
In this case QP value for the CU is derived at the last TU.
380 empty TUs must be buffered up before deblocking can begin, requiring large storage on silicon.
HW decoder must be designed to handle the worst case, no matter how unlikely.

## Slide 3: Problem Diagram

## Slide 4: Proposed Solution 1
Store QP values at an 8x8 granularity.
  Main Profile compliant decoders must do this anyway, so no new storage is required.
  TU buffering is reduced to just 3.
  Solution impacts deblocking and QP predictor
  Coding performance shows no impact on average
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class E | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.0%
Class F | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0%
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class C | -0.1% | -0.1% | -0.2% | 0.1% | 0.0% | -0.1%
Class D | 0.0% | -0.3% | -0.1% | 0.0% | 0.1% | 0.4%
Class F | -0.1% | -0.2% | -0.4% | -0.1% | -0.2% | -0.3%
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class C | -0.1% | 0.1% | 0.1% | 0.0% | 0.1% | 0.1%
Class D | 0.1% | 0.0% | -0.3% | 0.0% | 0.1% | 0.2%
Class E | 0.0% | 0.3% | -0.3% | -0.3% | 0.1% | 0.4%
Class F | -0.1% | -0.1% | 0.0% | 0.0% | -0.6% | -0.6%
 | Low delay P Main |  |  | Low delay P HE10 |  | 
 | Y | U | V | Y | U | V
Class C | 0.0% | 0.2% | 0.1% | 0.0% | 0.1% | -0.3%
Class D | 0.0% | 0.1% | -0.1% | 0.1% | 0.5% | 0.5%
Class E | -0.2% | -0.1% | -0.1% | -0.1% | -0.3% | -0.2%
Class F | 0.0% | -0.1% | 0.1% | 0.1% | -0.1% | -0.1%

## Slide 5: Solution 1 diagram

## Slide 6: Proposed Solution 2
Signal Delta QP at the start of the CU
  DQP not signaled when there is no residual data.
  Requires signaling no_residual_data_syntax for intra CUs
TU buffering requirement is removed since a CU’s QP value is always determined at before parsing TU tree.
Relatively simple change to the Text
Slight coding loss
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class C | 0.13% | -0.07% | -0.12% | 0.11% | -0.10% | -0.01%
Class D | 0.14% | -0.06% | -0.08% | 0.15% | 0.02% | -0.09%
Class E | 0.45% | -0.15% | -0.03% | 0.39% | -0.36% | -0.18%
Class F | 0.23% | 0.43% | 0.35% | 0.21% | 0.54% | 0.21%
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class C | 0.09% | -0.08% | -0.09% | 0.17% | 0.01% | 0.20%
Class D | 0.19% | -0.09% | 0.60% | -0.02% | 0.56% | 0.54%
Class F | 0.10% | -0.36% | -0.05% | 0.10% | 0.36% | 0.05%
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class C | 0.01% | 0.24% | 0.19% | 0.09% | 0.23% | 0.58%
Class D | 0.16% | 0.26% | 0.29% | -0.01% | 0.06% | -0.67%
Class E | 0.19% | 0.36% | -0.37% | -0.12% | -0.66% | -1.41%
Class F | 0.37% | 0.18% | 0.11% | -0.03% | -0.04% | -0.43%
 | Low delay P Main |  |  | Low delay P HE10 |  | 
 | Y | U | V | Y | U | V
Class C | 0.10% | 0.56% | 0.38% | 0.11% | 0.49% | 0.27%
Class D | -0.16% | -0.08% | 0.42% | 0.07% | 0.41% | -0.22%
Class E | 0.15% | -0.30% | -0.18% | 0.03% | -0.75% | -1.00%
Class F | 0.30% | 0.37% | -0.11% | 0.26% | 0.26% | 0.84%