## Slide 1
Full-chroma (YUV444) Dictionary+hybrid Dual-coder Extension of HEVC
JCTVC-K0133
10 Oct. – 19 Oct. 2012
Tao Lin

## Slide 2
Screen picture has two types of content
  Continuous-tone content + Discontinuous-tone content
Hybrid coding is not discontinuous-tone oriented
  Even 444 has bad quality (due to high QP) at low bit-rate
Dictionary coder can do a much better job
  Using a super-large predictor set (dictionary)
  Hash table based quick string search can code the picture at much lower bitrate
Motivation

## Slide 3
Dual-coder
As dictionary
Original Input CU O
For reference/prediction
Dictionary-entropy Coder
(String-matching, CABAC)
Dual-purpose Constructed Pixel Buffer
RD Cost Based Selector
Dual-coder Bitstream
O
P1
Bitstream b1
b2
P2
O
Traditional Hybrid Coder (Prediction, Transform, Quantization, CABAC, etc.)
  Coder 1
  Coder 2
=New dict-entropy coder added
=Traditional hybrid coder used w/o change
bitstream
constructed pixels
YUV 444 Input
Encoder

## Slide 4
cu_coded_by_dict_coder_flag
b2
Dual-coder Bitstream
2-to-1 Mux
CU Coder Type Parser
1-to-2 Demux
b1
Dictionary-entropy Decoder (String-construction, CABAC)
Traditional Hybrid Decoder (CABAC, DQ, IT, MC, etc.)
For reference/prediction
Dual-purpose Constructed Pixel Buffer
P2
P1
  Decoder 1
  Decoder 2
As dictionary
=New dict-entropy decoder added
=Traditional hybrid decoder used w/o change
Constructed CU Õ
Dual-coder
Decoder

## Slide 5
Dual-coder Bitstream Syntax
seq_parameter_set_rbsp( ) { | Descriptor
video_parameter_set_id | u(4)
<snip ……> | 
dual_coder_mode | ue(v)
log2_max_pic_order_cnt_lsb_minus4 | ue(v)
<snip ……> | 
rbsp_trailing_bits( ) | 
} | 

## Slide 6
Dual-coder Bitstream Syntax
coding_unit( x0, y0, log2CbSize ) { | Descriptor
if(dual_coder_mode = = 0) | 
{the traditional HEVC hybrid coder syntax is used w/o any change} | 
else { | 
cu_coded_by_dict_coder_flag | ae(v)
if(cu_coded_by_dict_coder_flag = = 0) //HYBRID_CODER | 
{the traditional HEVC hybrid coder syntax is used w/o any change} | 
else | 
dictionary_entropy_coder( x0, y0, log2CbSize ) | 
} | 
} | 

## Slide 7
Dual-coder Bitstream Syntax
dictionary_entropy_coder( x0, y0, log2CbSize ) { | Descriptor
decoded_sample_count = 0 | 
NumSamplesInCU = (3 << (log2CbSize << 1)) | 
while(decoded_sample_count < NumSamplesInCU) { | 
matching_string_flag | ae(v)
if(matching_string_flag = = 1) { | 
matching_string_distance_use_recent_8_flag | ae(v)
if(matching_string_distance_use_recent_8_flag = = 1) { | 
matching_string_distance_recent_8_idx | ae(v)
matching_string_distance_minus1 = Recent8Distances[matching_string_distance_recent_8_idx] | 
for( i = matching_string_distance_recent_8_idx; i > 0; i-- ) | 
Recent8Distances[i] = Recent8Distances[i-1] | 
Recent8Distances[0] = matching_string_distance_minus1 | 
} | 
else { | 
matching_string_distance_minus1 | ae(v)
for( i = 7; i > 0; i-- ) | 
Recent8Distances[i] = Recent8Distances[i-1] | 
Recent8Distances[0] = matching_string_distance_minus1 | 
} | 
matching_string_length_minus2 | ae(v)
decoded_sample_count += (matching_string_length_minus2 + 2) | 
} | 
else { | 
unmatchable_sample_residual_abs | ae(v)
unmatchable_sample_residual_sign | ae(v)
decoded_sample_count += 1 | 
} | 
} | 
} | 

## Slide 8
Dual-coder Bitstream Semantics
cu_coded_by_dict_coder_flag equal to 0 specifies that the cu is coded by the hybrid coder, cu_coded_by_dict_coder_flag equal to 1 specifies that the cu is coded by the dictionary coder .
matching_string_flag specifies whether the succeeding dictionary coding element is a matching string or an unmatchable (luma or chroma) sample residual.
If matching_string_flag = 1, the succeeding dictionary coding element is a matching string, otherwise, the succeeding dictionary coding element is an unmatchable (luma or chroma) sample residual.
matching_string_distance_minus1 + 1 specifies the distances between the first sample of current sample-string to be decoded/constructed and the first sample of matching sample-string previously decoded/constructed in the dictionary, which is actually DPB and the current decoded picture reordered in a “dictionary-scan” format defined as a column-wise-packed-pixel cu-by-cu format. The value of matching_string_distance_minus1 shall be in the range of 0 to 4194303, inclusive
matching_string_length_minus2 + 2 specifies the length of the matching sample-string. The value of matching_string_length_minus2 shall be in the range of 0 to 271, inclusive.
unmatchable_sample_residual_abs is the absolute difference between the unmatchable sample (y or u or v component of a pixel) to be decoded and its predictor that is the same component (y or u or v) of the previous pixel in the dictionary. The value of unmatchable_sample_residual_abs shall be in the range of 0 to (256<< bit_depth_luma_minus8) – 1 for luma component or (256<< bit_depth_chroma_minus8) – 1 for chroma component, inclusive.
unmatchable_sample_residual_sign specifies the sign of an unmatchable sample residual. If unmatchable_sample_residual_sign is equal to 0, the corresponding unmatchable sample residual has a positive value. Otherwise (unmatchable_sample_residual_sign is equal to 1), the corresponding unmatchable sample residual has a negative value.

## Slide 9
CABAC Parsing Process
 | Syntax element | ctxIdxTable | initType |  | 
 |  |  | 0 | 1 | 2
coding_unit() | cu_coded_by_dict_coder_flag | Table 2 | 0 | 1 | 2
 | matching_string_flag | Table 3 | 0 | 1 | 2
 | matching_string_distance_use_recent_8_flag | Table 4 | 0 | 1 | 2
 | matching_string_distance_recent_8_idx | Table 5 | 0..2 | 3..5 | 6..8
 | matching_string_distance_minus1 | Table 6 | 0..25 | 26..51 | 52..77
 | matching_string_length_minus2 | Table 7 | 0..15 | 16..31 | 32..47
 | unmatchable_sample_residual_abs | Table 8 | 0..7 | 8..15 | 16..23
 | unmatchable_sample_residual_signe | Table 9 | 0 | 1 | 2

## Slide 10
CABAC Parsing Process
Syntax element | initType | Type of binarization | maxBinIdxCtx | ctxIdxTable | ctxIdxOffset
cu_coded_by_dict_coder_flag | 0 | FL, cMax = 1 | 0 | Table 2 | 0
 | 1 |  | 0 | Table 2 | 1
 | 2 |  | 0 | Table 2 | 2
matching_string_flag | 0 | FL, cMax = 1 | 0 | Table 3 | 0
 | 1 |  | 0 | Table 3 | 1
 | 2 |  | 0 | Table 3 | 2
matching_string_distance_use_recent_8_flag | 0 | FL, cMax = 1 | 0 | Table 4 | 0
 | 1 |  | 0 | Table 4 | 1
 | 2 |  | 0 | Table 4 | 2
matching_string_distance_recent_8_idx | 0 | FL, cMax = 7 | 2 | Table 5 | 0
 | 1 |  | 2 | Table 5 | 3
 | 2 |  | 2 | Table 5 | 6
matching_string_distance_minus1 | 0 | prefix: FL, cMax = 21 suffix: FL, cMax = (1<< max(prefix,1)) - 1 | 25 | Table 6 | 0
 | 1 |  | 25 | Table 6 | 26
 | 2 |  | 25 | Table 6 | 52
matching_string_length_minus2 | 0 | prefix: TU, cMax = 2 suffix: FL, cMax = (prefix < 2)? 7:255 | 15 | Table 7 | 0
 | 1 |  | 15 | Table 7 | 16
 | 2 |  | 15 | Table 7 | 32
unmatchable_sample_residual_abs | 0 | FL, cMax = 255 | 7 | Table 8 | 0
 | 1 |  | 7 | Table 8 | 8
 | 2 |  | 7 | Table 8 | 16
unmatchable_sample_residual_sign | 0 | FL, cMax = 1 | 0 | Table 9 | 0
 | 1 |  | 0 | Table 9 | 1
 | 2 |  | 0 | Table 9 | 2

## Slide 11
CABAC Parsing Process
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >=5
cu_coded_by_dict_coder_flag | 0 | na | na | na | na | na
matching_string_flag | 0 | na | na | na | na | na
matching_string_distance_use_recent_8_flag | 0 | na | na | na | na | na
matching_string_distance_recent_8_idx | 0 | 1 | 2 | na | na | na
matching_string_distance_minus1 (prefix) | 0 | 1 | 2 | 3 | 4 | na
matching_string_distance_minus1 (suffix) | 0..20 ctxIdxInc = 5 + binIdx |  |  |  |  | 
matching_string_length_minus2 (prefix) | 0 | 1 | na | na | na | na
matching_string_length_minus2 (suffix) when prefix = 0 | 2 | 3 | 4 | na | na | na
matching_string_length_minus2 (suffix) when prefix = 1 | 5 | 6 | 7 | na | na | na
matching_string_length_minus2 (suffix) when prefix = 2 | 0..7 ctxIdxInc = 8 + binIdx |  |  |  |  | 
unmatchable_sample_residual_abs | 0..7 ctxIdxInc = binIdx |  |  |  |  | 
unmatchable_sample_residual_sign | 0 | na | na | na | na | na

## Slide 12
5 screen capture sequences
Anchor is HM-8.0-dev-ahg7
Experimental Results
sequence name | dictionary size option | AI_main |  |  | LP_main |  |  | RA_main |  | 
 |  | BD-rate (cubic) |  |  | BD-rate (cubic) |  |  | BD-rate (cubic) |  | 
 |  | Y | U | V | Y | U | V | Y | U | V
sc1_CAD_ waveform | 4 | -71.9% | -74.2% | -74.7% | -64.2% | -67.5% | -67.4% | -72.1% | -74.7% | -75.4%
Sc2_CAD_waveform_Street_Campus | 4 | -62.3% | -70.2% | -70.9% | -40.1% | -68.0% | -69.3% | -54.9% | -71.9% | -72.8%
Sc3_PCB_ layout | 4 | -79.9% | -82.4% | -84.2% | -60.7% | -64.1% | -63.4% | -73.3% | -75.9% | -76.7%
sc4_PCB_ schematic | 4 | -76.8% | -81.0% | -82.8% | -59.3% | -63.9% | -62.8% | -72.7% | -76.6% | -78.0%
sc5_ppt_ doc_xls | 4 | -45.6% | -49.7% | -57.0% | -34.1% | -39.6% | -44.7% | -46.7% | -50.6% | -56.0%
Average | 4 | -67.3% | -71.5% | -73.9% | -51.7% | -60.6% | -61.5% | -64.0% | -69.9% | -71.8%
 | Enc Time |  | 104% | Dec Time |  | 47% |  |  |  | 
See JCTVC-K0134-r2.xls for more dictionary size options

## Slide 13
Conclusions
Dictionary+hybrid dual-coder is a straightforward yet very effective extension of HEVC for SCC
Basically just adding three new syntax elements in cu
Significant BD-rate reduction and subjective improvement
Cross-check by JCTVC-K0329 (TI)
After 3 complete meeting cycles, quite mature now
Propose to adopt the dictionary+hybrid dual-coder extension
Propose to have discontinuous-tone content oriented test-set of sequences and test conditions

## Slide 14
THANK YOU